## Slide 1: C2 consideration based on WLTP status
TF TA
20th July, 2023

## Slide 2: List of the vehicle / major tyre size in WLTP investigation (in Japan)
According to our findings, the vehicles used to obtain driving data for WLTC, all vehicles have gross vehicles weight less than 3.5t, even if they are M2 vehicles.
Vehicle category | Vehicle name | Curb Mass(kg) | GVW(kg) | Major Tyre size
PC | TOYOTA VITZ | 860 | 1135 | 165/70R14
PC | MITSUBISHI CHARIOT | 1560 | 1945 | 205/65R14
PC | TOYOTA HI-ACE | 2050 | 2490 | 205/70R15
PC | NISSAN ELGRAND | 2210 | 2595 | 215/65R15
LDCV | DAIHATSU HIJET | 920 | 1380 | 145R12 6PRLT
LDCV | NISSAN VANETTE | 1310 | 2225 | 165R14 6PRLT
LDCV | TOYOTA HI-ACE | 1580 | 2995 | 195/80R15
LDCV | NISSAN CARAVAN | 1550 | 2965 | 195/80R15
LDCV | NISSAN VANETTE | 1380 | 2295 | 165R14 6PRLT
LDCV | TOYOTA HI-ACE | 1650 | 3065 | 195/80R15

## Slide 3: List of the vehicle / major tyre size in WLTP investigation (in Japan)
Vehicle category | Vehicle name | Curb Mass(kg) | GVW(kg) | Major Tyre size
PC | SUZUKI ALTO | 700 | 920 | 135/80R12
PC | TOYOTA VITZ | 840 | 1115 | 155/80R13
PC | TOYOTA COROLLA | 1020 | 1295 | 175/70R14
PC | HONDA CR-V | 1440 | 1715 | 205/65R16
PC | HONDA INTEGRA | 1180 | 1400 | 215/45R17
LDCV | SUZUKI EVERY | 800 | 1260 | 145R12 6PR LT
LDCV | SUZUKI EVERY | 880 | 1340 | 145R12 6PR LT
LDCV | MAZDA BONGO | 1210 | 2225 | 165R14 6PR LT 145R12 6PR LT
LDCV | MAZDA BONGO | 1350 | 2265 | 165R14 6PR LT
LDCV | MITSUBISHI LIBERO | 1160 | 1570 | 155R13 6PR LT
LDCV | MITSUBISHI CANTAR | 1790 | 3455 | 165R14 8PR LT 145R13 8PR LT
PC | TOYOTA COROLLA | 1040 | 1315 | 165/80R13
PC | HONDA FIT | 1140 | 1415 | 175/65R15 84S
LDCV | TOYOTA REGIUSACE | 1920 | 2085 (3100) | 195/80R15 107/105L LT
According to our findings, the vehicles used to obtain driving data for WLTC, all vehicles have gross vehicles weight less than 3.5t, even if they are M2 vehicles.

## Slide 4: Summary
The vehicles used to obtain driving data for WLTC, all vehicles have gross vehicles weight less than 3.5t, even if they are M2 vehicles.
C2 tyres have various sizes and not only fitted to vehicles with gross vehicle weight less than equal 3500kg but also more heavy vehicles.
Therefore, not all C2 tyres can be included in the test method scope now under development.
For C2 tyre sizes fitting vehicles included in the WLTC running mode, force input can be applied, but other test conditions could be different and need to be verified.