## Slide 1: EBSIG I Specialist sub-group to address the energy question Meeting # 3 I 8th of August 2023
Summary and Conclusions

## Slide 2: EBSIG I Specialist sub-group to address the energy question Summary
By energy in scope of the work of this group the reserve of energy is understood, which is dedicated to the braking system.
Pneumatic Braking Systems
  the reserve of energy can be measured and monitored at any time directly (by direct means at the moment of TA and PTI )
  the reserve of energy is direct proportional to the forcing clamp of the actuators.
  the clamping force depends directly on the number of full stroke applications.
EMB
  the reserve of energy cannot be measured and monitored at any time directly.
  The clamping force depends directly on the output power [KW] of the reserve of energy , but not on the content of the reserve of energy [kWh] itself.
  multiple signals ( voltage, current, temperature) are necessary to be observed to measure and monitor the output power of the reserve of energy.
  The clamping force does not depend directly on the number of full stroke applications but will be almost constant until as certain discharge level of the reserve of energy is reached.

## Slide 3: EBSIG I Specialist sub-group to address the energy question Justification statement (3) Measurement Reserve of Energy ( pneumatic EBS vs. EMB )
t
Pneumatic EBS
t
EMB
Secondary Braking Performance
8 full stroke braking applications  Eres_p
8 full stroke braking applications  Eres_e
Eres_p
U [V]
Secondary Braking Performance
t
t
? U1 ?
? U2 ?
? U3 ?
E1
t1
t1
t2
t3
NEW

## Slide 4: EBSIG I Specialist sub-group to address the energy question Conclusions (1)
A Rechargeable Electrical Energy Storage System (REESS) is needed to store, measure and monitor the reserve of energy dedicated to the braking system.
The REESS will use multiple signals ( voltage, current, temperature) and models (or observers) ensuring that , in real time, EMB “knows” which reserve of energy and output power is available and whether that is enough to guarantee a specific braking performance
The manufacturer shall demonstrate that REESS is robust under all reasonably foreseeable operating conditions to the satisfaction of the Approval Authority or the Technical Service acting on its behalf (hereafter referred to as Type Approval Authority)

## Slide 5: EBSIG I Specialist sub-group to address the energy question Conclusions (2)
REESS State Parameter are depending on Technology of Storage Device.
REESS is providing the State of Function to the Braking System
State of Function explains, if reserve of energy and output power is available to guarantee a specific braking performance
State of Function is containing a prediction on
  State of Health ( Aging )
  State of Charge
  Inner Resistance
  Providing warnings
NEW

## Slide 6: Rechargeable Electrical Energy Storage System(REESS) ( Energy Storage Device with a Reserve of Energy dedicated to the Braking System)
6
Estimator of states & parameters
Model of the ESD
I
T
U
state variables
Adaption of parameters
U
Unit of feedback
+
-
model parameters
Predictors
^
State of Charge (SoC) [kWh]
State of Health (SoH)
Load profiles e.g. 8+1 brake applications
e.g., Discharge Capacity Algorithm, Aging Sub-Algorithms, Capacitance Algorithm, Quiescent Voltage Measurement, Device Off Detection, Internal Resistance Determination, Device Temperature Model, …
State of charge is proportional to the amount of stored Energy Eres_e
Inner Resistance
Reserve of Energy dedicated to the Braking System
ESD
(Energy
Storage
Device)
REESS State Parameter
[ depending on Technology of Storage Device under Type Approval ]
SOC
State of Function (SoF) [kW]
 Prediction number of brakings
under discussion

## Slide 7
Estimator of battery states & parameters
Model of the battery
I
T
U
state variables
Adaption of parameters
U
Unit of feedback
+
-
model parameters
Examples of Predictors
^
Charge-Acceptance
State of Charge (SoC) Q
Voltage after safe stop (state of function (SoF) -> Upred)
Ageing State of Health (SoH)
SOC
∆SOC
Load profiles e.g. 8+1 brake applications
Examples for Sub-Algorithms
Battery Off
Detection
Quiescent Voltage
Measurement
Ageing Sub-
Algorithms
Discharge Capacity
Algorithm
Internal Resistance
Determination
Capacitance Algorithm
Battery Temperature
Model
State of charge is proportional to the amount of stored Energy Eres_e
Voltage after Safe Stop calculates the minimum Voltage for a defined (worst case) load profile. It takes into account the power output capability (Ri , Pres_e) and the stored Energy (Eres_e) of the reserve.
Voltage after Safe Stop indicates that the energy and power supply for the 8+1 brake applications is ensured.
Internal Resistance (Ri)
Rechargeable Electrical Energy Storage System(REESS)
(Example: Lead acid battery state detection)

## Slide 8: EBSIG I Specialist sub-group to address the energy question Interaction REESS to Braking System
Braking System
ESD
REESS
(related to the reserve of energy dedicated to the braking system system)
I, U, T
SOF
Request Status SOF
NEW
The setting of trigger conditions to issue the warning signal is done else ware ( e.g., REESS, EMB)

## Slide 9: EBSIG I Specialist sub-group to address the energy question Scenarios to proof the concept of REESS
Low temperature 
High temperature 
Exchange of a battery 
Aging 
Type Approval Test
Long Time Parking 

## Slide 10: EBSIG I Specialist sub-group to address the energy question Scenarios to proof the concept of REESS based on a lead-acid battery
Scenario | Physical effect on battery | REESS-Control Action | Warning
Low temperature e.g., the vehicle is parked outside during a cold night | Increased internal resistance (Ri) In combination with internal resistance increase due to battery aging, low temperature is problematic for battery’s power delivery capability | REESS-Control continuously measures voltage (U), current (I) and temperature (T). Because of low temperature the “predictor of Ri” will exceed the threshold. REESS-Control reports “State of function critical, due to insufficient Power Delivery Capability”. SOF Warning issued during vehicle startup Previous warnings to the driver due to battery aging are technically possible and recommended | Red The power supply for the 8+1 brake applications cannot be is ensured.

## Slide 11: EBSIG I Specialist sub-group to address the energy question Scenarios to proof the concept of REESS based on a lead-acid battery
Scenario | Physical effect on battery | REESS-Control Action | Warning
Long time parking | Battery charge low​ due to vehicle’s quiescent current draw | REESS-Control continuously measures voltage (U), current (I) and temperature (T) even during parking phase. Due to current flowing out of the Battery, and decreasing voltage, it recognized when charge drops below warning threshold.​ REESS-Control reports “too low state of charge”. SOF Warning issued immediately during vehicle startup As soon as the battery and is charged sufficiently, the REESS-Control reports “state of charge ok”. | Red The power supply for the 8+1 brake applications cannot be ensured.
NEW

## Slide 12: EBSIG I Specialist sub-group to address the energy question Scenarios to proof the concept of REESS based on a lead-acid battery
Scenario | Physical effect on battery | REESS-Control Action | Warning
High temperature e.g., Kuwait Taxi | Increased internal resistance (Ri) - due to calendric aging or - due to accelerated aging during high temperature exposure (high temperature has no negative effect on lead acid batteries apart from aging.) | REESS-Control continuously measures voltage (U), current (I) and temperature (T). Because of the increase of Ri, the Ri predictor will exceed the threshold. REESS-Control reports “State of function critical, due to insufficient Power Delivery Capability”. SOF Warning issued during vehicle startup Previous warnings to the driver due to battery aging are technically possible and recommended | Red The power supply for the 8+1 brake applications cannot be ensured.
Aging |  |  | 
NEW

## Slide 13: EBSIG I Specialist sub-group to address the energy question Scenarios to proof the concept of REESS based on a lead-acid battery
Scenario | Physical effect on battery | REESS-Control Action | Warning
Battery change | Battery is replaced. | REESS-Control has constantly measured U, I and T. REES detects the assembly of a new battery *. REESS-Control resets its battery model to new battery SOF warning issued Warning is removed as soon as battery model calibration is successful and battery state of function is ensured | Red The power supply for the 8+1 brake applications cannot be ensured. Warning is removed as soon as battery model calibration is successful and battery state of function is ensured
Hint: The process of changing battery of an EMB system could be compared to changing a tire on vehicles equipped with active Tire Pressure Monitoring System (TPMS) according ECE R64 – New tires can only be installed by a service technician using special equipment, because the TPMS controller in the vehicle needs to learn each Tire ID.
* New Battery recognized due to service technician’s electronic tooling service request and/or supply interruption and/or abrupt changes of battery parameters.
NEW

## Slide 14: EBSIG I Specialist sub-group to address the energy question Attachments

## Slide 15: EBSIG I Specialist sub-group to address the energy question Tasks given by GRVA SIG on Electromechanical Braking
Provide confidence that technology is able to do the following:
Measure and/or monitor in real time the energy available in the reserve in all operating conditions and over the lifetime (high temperatures, ageing, …).
Compare that measured value with the known threshold value required to meet the specific performances required by the regulations. Note: The known value means the value identified by the manufacturer to fulfil the specific requirements of the regulation.
To be able to generate the warning to the driver in real time in accordance with the known threshold value

## Slide 16
Energy level and clamping force analogies and differences in EBS vs. EMB
In pneumatic brake systems the Eres_p ~ pres and the Fclamp_p ~ pchamb. Since pchamb directly depens on pres in full stroke actions  change of Fclamp_p follows the reduction of Eres_p.
Both major quantities (Eres, Fclamp) can be easily measured with an external manometer by the technical service or PTI.
Eres_p ~ pres x constres
Fclamp_p ~ pchamb x constbrake
EBS
EMB
Eres_e [kWh]
Fclamp_e [kN]
In EMBs the Eres_e cannot be measured by a single proportional quantity, but from multiple signals and models (observer), similarly Fclamp_e is either measured internally by the EMB system or also estimated from other signals and caliper models (observer), therefore technical service/PTI shall rely on internal signals of the EMB system (e.g. SOC).
In an EMB system the Fclamp_e primarily depends on the power output capability of the reserve Pres_e and only indirectly on Eres_e !
Quantities to be monitored
Pres_e [kW]

## Slide 17
Clamping force and energy level degradations of the reserve in a capacity test of EBS vs. EMB
t
Fclamp_p
Pneumatic EBS
t
EMB
Fclamp_e
Secondary brake force limit
8 full stroke braking applications  Eres_p
8 full stroke braking applications  Eres_e
Degressive clamping force tendency
Widely constant then progressive clamping force tendency
The clamping force of pneumatic brakes gradually degrades with each application, since the clamping force is directly proportional to the reserve’s pressure level, i.e., with the energy level of the reserve.  Pressure level of the reserve well represents the energy state of the brake system.
The clamping force of EMBs is approximately constant till a critical discharge level, where the rated power output of the energy reserve cannot be anymore provided. After this a reduction of brake performance occurs, since the power output capability of the reserve depends also on its energy level.  Both the energy level and power output capability shall be monitored (e.g. by a BMS).
Eres_p
Eres_e

## Slide 18
Impact of the energy reserve characteristics to the EMB performance
UOCV
UReserve
The (secondary) clamping brake force of EMB is directly depending on the power output available to the EMB actuator (effect of harness and connectors, etc. also to be considered  board network design)
The available power output of the reserve depends primarily on its internal resistance
The ratio of internal resistance to the capacity of a reserve is technology dependent
The internal resistance and the capacity fade with different rates during the lifetime, which also depends on technology, i.e. both the energy amount as well as the power output requires monitoring
UReserve
Fclamp_e ~ Pmot_e

## Slide 19: Technology insight : Battery Sensor (EBS)
Example for a Technical Solution
Technical realizations of battery sensors from a variety of suppliers exist
EBS working principle:
Lead-acid technology has a long history of use. It’s ageing process and its failure modes are known and well-understood.
Reliable models exist for all relevant battery parameters. The EBS constantly measures voltage, current and temperature. Those values are fed into a battery model for continuous battery state estimation:
safety-state of function (SOF): estimates max. transient voltage drop, considering state of charge (SOC) and state of health (SOH)
Indicates battery availability in Safe Power Net: “Battery has enough energy and power to support a Minimal Risk Maneuver (MRM)”
ASIL-B conformity | Bosch EBS Gen1 SOP: 2006
l
Source: https://www.bosch-mobility.com/en/solutions/sensors/electronic-battery-sensor/

## Slide 20
Chart: Energy content [Wh]
| 50kWh Traction Battery @5% SoC | Nominal Content 60Ah Pb Battery | Degraded Battery | MRM | 9 full brake actuation | base load Power Net, 20 min. | base load Power Net max, 20min
Datenreihe 1 | 2500 | 720 | 72 | 10 | 10 | 115 | 495
Nominal Content 60Ah Pb Battery: 720Wh / degraded battery: 10% of initial value.
MRM: 2 x double lane change + braking to standstill; Full-size SUV, hydraulic brakes.
9 full brake actuation: full actuation with 7s hold, M1 vehicle, hydraulic brake system, worst case estimation
base load Power Net: C-Segment BEV, drive cycle with minimal comfort loads, source vehicle measurements
base load Power Net max: luxury BEV, drive cycle with max comfort loads, source vehicle measurements
Energy content comparison (e.g., M1 vehicle)

## Slide 21: EBSIG I Specialist sub-group to address the energy question Proposal Definition REESS
UN R100, para. 2.37 "Rechargeable Electrical Energy Storage System (REESS)" means the rechargeable energy storage system that provides electric energy for electrical propulsion. A battery whose primary use is to supply power for starting the engine and/or lighting and/or other vehicle auxiliaries’ systems is not considered as a REESS. The REESS may include the necessary systems for physical support, thermal management, electronic controls and casing.
Proposal UN R13, UN R13-H para. x.xy ( amended to read) "Rechargeable Electrical Energy Storage System (REESS)" means the rechargeable energy storage system that provides electric energy for braking electrical propulsion.
The same REESS may supply power for starting the engine and/or steering and/or other vehicle auxiliaries’ systems A battery whose primary use is to supply power for starting the engine and/or lighting and/or other vehicle auxiliaries’ systems is not considered as a REESS. The REESS may shall include the necessary systems for physical support, thermal management, and electronic controls and casing.
For later ;-) Proposal for a definition on RESS