## Slide 1: 3rd A-LCA IWG SG2 MTG
2023.Aug.24th

## Slide 2: Agenda
Overall schedule
Discussion of a way to proceed
Discussion of a goal image and a material classification
Discussion of planning a meeting in person(Face to Face)

## Slide 3: Overall schedule plan
 | 2023 |  |  |  |  |  | 2024 |  |  |  |  |  | 2025
 | Jun | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | 2Q | 3Q | 4Q | -
IWG MTG |  |  |  |  |  |  |  |  |  |  |  |  | 
material scope & topics setting due to a goal toward CN |  |  |  |  |  |  |  |  |  |  |  |  | 
a level concept setting |  |  |  |  |  |  |  |  |  |  |  |  | 
material list setting for automotive |  |  |  |  |  |  |  |  |  |  |  |  | 
a system boundary setting with manufacturing SG3 |  |  |  |  |  |  |  |  |  |  |  |  | 
a system boundary setting with waste/recycling SG5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Setting of each material carbon intensity |  |  |  |  |  |  |  |  |  |  |  |  | 
Info.exchange with material industries |  |  |  |  |  |  |  |  |  |  |  |  | 
Data collecting and operation setting |  |  |  |  |  |  |  |  |  |  |  |  | 
Info.exchange for verification |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 4: Discussion of a way to proceed
Reference: ISO14040/44 | 
Setting goal | Background and objective
 | Usage method of result
Setting a scope of the investigation | Applicable products and functional unit
 | System boundary
 | Cut-off criteria
 | Data requirement
 | Allocation method
 | Data quality
 | Interpretation method and limit
Analysis and evaluation of inventory | Data collection conditions and results
 | Analyzed results of inventory
 | Evaluation results of impact
Interpretation | Sensitivity analysis
 | Summary and limit
At first, material classification
A guideline of discussion points for material
Share common goal image

## Slide 5: SG2(Material) concept
Purpose
Set an internationally harmonized material carbon intensity
which enables a material technology to evaluate LCA
toward carbon neutral
: point of views
- Usage of recycled material, yield rate
- Development of global regionality (electric power)
Draft

## Slide 6: A way of thinking material classification
Strategy goal setting
Usage image of material in automotive development
Simulation
CAD/BOM
Design goal setting
IMDS/Measurement
/Data collection system
Verification , Certification, Regulation, SC traceability
Extract high sensitivity material types due to weight ratio or rough CO2 estimation ⇒Investigate what kind of material types were used for representative vehicle
models (ICE, HEV, EV, FCV) between OEMs
Add a future material type which is expected to decrease CO2
Material
Material
Purpose:
Material

## Slide 7: Material List by VDA classification
VDA Classification | VDA Classification Name
1.1 | Steel/cast steel/sintered alloys
1.1.1 | Unalloyed/low alloy steel
1.1.2 | high-alloy steel
1.2 | cast iron
1.2.1 | Gneissic graphite cast iron/ malleable cast iron
1.2.2 | Spheroidal graphite cast iron/Vermular cast iron
1.2.3 | high-alloy cast iron
2.1 | Aluminium / aluminium alloys
2.1.1 | Cast aluminium alloys
2.1.2 | Forged aluminium alloy
2.2 | Magnesium, magnesium alloys
2.2.1 | Cast magnesium alloy
2.2.2 | Forged magnesium alloy
2.3 | Titanium, titanium alloys
3.1 | Copper (e.g. copper in harnesses)
3.2 | copper alloy
3.3 | zinc alloy
3.4 | nickel alloy
3.5 | lead (the metal)
4.1 | Platinum/rhodium
4.2 | Other special metals
5.1 | thermoplastic resin
5.1.a | Thermoplastic resin (containing filler)
5.1.b | Thermoplastic resin (without filler)
5.2 | thermoplastic elastomer
5.3 | Elastomer/elastomer composites
5.4 | thermosetting resin
5.4.1 | polyurethane
5.4.2 | unsaturated polyester
5.4.3 | Other thermosetting resins
5.5 | Polymer composites (e.g. laminated trim parts)
5.5.1 | Resins in polymer composites.
5.5.2 | Fibres in polymer composites (textiles)
6.1 | painting material
6.2 | Adhesives, sealants
6.3 | underseal
7.1 | Organic natural materials (e.g. leather)
7.2 | Ceramics/glass
7.3 | Other composite materials (e.g. friction linings)
8.1 | Electronic component materials (e.g. PCBs, displays)
8.2 | Electrical component materials
9.1 | fuel
9.2 | lubricant
9.3 | brake fluid
9.4 | Coolant/other glycols
9.5 | refrigerant
9.6 | Washer fluid, battery fluid
9.7 | preservative
9.8 | Other fuels and replenishers
 | Tyre
 | lead-acid battery
 | Drive battery cell
VDA material
Not enough to show low CO2 material effect by VDA classification

## Slide 8: Vehicle hot spot analysis due to material type
VDA material definition | VDA classification |  | Small CE | Mid FCV | Small EV | Mid HEV | Small 2R | Mid 2R |  | Small | Small HEV | Large |  | ICE Body | ICE Lead acid battery | ICE Tire (4) | MHEV Body | MHEV Lead acid Battery | MHEV Li ion battery | MHEV Tire(4)
1.1 | Steel/cast steel/sintered alloys |  | 20.9% | 5.7% | 7.6% | 15.6% | 0.0% | 0.0% |  | 10.9% | 11.1% | 10.1% |  | 44.1% | 0.0% | 0.0% | 46.1% | 0.0% | 0.0% | 0.0%
1.1.1 | Unalloyed/low alloy steel |  | 30.0% | 13.4% | 15.4% | 22.4% | 53.7% | 44.0% |  | 50.9% | 50.3% | 51.2% |  | 18.2% | 0.0% | 14.1% | 15.1% | 0.0% | 0.0% | 11.9%
1.1.2 | high-alloy steel |  | 0.9% | 0.6% | 0.8% | 1.4% | 3.1% | 3.2% |  | 1.4% | 1.5% | 1.0% |  | 0.6% | 0.0% | 0.0% | 0.5% | 0.0% | 0.0% | 0.0%
1.2 | cast iron |  | 0.3% | 0.1% | 0.7% | 0.3% | 0.0% | 0.0% |  | 0.7% | 0.6% | 0.5% |  | 1.1% | 0.0% | 0.0% | 1.0% | 0.0% | 0.0% | 0.0%
1.2.1 | Gneissic graphite cast iron/ malleable cast iron |  | 0.9% | 0.6% | 0.5% | 1.1% | 0.0% | 0.0% |  | 8.2% | 8.0% | 8.9% |  | 2.2% | 0.0% | 0.0% | 2.0% | 0.0% | 0.0% | 0.0%
1.2.2 | Spheroidal graphite cast iron/Vermular cast iron |  | 0.4% | 0.7% | 0.7% | 1.6% | 2.5% | 2.0% |  | 5.3% | 5.1% | 7.3% |  | 1.3% | 0.0% | 0.0% | 1.2% | 0.0% | 0.0% | 0.0%
1.2.3 | high-alloy cast iron |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.7% |  | 0.1% | 0.1% | 0.1% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
2.1 | Aluminium / aluminium alloys |  | 20.2% | 35.8% | 15.6% | 24.8% | 0.0% | 0.0% |  | 1.1% | 1.2% | 2.9% |  | 1.8% | 0.0% | 0.0% | 4.2% | 0.0% | 21.4% | 0.0%
2.1.1 | Cast aluminium alloys |  | 2.5% | 3.1% | 2.8% | 4.9% | 17.2% | 26.8% |  | 4.7% | 5.3% | 6.6% |  | 5.4% | 0.0% | 0.0% | 3.2% | 0.0% | 0.0% | 0.0%
2.1.2 | Forged aluminium alloy |  | 3.1% | 6.9% | 3.9% | 3.4% | 0.1% | 2.8% |  | 5.4% | 5.2% | 4.6% |  | 0.5% | 0.0% | 0.0% | 0.4% | 0.0% | 0.0% | 0.0%
2.2 | Magnesium, magnesium alloys |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
2.2.1 | Cast magnesium alloy |  | 0.5% | 0.1% | 0.2% | 0.1% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
2.2.2 | Forged magnesium alloy |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
2.3 | Titanium, titanium alloys |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
3.1 | Copper (e.g. copper in harnesses) |  | 0.6% | 1.5% | 1.1% | 1.1% | 0.7% | 0.6% |  | 0.6% | 0.8% | 0.5% |  | 1.2% | 0.0% | 0.0% | 1.7% | 0.0% | 13.4% | 0.0%
3.2 | copper alloy |  | 0.1% | 0.2% | 0.2% | 0.2% | 0.1% | 0.0% |  | 0.2% | 0.2% | 0.3% |  | 0.2% | 0.0% | 0.0% | 0.3% | 0.0% | 0.0% | 0.0%
3.3 | zinc alloy |  | 0.3% | 0.2% | 0.3% | 0.5% | 1.4% | 0.5% |  | 0.3% | 0.3% | 0.1% |  | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
3.4 | nickel alloy |  | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
3.5 | lead (the metal) |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.8% | 64.6% | 0.0% | 1.0% | 59.1% | 0.0% | 0.0%
4.1 | Platinum/rhodium |  | 0.0% | 2.1% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
4.2 | Other special metals |  | 0.2% | 0.3% | 0.6% | 0.8% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
5.1 | thermoplastic resin |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.1% |  | 0.0% | 0.0% | 0.0% | 1.7% | 0.0% | 0.0% | 0.0%
5.1.a | Thermoplastic resin (containing filler) |  | 3.8% | 2.3% | 2.0% | 3.6% | 2.9% | 0.4% |  | 2.3% | 2.3% | 0.7% |  | 6.2% | 1.6% | 0.0% | 5.0% | 1.3% | 0.0% | 0.0%
5.1.b | Thermoplastic resin (without filler) |  | 3.8% | 2.1% | 2.3% | 3.7% | 8.8% | 7.3% |  | 2.0% | 2.0% | 1.2% |  | 5.7% | 4.5% | 4.5% | 6.4% | 5.6% | 6.0% | 0.0%
5.2 | thermoplastic elastomer |  | 0.8% | 0.4% | 0.4% | 0.6% | 0.0% | 0.0% |  | 0.4% | 0.4% | 0.2% |  | 0.4% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0%
5.3 | Elastomer/elastomer composites |  | 1.8% | 1.0% | 1.1% | 1.3% | 2.4% | 3.7% |  | 1.5% | 1.5% | 1.1% |  | 3.5% | 0.0% | 81.4% | 3.9% | 0.0% | 0.0% | 82.9%
5.4 | thermosetting resin |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.1% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
5.4.1 | polyurethane |  | 1.2% | 0.4% | 0.5% | 0.8% | 1.3% | 0.6% |  | 0.4% | 0.4% | 0.2% |  | 1.1% | 0.0% | 0.0% | 0.7% | 0.0% | 0.0% | 0.0%
5.4.2 | unsaturated polyester |  | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% |  | 0.1% | 0.1% | 0.2% |  | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
5.4.3 | Other thermosetting resins |  | 0.1% | 1.3% | 0.2% | 0.2% | 0.0% | 0.0% |  | 0.1% | 0.1% | 0.0% |  | 0.2% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
5.5 | Polymer composites (e.g. laminated trim parts) |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.3% | 0.0% | 0.0% | 0.0%
5.5.1 | Resins in polymer composites. |  | 0.4% | 0.3% | 0.0% | 0.7% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.1% |  | 0.1% | 0.0% | 0.0% | 0.4% | 0.0% | 0.0% | 0.0%
5.5.2 | Fibres in polymer composites (textiles) |  | 1.3% | 0.5% | 0.3% | 0.6% | 0.0% | 0.0% |  | 0.1% | 0.1% | 0.0% |  | 0.8% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 5.1%
6.1 | painting material |  | 0.2% | 0.2% | 0.1% | 0.4% | 0.0% | 0.0% |  | 0.6% | 0.6% | 0.3% |  | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
6.2 | Adhesives, sealants |  | 0.1% | 0.2% | 0.1% | 0.7% | 0.0% | 0.0% |  | 0.1% | 0.1% | 0.1% |  | 0.3% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
6.3 | underseal |  | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
7.1 | Organic natural materials (e.g. leather) |  | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 2.4% | 0.0% | 0.1% | 0.0%
7.2 | Ceramics/glass |  | 2.3% | 1.0% | 1.5% | 1.6% | 0.0% | 0.0% |  | 1.7% | 1.7% | 0.8% |  | 2.7% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0%
7.3 | Other composite materials (e.g. friction linings) |  | 0.8% | 12.1% | 0.2% | 0.8% | 0.5% | 0.0% |  | 0.1% | 0.1% | 0.1% |  | 0.7% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
8.1 | Electronic component materials (e.g. PCBs, displays) |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0%
8.2 | Electrical component materials |  | 0.0% | 0.0% | 0.0% | 0.0% | 1.7% | 2.6% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 59.1% | 0.0%
9.1 | fuel |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0%
9.2 | lubricant |  | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.4% |  | 0.2% | 0.2% | 0.2% |  | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
9.3 | brake fluid |  | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
9.4 | Coolant/other glycols |  | 0.3% | 0.1% | 0.1% | 0.2% | 0.0% | 0.5% |  | 0.3% | 0.3% | 0.1% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
9.5 | refrigerant |  | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.6% | 0.0% | 0.0% | 0.0%
9.6 | Washer fluid, battery fluid |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.1% | 0.1% | 0.0% |  | 0.4% | 29.3% | 0.0% | 0.0% | 34.0% | 0.0% | 0.0%
9.7 | preservative |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
9.8 | Other fuels and replenishers |  | 0.1% | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% |  | 0.4% | 0.4% | 0.2% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
■Passenger car/MC
■Truck
■Passenger car ICE/HEV (battery, tire)
■Material types
Steel
Alluminium
Resin
Initial study
↑Total: CO2 100% as each vehicle (JPN OEMs)
↓
Mostly main material types are dominant
<IMDS>
・Parts list
・VDA
Mat.Type
&
・Weight
×
・Carbon
Intensity
Data
(2011y
JAMA)

## Slide 9: Vehicle hot spot analysis due to material type
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0.076218 | 0.15352 | 0.0081075 | 0.0069775 | 0.0054789 | 0.0065432 | 0 | 0.15628 | 0.02804 | 0.038657 | 0 | 0.0020645 | 0 | 0 | 0.011116 | 0.0017432 | 0.0028921 | 0.00026588 | 7.993e-08 | 9.1269e-06 | 0.0056742 | 0 | 0.020114 | 0.023078 | 0.0038825 | 0.011028 | 0.00012729 | 0.0049735 | 0.00093585 | 0.0021081 | 0 | 0.000253 | 0.0028373 | 0.00090171 | 0.0012166 | 0 | 5.9021e-05 | 0.01456 | 0.0018766 | 9.3844e-06 | 3.5803e-06 | 0 | 0.00016373 | 0.00020529 | 0.0011237 | 0.00026592 | 1.0663e-05 | 0 | 0.0014859 | 0.0076002 | 0.0016378 | 0.39595
Small EV
Steel/cast steel
/sintered alloys
Aluminium /
aluminium alloys
Resin
Drive battery cell
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0.056893 | 0.13381 | 0.0062477 | 0.0014129 | 0.0059123 | 0.0070964 | 0 | 0.35798 | 0.030829 | 0.069101 | 0 | 0.00085073 | 0 | 0 | 0.014839 | 0.0016848 | 0.0019126 | 0.0009911 | 6.1105e-08 | 0.021119 | 0.0026737 | 0 | 0.022655 | 0.021468 | 0.0036963 | 0.010101 | 2.6179e-05 | 0.003907 | 0.00014256 | 0.013079 | 0 | 0.0028092 | 0.0052164 | 0.0019195 | 0.0016465 | 0 | 0.0013324 | 0.0099628 | 0.12081 | 2.6149e-05 | 6.688e-05 | 0 | 0.00012662 | 0.00015891 | 0.00086988 | 0.00020584 | 7.0076e-06 | 0 | 0.00028021 | 0.0067416 | 0.0012278 | 0.058163
FCV
Steel/cast steel/sintered alloys
Aluminium / aluminium alloys
Resin
Other composite materials
Example of applicable products
It depends on each vehicle design concept
But we’d like to make agreement of common material classification

## Slide 10: Example
Resin
Material classification | Wt(%)
PP | 4.48%
PET | 0.95%
PA | 0.93%
PUR | 0.73%
PBT | 0.73%
ABS | 0.53%
PVC | 0.50%
PC | 0.47%
PE | 0.38%
POM | 0.34%
EP | 0.23%
PMMA | 0.18%
PVB | 0.14%
PPS | 0.14%
LCP | 0.04%
ASA | 0.02%
PA11 | 0.01%
PF | 0.01%
PESU | 0.01%
Material classification | Wt%
PP | 0.91%
PA | 0.24%
PE | 0.16%
PVC | 0.11%
ABS | 0.10%
PUR | 0.09%
PET | 0.07%
POM | 0.04%
PC | 0.04%
EP | 0.03%
PBT | 0.03%
ASA | 0.02%
PC+ABS | 0.02%
PMMA | 0.02%
PPA | 0.01%
PF | 0.01%
PPS | 0.01%
PC＋PET | 0.01%
PPE | 0.01%
Material classification | Wt%
PP | 3.86%
PA | 2.07%
ABS | 1.45%
PVC | 1.02%
PC | 0.65%
PUR | 0.45%
POM | 0.15%
PBT | 0.12%
PE | 0.00%
PET | 0.00%
PA11 | 0.00%
PLA | 0.00%
PBS | 0.00%
EP | 0.00%
ASA | 0.00%
PC+ABS | 0.00%
PMMA | 0.00%
BEV
Truck
Motorcycle
Extracted
common
-high sensitivity
-future usage
↓
11 resin types
OEMs are thinking a granularity of material classification
<IMDS>
・Parts list
・Detailed
Mat.Type
&
・Weight

## Slide 11: Next study proposal for level concept
 | Intensity data |  |  | 
Lv | Classification | Primary / Secondary | Electricity regionality | Recycle content ratio
1 | VDA | Secondary | Not considered - Global average | Not considered
2 | Detail classification | Secondary | Considered - By modeling | Considered - By modeling Secondary
3 | As above | Secondary & Primary combination | Considered - For secondary by modeling | Considered - By modeling Primary & Secondary
4 | As above | Primary | Considered | Considered Primary
Example
As we discussed in last meeting, material classification is one of discussion point on level concept.
However, If we see level concept in detail, especially as modeling, we can study to add some perspectives.

## Slide 12: Planning of Face to Face MTG
Deep discussion are necessary for Main material of Vehicle
Date |  | Item | 
28.Sep (Thu) | AM | Steel Discussion | Classification & System boundary definition
 | PM | Aluminum Discussion | 
29.Sept (Fri) | AM | Copper Discussion | 
 | PM | Resin Discussion | 

## Slide 13: MTG Schedule plan
SG2 MTG date | 2023 |  |  |  |  |  |  | 2024 |  | 
 | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar
 | 22 | 27 | 24 | 28 | 26 | 23 | - | 25 | 22 | 28
Every Month's 4th Thursday
19:00-20:00 (JST)
Online MTG
A-LCA IWG MTG
Jul.10 @online
Oct.17-18 ＠Brussel
Jan.xx @Geneva

## Slide 15: Agenda
Overall schedule
Discussion of Activity data & Intensity data
Discussion of Primary data (level concept)
Discussion of Material list for planning of Face to Face (in person) Meeting

## Slide 16: Discussion item for SG2
Discussion items for SG2 is updated in the meeting as below.
Definition of Activity data & Intensity Data
Primary Data concept (level concept)
Definition of Material list for Automotive LCA
System scope & boundary
How shall we collect data
Global & Regional Secondary data handling
Secondary data definition/which DB to use (incl. data quality)
Verification of data

## Slide 17: Overall schedule plan
 | 2023 |  |  |  |  |  |  |  |  | 2024 |  |  |  | 2025
 | Jun | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | 1Q | 2Q | 3Q | 4Q | -
IWG MTG |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Definition of Activity data & Intensity Data |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Primary Data concept |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Definition of Material list for Automotive LCA |  |  |  |  |  |  |  |  |  |  |  |  |  | 
System scope & boundary |  |  |  |  |  |  |  |  |  |  |  |  |  | 
How shall we collect data |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Global & Regional Secondary data handling |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Secondary data definition/which DB to use |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Verification of data |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 18: Level Concept of SG2
Level | Activity Data | Activity Data |  | Intensity Data
 | Vehicle Wight [kg] | Material Distribution [%] | Scrap Rate of Material [%] | Carbon Intensity of Material Acquisition [kg-CO2e/kg]
Level1 | Primary data | All Secondary data | All Secondary data | All Secondary data
 | Amount of Material Use at the Vehicle [kg] | Amount of Material Use [kg] | Scrap Rate of Material [%] | Carbon Intensity of Material Acquisition [kg-CO2e/kg]
Level2 | All Primary data | All Primary data | All Secondary data | All Secondary data
Level2.5 | ↑ | ↑ | Partially Primary data | ↑
Level3 | ↑ | ↑ | All Primary data | ↑
Level3.5 | ↑ | ↑ | ↑ | Partially Primary data
Level4 | ↑ | ↑ | ↑ | All Primary data

## Slide 19: Discussion of Activity data & Intensity data
reference:（2)Impact of recycling effect in comparative life cycle assessment for materialsselection - A case study of light-weighting vehicles
https://www.sciencedirect.com/science/article/pii/S0959652622009465?via%3Dihub
Material Weight
Material Loss Weight
Material Process

## Slide 20: Material List by VDA classification
VDA Classification | VDA Classification Name
1.1 | Steel/cast steel/sintered alloys
1.1.1 | Unalloyed/low alloy steel
1.1.2 | high-alloy steel
1.2 | cast iron
1.2.1 | Gneissic graphite cast iron/ malleable cast iron
1.2.2 | Spheroidal graphite cast iron/Vermular cast iron
1.2.3 | high-alloy cast iron
2.1 | Aluminium / aluminium alloys
2.1.1 | Cast aluminium alloys
2.1.2 | Forged aluminium alloy
2.2 | Magnesium, magnesium alloys
2.2.1 | Cast magnesium alloy
2.2.2 | Forged magnesium alloy
2.3 | Titanium, titanium alloys
3.1 | Copper (e.g. copper in harnesses)
3.2 | copper alloy
3.3 | zinc alloy
3.4 | nickel alloy
3.5 | lead (the metal)
4.1 | Platinum/rhodium
4.2 | Other special metals
VDA Classification | VDA Classification Name
5.1 | thermoplastic resin
5.1.a | Thermoplastic resin (containing filler)
5.1.b | Thermoplastic resin (without filler)
5.2 | thermoplastic elastomer
5.3 | Elastomer/elastomer composites
5.4 | thermosetting resin
5.4.1 | polyurethane
5.4.2 | unsaturated polyester
5.4.3 | Other thermosetting resins
5.5 | Polymer composites (e.g. laminated trim parts)
5.5.1 | Resins in polymer composites.
5.5.2 | Fibres in polymer composites (textiles)
6.1 | painting material
6.2 | Adhesives, sealants
6.3 | underseal
7.1 | Organic natural materials (e.g. leather)
7.2 | Ceramics/glass
7.3 | Other composite materials (e.g. friction linings)
8.1 | Electronic component materials (e.g. PCBs, displays)
8.2 | Electrical component materials
9.1 | fuel
9.2 | lubricant
9.3 | brake fluid
9.4 | Coolant/other glycols
9.5 | refrigerant
9.6 | Washer fluid, battery fluid
9.7 | preservative
9.8 | Other fuels and replenishers
 | Tyre
 | lead-acid battery
 | Drive battery cell

## Slide 21: Example of Material weight for each segment
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0.20946 | 0.30026 | 0.0092691 | 0.0032024 | 0.0086482 | 0.0042432 | 0 | 0.20175 | 0.024682 | 0.030608 | 0 | 0.0045494 | 0 | 0 | 0.0056142 | 0.0014751 | 0.0031462 | 0.00035558 | 0 | 0 | 0.0019449 | 0 | 0.038063 | 0.037992 | 0.0078869 | 0.017908 | 0.00017426 | 0.011989 | 5.7031e-05 | 0.0012467 | 0 | 0.0042059 | 0.013451 | 0.0018179 | 0.0014207 | 0 | 5.157e-05 | 0.023149 | 0.0077749 | 6.3388e-06 | 8.8867e-05 | 0 | 0.0010535 | 0.00061412 | 0.0033616 | 0.00079548 | 4.3111e-05 | 0 | 0.00066783 | 0.012535 | 0.0044373 | 0
Small ICE
Steel/cast steel/sintered alloys
Aluminium /
aluminium alloys
Resin
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0.15595 | 0.22426 | 0.013917 | 0.0027497 | 0.011466 | 0.016368 | 0 | 0.24782 | 0.048887 | 0.033641 | 0 | 0.00084054 | 0 | 0 | 0.011025 | 0.0017233 | 0.0050838 | 0.00059302 | 9.8896e-08 | 0.00016405 | 0.0079923 | 0 | 0.036414 | 0.037386 | 0.0064279 | 0.01301 | 0.00020903 | 0.0081403 | 0.00022645 | 0.0018556 | 0 | 0.0072618 | 0.00643 | 0.0040754 | 0.0071225 | 0.00058112 | 0.00017123 | 0.016003 | 0.0080245 | 4.6727e-05 | 0.00013486 | 0 | 0.00082835 | 0.00019091 | 0.0023218 | 0.00026105 | 0.00011283 | 5.8896e-06 | 0.00054861 | 0.016345 | 0.0021545 | 0.041228
Mid HEV
Steel/cast steel/sintered alloys
Aluminium /
aluminium alloys
Resin

## Slide 22: Example of Material weight for each segment
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0.076218 | 0.15352 | 0.0081075 | 0.0069775 | 0.0054789 | 0.0065432 | 0 | 0.15628 | 0.02804 | 0.038657 | 0 | 0.0020645 | 0 | 0 | 0.011116 | 0.0017432 | 0.0028921 | 0.00026588 | 7.993e-08 | 9.1269e-06 | 0.0056742 | 0 | 0.020114 | 0.023078 | 0.0038825 | 0.011028 | 0.00012729 | 0.0049735 | 0.00093585 | 0.0021081 | 0 | 0.000253 | 0.0028373 | 0.00090171 | 0.0012166 | 0 | 5.9021e-05 | 0.01456 | 0.0018766 | 9.3844e-06 | 3.5803e-06 | 0 | 0.00016373 | 0.00020529 | 0.0011237 | 0.00026592 | 1.0663e-05 | 0 | 0.0014859 | 0.0076002 | 0.0016378 | 0.39595
Small EV
Steel/cast steel/sintered alloys
Aluminium /
aluminium alloys
Resin
Drive battery cell
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0.056893 | 0.13381 | 0.0062477 | 0.0014129 | 0.0059123 | 0.0070964 | 0 | 0.35798 | 0.030829 | 0.069101 | 0 | 0.00085073 | 0 | 0 | 0.014839 | 0.0016848 | 0.0019126 | 0.0009911 | 6.1105e-08 | 0.021119 | 0.0026737 | 0 | 0.022655 | 0.021468 | 0.0036963 | 0.010101 | 2.6179e-05 | 0.003907 | 0.00014256 | 0.013079 | 0 | 0.0028092 | 0.0052164 | 0.0019195 | 0.0016465 | 0 | 0.0013324 | 0.0099628 | 0.12081 | 2.6149e-05 | 6.688e-05 | 0 | 0.00012662 | 0.00015891 | 0.00086988 | 0.00020584 | 7.0076e-06 | 0 | 0.00028021 | 0.0067416 | 0.0012278 | 0.058163
FCV
Steel/cast steel/sintered alloys
Aluminium /
aluminium alloys
Resin
Other composite materials

## Slide 23: Example of Material weight for each segment
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0 | 0.53677 | 0.030684 | 0 | 0 | 0.024514 | 0 | 0 | 0.17205 | 0.00074104 | 0 | 0 | 0 | 0 | 0.0068189 | 0.00063537 | 0.013502 | 0 | 0 | 0 | 0 | 0 | 0.029289 | 0.088125 | 0 | 0.023986 | 0 | 0.012899 | 0 | 0.00034613 | 0 | 0 | 0 | 0 | 0 | 0 | 6.4262e-05 | 7.2741e-05 | 0.0047102 | 0.00010373 | 0.017223 | 0 | 0.00030139 | 0 | 0 | 0 | 0 | 0 | 0 | 0.030986 | 0.0061809 | 0
Chart: 
| 鉄鋼/鋳鋼/焼結合金 | 非合金/低合金鋼 | 高合金鋼 | 鋳鉄 | 片状黒鉛鋳鉄/可鍛鋳鉄 | 球状黒鉛鋳鉄/ﾊﾞｰﾐｭﾗｰ鋳鉄 | 高合金鋳鉄 | ｱﾙﾐﾆｳﾑ/ｱﾙﾐﾆｳﾑ合金 | 鋳造ｱﾙﾐﾆｳﾑ合金 | 鍛造ｱﾙﾐﾆｳﾑ合金 | ﾏｸﾞﾈｼｳﾑ、ﾏｸﾞﾈｼｳﾑ合金 | 鋳造ﾏｸﾞﾈｼｳﾑ合金 | 鍛造ﾏｸﾞﾈｼｳﾑ合金 | チタン、チタン合金 | 銅 (例，ﾊｰﾈｽの銅) | 銅合金 | 亜鉛合金 | ニッケル合金 | 鉛 | 白金/ロジウム | その他の特殊金属 | 熱可塑性樹脂 | 熱可塑性樹脂（ﾌｨﾗｰ含有） | 熱可塑性樹脂（ﾌｨﾗｰ無し） | 熱可塑性エラストマー | エラストマー/エラストマー複合材 | 熱硬化性樹脂 | ポリウレタン | 不飽和ポリエステル | その他の熱硬化性樹脂 | 高分子複合材（例，ﾗﾐﾈｰﾄされたﾄﾘﾑ部品） | 高分子複合材に含まれる樹脂 | 高分子複合材に含まれる繊維（織物） | 塗料 | 接着剤、シーラント | アンダーシール | 有機天然材料 (例，皮革) | セラミックス/ガラス | 他の複合材（例，摩擦ライニング） | 電子部品材料（例，PCB、ﾃﾞｨｽﾌﾟﾚｰ） | 電気部品材料 | 燃料 | 潤滑剤 | ブレーキフルード | 冷却液/その他グリコール | 冷媒 | ウォッシャー液、バッテリー液 | 防腐剤 | その他の燃料及び補充剤 | タイヤ | 鉛電池 | 駆動用電池セル
 | 0 | 0.44029 | 0.03235 | 0 | 0 | 0.019976 | 0.0073799 | 0 | 0.26845 | 0.027938 | 0 | 0 | 0 | 0 | 0.0057949 | 0.00036358 | 0.0048947 | 0 | 0 | 0 | 0 | 0 | 0.0037685 | 0.072951 | 0.00011609 | 0.037127 | 0 | 0.0057814 | 0 | 0.00012253 | 0 | 0 | 0 | 0 | 0 | 0 | 2.8085e-05 | 0.00034175 | 0.00011242 | 0 | 0.026157 | 0 | 0.0042718 | 0 | 0.0046231 | 0 | 0 | 0 | 0 | 0.029817 | 0.0073502 | 0
Small Motorcycle
Steel/cast steel/
sintered alloys
Resin
Aluminium /
aluminium alloys
Steel/cast steel/
sintered alloys
Resin
Aluminium /
aluminium alloys
Mid Motorcycle

## Slide 24: Example of Material weight for each segment
Need to discuss system boundary of each material
■Example of Steel
Mining

## Slide 25: Request till next MTG
Please bring your idea of Material classification

## Slide 26: Planning of Face to Face MTG
Deep discussion are necessary for Main material of Vehicle
Date |  | Item | 
28.Sep (Thu) | AM | Steel Discussion | Classification & System boundary definition
 | PM | Aluminum Discussion | 
29.Sept (Fri) | AM | Copper Discussion | 
 | PM | Resin Discussion | 

## Slide 27: MTG Schedule plan
SG2 MTG date | 2023 |  |  |  |  |  |  | 2024 |  | 
 | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar
 | 22 | 27 | 24 | 28 | 26 | 23 | - | 25 | 22 | 28
Every Month's 4th Thursday
19:00-20:00 (JST)
Online MTG
A-LCA IWG MTG
Jul.10 @online
Oct.17-18 ＠Brussel
Jan.xx @Geneva