## Slide 1: SG4 Status report
34th VMAD Meeting Somewhere between 11 - 15 December 2023
VMAD-34-03-rev.1

## Slide 2: SG4 Meetings
2
  SG4 held 3 meetings in October:
    13, 20, 31 October
  Focus on final discussions on the proposed amendments to the NATM Guidelines
  If no consensus limit the possibilities to two options. These options are presented in Tokio.
  For the context please see VMAD-34-04-rev1 “SG4 proposed Amendments to the NATM Guidelines”
  Note in VMAD-34-04-rev1
    all bold items are new items
    all items in [ ] still require agreement (focus today on these items).

## Slide 3: SG4 Draft Amendments
3
Decision Amendment to the Track Testing chapter
47c.
OPTION 1:
It is recommended that the selection of scenarios to be conducted on a test track contributes towards the overall coverage necessary for the validation of parameters that can vary in the ODD, where possible. Track test environments allow for controllability and assurance that specific parameters that can vary in the ODD can be delivered during physical testing.
OPTION 2:
It is recommended that the selection of scenarios to be conducted on a test track is suitably representative of the ODD, where possible. Track test environments allow for controllability and assurance that specific parameters that can vary in the ODD can be delivered during physical testing.

## Slide 4: SG4 Draft Amendments
4
Decision Amendment to the Track Testing chapter
47g.
Option 1:
It is recommended that for track testing a protocol is developed containing minimum requirements that standardise how for the test relevant data are to be collected and analysed (e.g., how the data is recorded, how measurements are derived from the recorded data, and how the measurements are analysed).
Option 2:
No 47g

## Slide 5: SG4 Draft Amendments
5
Decision Amendment to the Real-World Testing chapter
51 It is recommended that real world testing:
Option 1:
(aa-new) is done safely. It is therefore recommended, if applicable to the ADS use case,] the test supervisor has the possibility to [trigger/request] the end of the real world test at any point. In addition, it is also recommended that any dangerous behaviour observed and/or the reason to [trigger/request] the end of the real world test is investigated in detail later;
(aa-new) is done safely. It is therefore recommended, if applicable to the ADS use case, the test supervisor has the possibility to end the real world test at any point. In addition, it is also recommended that any inappropriate behaviour observed and/or the reason for the forced end is investigated in detail later;
Option 2:
No (aa-new)

## Slide 6: SG4 Draft Amendments
6
Decision Amendment to the Real-World Testing chapter
51a. It is furthermore recommended that:
Option 1:
(a) a methodology is developed to determine the minimum exposure based on the ODD of the ADS under test;
Option 2:
No (a)

## Slide 7: SG4 Draft Amendments
7
Decision Amendment to the Real-World Testing chapter
51a. It is furthermore recommended that:
Option 1:
(b) the minimum test exposure refers to the minimum exposure during which the ADS vehicle is tested on public roads in each country/state in which the vehicle is intended to be deployed;
Option 2:
No (b)

## Slide 8: SG4 Draft Amendments
8
Decision Amendment to the Real-World Testing chapter
54a.
Option 1:
It is recommended that for real world testing a protocol is developed containing minimum requirements that standardise how for the test relevant data are to be collected and analysed (e.g., how the data is recorded, how measurements are derived from the recorded data, and how the measurements are analysed).
Option 2:
No 54a

## Slide 9: SG4 Draft Amendments
9
Agreement on use of ‘naïve other road users’:
“naïve other road user” means another road user (ORU) encountered during real-world testing (presumed to be) unaware that the ADS vehicle is under test.
Justification:
“Naïve” to be used in order to emphasize that the other road users, as referenced in the section on real world testing, are (presumed to be) unaware that the ADS vehicle is being submitted to a real world test.
Option 1: Agree and use
Option 2: No need for naïve other road users

## Slide 10: SG4 Draft Amendments
10
Agreement on definition of ‘Real-world test scenario’:
“real-world testing scenario” (or RWT scenario for short) means a traffic scenario that occurs, or is desired to occur, during a real-world test. Due to the dynamic nature of traffic on public roads, the description of RWT scenarios desired to occur during real-world testing remains at the level of a functional scenario in order to ensure the desired scenario has a higher likelihood to occur during real-world testing. By collecting data during the test, a scenario that occurs during real-world testing can be described with the level of detail of a concrete scenario.
Comments?
There is no need for it

## Slide 11: SG4 Draft Amendments
11
Agreement on use of ‘Pass-fail criteria’ in Real-world test without a definition:
No definition for pass-fail criteria (in the context of RWT scenarios) is proposed, as by adding a more elaborate definition for RWT scenario, it is implicit that the level of detail of the pass-fail criteria would depend on the level of detail of the respective RWT scenario.
Comments?
Future work

## Slide 12: From SG4 to SG3
12
VMAD SG4 request/suggestion to VMAD SG3
Consider including testing with a naïve participant in the driver seat as part of the audit, if not already covered. Moreover, consideration should be given to have manufacturers expand on the details of the naïve participants to ensure representativeness of the general population
For more details see VMAD-34-05 SG4‘Recommendation for consideration at SG3 of naïve participant testing’
Future work?

## Slide 13: SG4’s call to the future
13
No recommendations on ‘on-board operator’.
  SG4 had suggestions on testing with on-board operator
No recommendations on ‘remote operation’
  SG4 had suggestions on testing with remote operation
Fall-back user selection
  Professional user or not? Experienced or not?
Who is liable during a real-world test?
  Not part of WP.29, belongs WP.1
No pass fail criteria
How to deal with tests on test tracks which are outside ODD
RWT scenarios / engineered test routes protocols
(Driving monitoring Systems)
See VMAD34-06 SG4 ‘Recommendations on topics for future discussions at VMAD’

## Slide 14: Thanks
14