## Slide 1: WTPP status report to IWG WGWT 5 December 2023
IWG WGWT 53rd session
WT-53-3

## Slide 2: WTPP meetings
WTPP convened on 27 November 2023
WTPP reviewed the test data from the 12 test centers (80% of the participants)
ETRTO presented its preliminary assessment on 27 November.
Next meeting is foreseen on 6 December 2023

## Slide 3: WTPP 2023 test campaign target.
PROBLEMATIC:
In previous UNECE IWG Round Robins/Test Campaigns (2021-2022):
Worn WG test uncertainty was shown to be in the same order of magnitude as the old WG test method (R117.02 Suppl. 12 or ISO 23671:2015), before improvement of the Pooled StdDev with R117.02 Suppl. 13
Higher spread was observed for ‘worn’ SRTT16 (buffed & molded) compared to ‘new’ SRTT16, what could potentially explain the test uncertainty situation - even if terms for Mu-Peak / BFC of ‘worn’ SRTT16 are included in the correction equations of WWGI (R117.03/.04 Annex 9). The Water Depth* was identified as the main parameter influencing this spread.
GOAL:
Build a better understanding and link between the “real” Water Depth seen by the tyres during testing and the raw Wet Grip test outcome (Mu-Peak/BFC)
APPROACH:
Improve alignment between test centers on Water Depth measurement
Collect data of ‘worn’ & ‘new’ SRTT16 tested back-to-back with Trailer & Vehicle methods and in different conditions (Temperature, Track, Self-/External-Watering,…) along with measurements of Water Depth & Mean Texture Depth (MTD)
* The current text of R117 Annex 5 & 9, requires a Water Depth between 0.5 & 1.5 mm, however, it does not specify a standard method for measuring this Water Depth

## Slide 4: IWG WGWT 2023 Test campaign – Test Plan
Test Centers: 15
Test Methods: Trailer & Vehicle
Candidate tyres: 0
Reference:
  SRTT16 (‘new’ state)  RN
  LTD SRTT16 (‘worn’ state - molded)  RM
Test Conditions: R117.04 Annex 9
Track Characterization:
  Water Depth mapping
  MTD mapping
Dataset: 208 data points
Data collection status: 80% (12/15 test centers) – 17th Nov. 2023
 | Screening | Self- vs External-Watering (Trailer)
Number of Test Centers | 12 | 3
Test Sequence | RM-RN-RM | RM-RN
Repeats | 6 (2 per Temp. Range) | 1
Temperature Ranges | Low: 5-14°C Medium: 15-24°C High: 25-35°C | Nominal
Water Depth [mm] | Nominal | Self-Watering: 0 / 0.5 / 1.0 / 1.5 External-Watering: 0 / 0.5 / 1.0 / 1.5

## Slide 5: WTPP ongoing analysis
WTPP will review the ETRTO analysis on:
  Test results overview – Trailer/Vehicle, ‘worn’/’new’ SRTT16
  Overview per test center
  Trailer method – Water Depth & track MTD trends, External-/Self-Watering
  Trailer method – Wetted surface Temperature trend, External-/Self-Watering
  Vehicle method – Water Depth & track MTD trends
  Vehicle method – Wetted surface Temperature trend
WTPP will need the additional data (mainly low temperature range) to pursue and complete the analysis.
JASIC will proceed with the study of self-watering versus external watering (6 December).

## Slide 6: Next steps
WTPP experts to review and complete the data analysis
WTPP experts to draft conclusions on:
  Need for recommendations on waterheight measurement instruments
  The“real” Water Depth seen by the tyre for the 2 testing methods including watering systems.
  Deciding on the need for additional test campaign 2024-2025
 WTPP to report its conclusions by next IWG WGWT meeting before GRBP 79th session.

## Slide 7: Thank you