## Slide 1
Are the requirements as proposed during SLR 65 (SLR-65-08) sufficient to improve the visibility and ensure a clear signal of the direction indicator?
The following schematic illustration is showing an example seen on the road. Even if the DIs are clearly visible when they light up on their own, it is very difficult to recognise the DIs when they light up together with the brake lights.
Stop lamp
Direction indicator
Position lamp
High luminance of the stop lamp causes the DI to be outshone!
SLR-66-09
Improve visibility of DI

## Slide 2
Although the arrangement shown in the example would fulfil the proposed requirements of SLR-65-08, the visibility of the DI is not guaranteed if it is illuminated together with the stop light.
Further aspects mentioned during SLR 64 and 65 to be discussed:
Define a minimum distance from DI to the stop lamp (in the front minimum distance from DI to passing beam and DRL)
Consider a luminous intensity or luminance ratio between DI and stop lamp
measurements with simultaneous activation of the function (problem: different manufacturers of the functions and aftermarket devices!)
Improve visibility of DI