## Slide 1: Task Force Tire Abrasion
Questions on test method and type approval procedure
24 January 2024
Transmitted by experts of OICA

## Slide 2: Vehicle Selection for on-road method
Vehicle related requirements exclude certain vehicles from regulatory testing.
Example 1:
  Air spring systems allow the ride height to change during driving.
  This causes the axle kinematics to change, including toe and camber.
  The ride hight is typically adjusted automatically depending on speed, driving mode, state of charge, and other factors and cannot be predeterminded or fixed by the driver.
Example 2:
  Some OEM use mixed fitment exclusively (different tyre sizes on front and rear axles).
Consequently, toe and camber cannot be guaranteed pursuant to paragraph 1.6.6.
OICA is seeking confirmation that
  the on-road test method is suitable for type approval of all tyre sizes,
  in case no suitable vehicle can be found for special tyre sizes, type approval can be obtained by testing „representative sizes“ in combination with „worst case testing“.

## Slide 3: Repeatability vs. Representativity
The very neutral requirements for axle kinematics do not match the settings of some OEM vehicles.
We received feedback from individual OEMs that non of their vehicles meet the current requirements for very neutral axle kinematics (low fall and lead lane).
As a result, the actual tire abrasion of some OEM vehicles is not reflected by the current test methods.
However, OICA understands this to be a compromise to allow for high repeatability and a robust regulation fit for 3rd party testing.

## Slide 4: Thank you for your attention!