## Slide 1: WLTP Open Issue Phase 1B
Issue: Generic formula for total hydrocarbon density
.
ACEA Informal Document 04.06.2014
WLTP-07-11e

## Slide 2
Proposal:
A generic formula for the density of total hydrocarbons should be added. The ratios of H/C and O/C for reference fuels shall be taken from Annex 3. These numbers have to be added to the actual draft. The density shall be rounded to three decimal places.
Rationale:
The density of total hydrocarbons (THC) of different types of fuel differ due to varying H/C and O/C ratios. This approach supports the simple adaption to future reference fuels or changes to the existing ones. A generic formula in combination with the nomination of the H/C and O/C ratios in Annex 3 results in clarification and standardization of the density values.

## Slide 3
ρTHC: density of total hydrocarbons and non-methane hydrocarbons [g/l]
MWC: molecular weight of carbon = 12.011 g/mol
MWH: molecular weight of hydrogen = 1.008 g/mol
MWO: molecular weight of oxygen = 15.999 g/mol
VM: molar volume for an ideal gas at 0°C and 101.325 kPa = 22.413 l/mol
H/C: ratio of hydrogen to carbon for a specific fuel CxHyOz
O/C: ratio of oxygen to carbon for a specific fuel CxHyOz
Generic formula

## Slide 4
Hydrocarbons:
for petrol (E0) (C1H1.85) ρ = 0.619 g/l
for petrol (E5) (C1H1.89O0.033) ρ = 0.645g/l
for petrol (E10) (C1H1.93O0.016) ρ = 0.631 g/l added to current GTR
for diesel (B0) (C1H1.86) ρ = 0.619 g/l
for diesel (B5) (C1H1.86O0.005) ρ = 0.622 g/l
for diesel (B7) (C1H1.86O0.007) ρ = 0.623 g/l added to current GTR
for LPG (C1H2.525) ρ = 0.649 g/l
for NG/biomethane (CH4) ρ = 0.714 g/l
for ethanol (E85) (C1H2.74O0.385) ρ = 0.932 g/l
  The density for NMHC mass calculations shall be equal to that of total hydrocarbons at 273.15 K and 101.325 kPa and is fuel-dependent.
Text of WLTP GTR

## Slide 5
Hydrocarbons: GTR Calc.
for petrol (E0) (C1H1.85) ρ = 0.619 g/l 0.619 g/l
for petrol (E5) (C1H1.89O0.033) ρ = 0.645g/l 0.646 g/l
for petrol (E10) (C1H1.93O0.016) ρ = 0.631 g/l 0.632 g/l
for diesel (B0) (C1H1.86) ρ = 0.619 g/l 0.620 g/l
for diesel (B5) (C1H1.86O0.005) ρ = 0.622 g/l 0.623 g/l
for diesel (B7) (C1H1.86O0.007) ρ = 0.623 g/l 0.625 g/l
for LPG (C1H2.525) ρ = 0.649 g/l 0.649 g/l
for NG/biomethane (CH4) ρ = 0.714 g/l 0.716 g/l
for ethanol (E85) (C1H2.74O0.385) ρ = 0.932 g/l 0.934 g/l
  The density for NMHC mass calculations shall be equal to that of total hydrocarbons at 273.15 K and 101.325 kPa and is fuel-dependent.
Deviation: GTR vs. Calculation

## Slide 6
ρTHC: density of total hydrocarbons and non-methane hydrocarbons [g/l]
MWC: molecular weight of carbon = 12.011 12 g/mol
MWH: molecular weight of hydrogen = 1.008 1 g/mol
MWO: molecular weight of oxygen = 15.999 16 g/mol
VM: molar volume for an ideal gas at 0°C and 101.325 kPa = 22.413 l/mol
H/C: ratio of hydrogen to carbon for a specific fuel CxHyOz
O/C: ratio of oxygen to carbon for a specific fuel CxHyOz
Reason for deviation

## Slide 7
Approach
- Generic formula will be added to GTR
- Any new fuel will be added to Annex 3
- Based on generic formula and new ref. fuel the density will be calc.
- Density of new ref. fuel will be added to Annex 7
- Density values in GTR will be adjusted (molecular weight C, H, O
with 3 decimal places)