## Slide 1: TASK FORCE ON AUTOMATED VEHICLE CATEGORISATION (AVC)
Second Meeting:
20 & 21st February 2024
Agenda Item 4:
High level thinking on the challenges raised by automation

## Slide 2: 1. Key definitions in R.E.3 and S.R.1 underpin the definitions in UNRs/GTRs and domestic frameworks (e.g. M1, N1 and defining ADS, ADS vehicle, dual-mode vehicle, manual controls etc). 2. Categorisation groups together vehicles with similar characteristics in order to: - define applicability of UNRs/GTRs (e.g. scope). - apply different technical requirements within UNRs/GTRs. 3. Impact on domestic requirements/regulations. 4. Clear guidance for industry: - if we don't consider novel vehicle designs, we may not see them come to market. Vehicle categories are also used outside of type approval… considerations for traffic rules, driver licensing, taxation, statistics etc.
Why are common definitions and vehicle categorisation important?
Notes: Harmonised understanding of what these vehicle types are, a single reference point to refer to in all other groups/documents.

## Slide 3: 1. References to ‘driver’, number of seats in relation to ‘driver’s seat’: there may not be a driver or driver’s seat: "Category M1": Vehicles used for the carriage of passengers and comprising not more than eight seats in addition to the driver's seat. 2. New definitions are needed which are harmonised across multiple regulations (e.g. ADS, ADS Vehicle, dual-mode vehicle, manual controls etc). 3. Current technical requirements are not suitable for every automated vehicle that falls into a given category. For example: vehicles without manual driving controls, etc. Resulting in: - inappropriately applied technical requirements OR - lack of technical requirements which address unique aspects of AV functionality OR - barriers to the application of a particular regulation/s
What are the challenges raised by vehicle automation?
Addressed with definition changes new definitions
Addressed with re-consideration of vehicle categories

## Slide 4: - Carriage of 5 seated passengers - DDT can only be performed by an ADS (i.e. no manual controls or driver's seat) Low-speed​ vehicle - Limited ODD, e.g. speed restricted roads Currently… M1 requirements would apply, e.g. crashworthiness regulations: - UNR 94: Protection of occupants in the event of a frontal collision - UNR 95: Protection of occupants in the event of a lateral collision How do we set appropriate requirements?
For example…
Notes: Similar example for a vehicle with 0 occupants, might be considered as N1 which is still subject to increased crashworthiness requirements?

## Slide 5: Additional considerations: 1. Development of AV categorisation would assist the development of an ADS UNR/GTR. This work should be done in parallel, with consideration to complete work on categorisation first. 2. Development of AV categorisation would assist the work of TF-FADS to consider amendments to non-ADS UNRs/GTRs
All proposals should (taken from guidance document):
1. Vehicle categories classify vehicles according to their typical usage and common characteristics, allowing their inclusion in (or exclusion from) the scope of individual UN Regulations, Global Technical Regulations, and specific requirements within these Regulations.
2. Categories for automated vehicles are also needed for administrative considerations such as vehicle registration, traffic rules and their enforcement, taxation, and road traffic safety statistics. The experts of this group shall be considerate to these aspects where possible.
3. Understanding how categories of vehicles can affect national and regional laws, the expert group is open to stakeholders from all affected Contracting Parties — including Regional Economic Integration Organisations — to strongly contribute to this work. Other stakeholders from international organisations and the industry are also welcome.
4. Categories of vehicles are relevant to international and national activities beyond the World Forum. The task force should therefore be open to experts with a strong technical expertise, and all stakeholders with a direct interest in the evolution of vehicle categories.
5. The redefinition or addition of categories should be as simple as possible and limited to what is necessary. Furthermore, new subcategories represent a lower administrative impact than new categories. Finally, maintaining existing categories is less complex than a complete redefinition of all categories.
6. The updated categories should be technologically neutral and tackle all relevant use cases for automated vehicles transporting passengers, goods, a combination of both, or neither. This includes vehicles also equipped with manual controls, those which are not designed to carry human occupants and those which are also designed for off-road operation.
7. The group should therefore:
Identify the challenges raised by automation and explain in writing how the proposals will address those issues.
Determine how vehicle categorisation should be approached to address automated vehicle specificities and
in doing so keeping in mind the two categorisation systems set in the consolidated resolution on the construction of vehicles (R.E.3) and consolidated special resolution concerning the common definitions of vehicle categories, masses and dimensions (S.R.1).
Prepare a proposal for automated vehicle categorisation, which could be used to adapt R.E.3 and S.R.1.
Consider the addition/amendment of definitions within proposals to accommodate automated vehicles.
Measures of success