## Slide 1: ETRTO proposal for IWG WGWT workplan 2024-2025
IWG WGWT meeting 56th session on 13 March 2024

## Slide 2: Outlines
Reminder: IWG WGWT work progress
Objectives of the next test campaign
Definition of the test plan
JASIC proposal
Concept proposal for tyre selection
Conclusions

## Slide 3: 1. Reminder: IWG WGWT work progress

## Slide 4: 1. Reminder: IWG WGWT work progress

## Slide 5: 2. Objectives of the test campaign 2024/2025
ETRTO propose to adjust the test plan to the chosen objectives.
Option 1: to confirm the effectiveness of the proposed change in wetted frictional properties, and its impact on candidate tires Analytical plan
Option 2: to evaluate the need to review the coefficients of the correction equations
Tyres’ trends confirmation

## Slide 6: 3. Definition of the test plan (analytical).
Objective: to confirm the effectiveness of the proposed change in wetted frictional properties
Analytical plan for candidate tires: Candidate 1-4: Summer Candidate 5-7: 3PMSF Candidate 8: Ice
Test sequence: Molded SRTT- Candidate 1 – Candidate 2 – Candidate 3 – Molded SRTT
Method Trailer and vehicle
Participants: All the test centers (14?)
Track friction range: New tightened friction range
Repeat: 5 measurements per tire per method = 5 x 8 tires* x 2 = 80  6 to 8 tires to be measured by participants (assuming 10 to 14 participants)  2 to 3 tests sequences by participant
* Pending on the number of participating test centers

## Slide 7: 3. Definition of the test plan (tyres’ trends confirmation).
Objective: to review the coefficient of the equation based on complementary data to initial market assessment
Candidate tires: Minimum 20 Summer, 4 M&S, 12 Winter = half size of previous RRT
Test sequence: Molded SRTT- Candidate 1 – Candidate 2 – Candidate 3 – Molded SRTT
Methods Trailer and vehicle
Participants: All the test centers will test some tires
Track friction range: New tightened friction range
Repeat: 3 measurements per tyre per method = 3 x 36 tires* x 2 = 216 measurements  16 to 22 tires to be measured by participants (assuming 10 to 14 participants)  6 to 8 test sequences by participant
* Pending on the number of participating test centers

## Slide 8: 4. JASIC proposal (WT-53-7)

## Slide 9: 5. Concept proposal for tyre selection
For wet adhesion of tyres in worn state, UNECE R117.04 categorizes C1 tyres as follows:
NORMAL
SNOW
SPECIAL
USE
Tyres commonly referred to as ‘Summer Tyres’
Tyres commonly referred to as ‘Ultra High Performance Tyres’
Tyres commonly referred to as ‘All Season Tyres’
Tyres commonly referred to as ‘Winter Tyres’
Tyres commonly referred to as ‘All Terrain Tyres’
Tyres referred to as ‘Scandinavian Winter Tyres’ or ‘Nordic Winter Tyres’

## Slide 10: UNECE R117.04 Tyre Categorization (wet adhesion in worn state)
The table shows C1 Categorization as specified in UNECE R117.04 – section 6.4.1.
We propose to select candidate tires which reflect ‘worst case’ and ‘best case’ from each of the defined categories (and sub-categories).
A definition for ‘worst case’ performance of wet grip in worn state may be available by Tyre Type Approval Authorities (e.g. RDW).

## Slide 11: Concept proposal
Evaluate all categories of tires as defined in section 6.4.1. of UNECE R117.04.
Evaluate all categories from a ‘worst case’ and ‘best case’ perspective.
Evaluate tires which are labeled to perform both well and poorly (in new state) in both case scenarios.
Tyres to be representative of the market
example
To be considered by IWG WGWT

## Slide 12: Timeline for workplan2024-2025
Q1 2024 Q2 2024 Q3 2024 Q4 2024 Q1 2025 Q2 2025 Q3 2025 Q4 2025 Q1 2026
Testing
Regulatory
process
GRBP Informal document
Workplan 2024-2025 definition
Testing period
Tyre selection
GRBP Working document
13 March 2024
Logistics and test center preparation
Post processing
Drafting group
Tyre preparation

## Slide 13: 6. Conclusions
The workplan 2024-2025 proposal to perform the 2 options (analytical plan and tyres’ trend confirmation) will permit to achieve the objectives defined: - to confirm the effectiveness of the reduced friction range in reducing test dispersion - to evaluate the need to update the correction coefficients
This will require roughly 10 tests (8 to 11) sequences per test center [SRTT- Candidate 1- candidate 2- candidate 3 – SRTT]
The proposed tyre selection concept will allow to get a representative sample of UN market in term of WGI @ worn performance and tyres’ trends

## Slide 14: Thank you