## Slide 1: SIG on Thermal propagation Discussion points
3rd meeting, 12/Mar – 14/Mar 2024
Prepared by Secretary
SIGTP-03-03r2
Update noting the conclusions at SIG#3

## Slide 2: 1. Objective and principles
Objective (of SIG-TP)
To provide robust procedures to assess thermal propagation performance that enable harmonized implementation (among CP to the 58 Agreement and other nations interested)
Principles
UN-R100-03 Transitional provisions: Sep 23 (NT), Sep 25 (All) [R100-04 Sep 26 (NT), Sep 27 (All)]
EU policy decision to ban (in principle) ICE from 2035
Improve implementation of R100-03 Thermal propagation requirements
No intention to strengthen/reduce the stringency level from R100-03
Maintain framework of REESS type approval
To be reasonable, effective and practicable
Remain focusing on occupant protection
Re-Confirmed
Action (All)
Consider Transitional provisions for R100
REMINDER
See slides 14 - 16

## Slide 3: 2. Alignment points (1)
SOC adjustment according to R100-03 (=GTR20 Phase 1)
Observation for 2h from TR initiation
No hazardous situation w/o warning or within 5 min from warning
TR but No Thermal Propagation = PASS condition
SOC adjustment according to R100-03 (=GTR20 Phase 1)
Need to define “master (main)” initiation method  Fast external heating (with 20% input energy limit) + 1h observation
  If no TR (with external heater & 20% energy limit) is confirmed (on cell/module level), no need to use other initiation method
No Thermal Runaway = PASS condition
dT/dt >1K/s should be reconfirmed with available data (minimize probability of force positive)
TR detection criteria
Confirmed
1h observation
Amended
Confirmed dT/dt criterion

## Slide 4: 2. Alignment points (2)
By nature (smaller cell/battery, low SOC in normal use cases), NOVC-HEVs are unlikely to cause TP/TR due to internal SC
OICA proposal is to apply risk management approach (possibly with smaller scale experiments (e.g. cell or module level)
Treatment of REESS for NOVC-HEV
Proposed text in 6.15.3.1
[If the REESS is designed not to have coupling system for charging the Rechargeable Electrical Energy Storage System (REESS), only the risk management analysis according to paragraph 6.15.4. needs to shall be performed. ]
Text for 6.15.3. is amended as above.
CPs to confirm the decision

## Slide 5: 2. Alignment points (3)
The (REESS or vehicle) manufacturer submit their proposal whether testing with REESS (or REESS subsystem) or vehicle.  TS/TAA to approve/not to approve.
Are the test procedures (and criteria) sufficiently described for REESS level test?
  Smoke assessment (see later slides)
  Egress time (see later slides)
Need to refine vehicle installation requirements and its certification procedure
REESS level certification
CPs (NL, DE, FR, AUS, (SE)) requested to keep REESS level test at mfr’s discretion (approval by TAA/TS)
6.15.3. (verification procedure) is amended to allow REESS level certification and to require additional assessment at vehicle level.
5.2.1.1. (vehicle installation) need to be adapted.
Flowchart to be prepared by Secretary in line with the conclusions and added somewhere in the document.

## Slide 6: 2. Alignment points (4)
What will be the practicable way to assess at both vehicle level and REESS level?
No quantitative measurement feasible  What and how to confirm in visual inspection?
Any supplemental analysis?  Additional requirements for vehicle level
Smoke assessment
Maintain “visual inspection”
For REESS level test/certification, additional requirements for vehicle level (smoke ingress test, ensure relevant behaviour) are added.
5.2.1.1. (vehicle installation) need to be adapted.

## Slide 7: 2. Alignment points (5)
“allow egress” requires manufacturer’s justification  Only feasible for certification in combination with certain vehicle models
5 minutes is the default length if no justification provided
Should “no smoke ingress” into passenger compartment apply only until the door is opened?
Allow egress or 5 minutes
Delete “allow egress” and only to use “5 minutes” duration in 05 series
Exemption from AT date for vehicles approved to 03/04 series using “allow egress” provision.  03/04 series needs to be amended to allow distinction.

## Slide 8: 2. Alignment points (6)
Manufacturers should not be obliged to evaluate using multiple initiation methods  Manufacturer should be able to chose the most suitable method
Should alternative methods be limited to those in the Regulation?
How much variables would be acceptable? (Even for external heater there are variables such as heater specifications)
What should be accounted for equivalency?
Alternative initiation methods
Agreed on the text proposed by OICA with some editorials and recording requirement for TAA/TS.
Since “e.g.” is given, “etc.” is considered as redundant.

## Slide 9: 2. Alignment points (7)
Pre-instrumentation is not allowed  Feasibility to apply the test procedure might be reduced
For consideration of the influence to the test results, will the prescriptions in Annex 9K, para.3.2. be sufficient?
DUT modification
Pre-instrumentation is allowed
Details of the pre-instrumentation shall be included in the initial documentation.
Reconfirm updated text of Annex 9K, 3.2

## Slide 10: 2. Alignment points (8)
For testing, only temporary parking mode will be tested
For risk management analysis, other normal operation modes (e.g. parking, charging, active driving) should also be considered.
Occupant protection in parking mode may depends on the manufacturer’s philosophy.
Operating mode
No questions/inputs provided

## Slide 11: 2. Alignment points (9)
Need to clarify how to apply the family concept in practise  To allow carry-across the thermal propagation verification between different type of REESS or vehicles
Will vehicle family be necessary if REESS type approval and REESS family concept are agreed?
Family concept for thermal propagation assessment
OICA: Withdraw proposal as REESS type approval can serve for this.

## Slide 12: 2. Alignment points (10)
Review updated text of Annex 9K (general conditions) and each Appendix (Specific to the initiation method)
Test procedure details
JRC to provide updates taking account of the comments give.

## Slide 13: 3. Other issues(1)
OICA proposed new paragraphs 3.4. & 3.5, similar to R155/R156
Manufacturer is responsible to provide and retain the information supplemental to the documentation package
Confidentiality
All to reconfirm the description.
To be included in the supplements to 03 and 04 as well

## Slide 14: 3. Other issues(2)
Transitional provisions
2021
2022
2023
2024
2025
2026
2027
2028
2029
2030
2031
R100/03 (all M/N affected)
Entry into force (Jun/2021)
AT (Sep/2025)
NT (Sep/2023)
R100/04 (M2,M3,N2,N3 vehicles)
Entry into force (Jan/2025)
AT (Sep/2027)
NT (Sep/2026)
R100/05 (REESS with LiB)
GRSP#1
GRSP#2
WP29
WP29
Entry into force (Jan/2026)
(Expected timelines in current proposal)
Will AT date needed?  No stringency level change  Include AT date but certain exemption for smoke in 5min.
How long period is needed for NT date (test facility preparation, etc.)
REESS other than LiB (flammable electrolyte) are not affected
How long??

## Slide 15: (Transitional provisions in guideline – WP29/1044/Rev.3)
V.1. As from the official date of entry into force of the XX series of amendments, no Contracting Party applying this Regulation shall refuse to grant or refuse to accept type approvals under this Regulation as amended by the 05 series of amendments.
V.2. As from 1 September Date (b), Contracting Parties applying this Regulation shall not be obliged to accept type approvals to the preceding series of amendments, first issued after 1 September Date (b).
V.3. Until 1 September Date (c), Contracting Parties applying this Regulation shall accept type approvals to the preceding series of amendments, first issued before 1 September Date (b).3
V.4. As from 1 September Date (c), Contracting Parties applying this Regulation shall not be obliged to accept type approvals issued to the preceding series of amendments to this Regulation., ,
V.5. Notwithstanding the transitional provisions above, Contracting Parties who start to apply this Regulation after the date of entry into force of the most recent series of amendments are not obliged to accept type approvals which were granted in accordance with any of the preceding series of amendments to this Regulation / are only obliged to accept type approval granted in accordance with the XX series of amendments.
V.6. Notwithstanding paragraph V.4, Contracting Parties applying this Regulation shall continue to accept type approvals of the equipment/parts issued according to the preceding series of amendments to this Regulation.1
(Note: V.6 is for special case 1-1 and comes in addition to V.4 when applicable)
V.7. Notwithstanding paragraph V.4, Contracting Parties applying this Regulation shall continue to accept type approvals issued according to the preceding series of amendments to this Regulation, for the vehicles/vehicle systems which are not affected by the changes introduced by the XX series of amendments.2
(Note: V.7 is for special case 1-2 and comes in addition to V.4 when applicable.)
V.8. Contracting Parties applying this Regulation shall continue to accept type approvals issued according to the preceding series of amendments to this Regulation first issued before Date (b).3
(Note: V.8 is for special case 1-3 and would replace V.4 when applicable.)
V.9. Contracting Parties applying this Regulation may grant type approvals according to any preceding series of amendments to this Regulation.
V.9bis. Contracting Parties applying this Regulation shall continue to grant extensions of existing approvals to any preceding series of amendments to this Regulation
Special case 1-1: V.6 can be used in addition to V.4 when requirements for the installation of equipment/parts are added to a UN Regulation but without modifying the requirements of, and the approval markings for these equipment/parts.
Special case 1-2: V.7 can be used in addition to V.4 when some vehicle categories/vehicle systems are not affected by the amendment.
Special case 1-3: V.8 replaces V.3 and V.4 in the case of indefinite acceptance of existing approvals previously granted according to the former series of amendments.
No AT date: V.1, V.2, V.8, V.5, V.9 and V.9bis
With At date: V.1, V.2, V.3, V.4, V.5, V.7, V.9 and V.9bis + special provision for egress time
Possible choices

## Slide 16
Insert new paragraphs 12.10. to 12.16., to read:
12.10. As from the official date of entry into force of the 05 series of amendments, no Contracting Party applying this UN Regulation shall refuse to grant or refuse to accept UN type approvals under this UN Regulation as amended by the 05 series of amendments.
12.11. As from [1 September 2028], Contracting Parties applying this UN Regulation shall not be obliged to accept UN type approvals to the preceding series of amendments that were first issued on or after [1 September 2028].
12.12. Until [1 September 2030], Contracting Parties applying this Regulation shall accept type approvals to the preceding series of amendments, first issued before [1 September 2028].
12.13. As from [1 September 2030], Contracting Parties applying this Regulation shall not be obliged to accept type approvals issued to the preceding series of amendments to this Regulation.,
12.14. Notwithstanding paragraph 12.13., Contracting Parties applying this Regulation shall continue to accept type approvals issued according to the 03 or 04 series of amendments to this Regulation, applying the provisions in paragraph 6.15.1. (a) of the 03 or 04 series of amendments to this Regulation, first issued before [1 September 2028].
12.15. Notwithstanding paragraph 12.13., Contracting Parties applying this Regulation shall continue to accept type approvals issued according to the preceding series of amendments to this Regulation, for the vehicles/vehicle systems which are not affected by the changes introduced by the 05 series of amendments.
12.16. Notwithstanding the transitional provisions above, Contracting Parties who start to apply this Regulation after the date of entry into force of the most recent series of amendments are not obliged to accept type approvals which were granted in accordance with any of the preceding series of amendments to this Regulation / are only obliged to accept type approval granted in accordance with the 05 series of amendments.“
Renumber )former) paragraphs 12.10. to 12.11. as paragraphs 12.17 and 12.18.
Need to amend 03 and 04 series as supplement

## Slide 17
Timelines
By 27 March: Immediate inputs for current draft to Secretary
By the end of March: Secretary will distributed updated (cleaned) documents.
By end of April: all to review and provide feedback
By 15 May: Consolidate and update the documents for submission to GRSP
27 – 31 May: GRSP presentation of the proposals
By 9 Sep: Submit formal WD to GRSP reflecting the feedbacks made after May GRSP
2-6 Dec: GRSP for adoption