## Slide 1: WLTP Open Issue Phase 1B
Issue: Amendment of OIL#42 -
Willans factors for petrol (E10) & diesel (B7)
.
ACEA Informal Document 12.09.2014
WLTP-08-06-rev1e

## Slide 2
Background:
At WLTP-IWG meeting #7 the request came up to complete the list of Willans factors in Annex 6, Appendix 2.
Proposal:
The proposal deals with the determination of the missing Willans factors for E10 & B7 by interpolation of the heat values.
Rationale:
Since the energy content of a fuel is given by the net heat value and the Willans factor is an energy-dependent fuel characteristic, Willans factors are indirectly proportional to the heat value of the corresponding fuels. Therefore, fuel-dependent Willans-factors can be calculated by interpolating the respective heat values of the fuels.

## Slide 3
Approach: Derivation from fuel heat values
Fuel | Petrol |  |  |  |  |  |  | Diesel |  |  |  | 
Content Ethanol / Biodiesel [%] | E0 | E5 | E10 | E15 | E22 | E85 | E100 | B0 | B5 | B7 | B20 | B100
Heat value [kWh/l] | 8.92 | 8.78 | 8.64 | 8.50 | 8.30 | 6.41 | 5.95 | 9.85 | 9.80 | 9.79 | 9.67 | 8.90
Source: VW

## Slide 4
Approach: Derivation from fuel heat values
Willans Factor E10:
= 1/ (0.3995 x 8.64 – 0.0099)
= 0.289 l/kWh
Gasoline - pressure-charged
Gasoline - naturally-aspirated
Willans Factor E10:
= 1/ (0.4247 x 8.64 – 0.003)
= 0.272 l/kWh

## Slide 5
Approach: Derivation from fuel heat values
Since the Willans Factor for B0 and B5 are equal, and the difference in heat value from B5 to B7 is smaller than from B0 to B5, it is proposed to use the same factor for all three types of fuel.

## Slide 6
Generic formulae for Willans factors
1) Gasoline naturally-aspirated:
Willans Factor = 1/ (0.4247 x heat value – 0.003)
2) Gasoline pressure-charged:
Willans Factor = 1/ (0.3995 x heat value – 0.0099)
3) Diesel naturally-aspirated:
Willans Factor = 0.220 l/kWh
4) Diesel pressure-charged:
Willans Factor = 0.220 l/kWh

## Slide 7
Draft
 |  |  | Naturally aspirated | Pressure-charged
Positive ignition | Petrol (E0) | l/kWh | 0.264 | 0.280
 |  | gCO2/kWh | 630 | 668
 | Petrol (E5) | l/kWh | 0.268 | 0.284
 |  | gCO2/kWh | 628 | 666
 | Petrol (E10) | l/kWh | 0.272 | 0.289
 |  | gCO2/kWh | 625 | 664
 | CNG (G20) | m³/kWh | 0.259 | 0.275
 |  | gCO2/kWh | 465 | 493
 | LPG | l/kWh | 0.342 | 0.363
 |  | gCO2/kWh | 557 | 591
 | E85 | l/kWh | 0.367 | 0.389
 |  | gCO2/kWh | 608 | 645
Compression ignition | Diesel (B0) | l/kWh | 0.220 | 0.220
 |  | gCO2/kWh | 581 | 581
 | Diesel (B5) | l/kWh | 0.220 | 0.220
 |  | gCO2/kWh | 581 | 581
 | Diesel (B7) | l/kWh | 0.220 | 0.220
 |  | gCO2/kWh | 581 | 581
Table A6.App2/2
Willans factors

## Slide 8
Draft
Table A6.App2/2
Willans factors (MJ)

## Slide 9
Backup - Willans factors in g CO2/kWh
(4) Willans_factor [g_CO2/kWh] = Willans_factor [L/kWh] * g_CO2/L_fuel
(3) g_CO2/L_fuel = g_CO2/g_fuel * ρ_fuel
(2) g_CO2/g_fuel = molar weight_CO2 / molar weight_fuel
(1) molar weight_fuel = X * molar weight C + Y * molar weight H + Z * molar weight O
Fuel: CxHyOz
Example E10: C1H1.93O0.033
(1) molar weight_fuel = (1 * 12.011 + 1.93 * 1.008 + 0.033 * 15.999) g/mol = 14.48 g/mol
(2) g_CO2/g_fuel = 44.01/ 14.48 g/mol = 3.039 g CO2/g_fuel
(3) g_CO2/L_fuel = 3.039 g CO2/g_fuel * 756 g/L = 2297 g CO2/L_fuel
(4) Willans_factor [g_CO2/kWh] = 0.272 [L/kWh] * 2297 g CO2/L_fuel = 625 g_CO2/kWh