## Slide 1: WLTP Open Issue Phase 1B
Issue: Fuel Consumption interpolation method
.
ACEA Informal Document 09.09.2014
WLTP-08-08e

## Slide 2
Background:
Currently, there is only an interpolation method for CO2 in the GTR. Individual FC values are requested by several contracting parties.
Proposal:
Interpolation of the worst and best case FC values.
Rationale:
The calculation of FC values is based on the carbon balance. The influence of HC and CO is rather low. Therefore, when interpolating the best case and the worst case FC values, the possible error for the determination of intermediate values is little.

## Slide 3
NEDC test series
Energy best case
Energy worst case
Worst case THC ≠ worst case CO ≠ worst case Energy
Example (NEDC): Light duty vehicle, Automatic gearbox, curb mass 4250 - 4750 lbs
Measured at different energy levels

## Slide 4
NEDC test series with Interpolation Points
Energy best case
Energy worst case
Worst case THC ≠ worst case CO ≠ worst case Energy
Example (NEDC): Light duty vehicle, Automatic gearbox, curb mass 4250 - 4750 lbs
Measured at different energy levels

## Slide 5
Influence of HC and CO on Fuel Consumption
Interpolation between best an worst case shows a very good correlation
With CO2 = 0
best case
worst case

## Slide 6
Influence of HC and CO on Fuel Consumption
Maximum influence of interpolation due to HC and CO contribution is lower than 0.06 % of fuel consumption value in this example (~ 8 l/100 km)
FC ~ 8 l/100 km
Difference between measured and interpolated values
1. liters per 100 km
2. percentage

## Slide 7
Proposal for gtr 15
All abbreviations according to Annex 7