## Slide 1: WLTP Vehicle range and energy consumption
EVE 12
28 October 2014

## Slide 2
Test cycle, test procedure and test conditions are in principle the same for conventional vehicles and electrified vehicles
Areas where there is differences is described in annex 8 of the GTR
  Charge depleting test (OVC-HEV and PEV)
  Preconditioning (OVC-HEV)
  REESS conditioning

## Slide 3
GTR No 15
  Phase 1 includes test cycle and test procedure for type 1 test, normal ambient conditions
  Proposal for phase 2 includes test procedure for low ambient temperature, high altitude, durability and in-service conformity
    Consider for EV, durability for battery and electric motor

## Slide 4
Electric vehicles considered in the GTR
  NOVC-HEV
  OVC-HEV
  PEV
  FCV

## Slide 5
For electrified vehicles test procedure consist of two tests
  Charge sustaining
  Charge depleteting
Test cycle WLTC and WLTCcity

## Slide 6: Charge depleting CD

## Slide 7: Charge sustaining CS

## Slide 8: Charge depleting PEV

## Slide 9
OVC-HEV
  CD and CS test
PEV
  CD test
NOVC-HEV
  CS test
FCV
  Procedure under development in phase 1b

## Slide 10
Test conditions same as for conventional vehicles
  Ambient temperature
  Soak
  Test equipment

## Slide 11
Values derived from the tests
  Emission compound (OVC-HEV and NOVC-HEV)
  CO2 and fuel consumption (OVC-HEV and NOVC-HEV)
  Electric energy consumption (OVC-HEV and PEV)
  Electric range (OVC-HEV and PEV)
    All Electric Range
    Charge Depleting Range

## Slide 12
Amendments for EV in phase 1b
  Phase specific calculation for CO2 and fuel consumption
  Shortened test procedure for PEV
  Combined approach for EV
  Test procedure for FCV