## Slide 1: EV Safety GTR Task Force Group #2 – Low Electric Energy
#6 EVS GTR Status Briefing
November, 2014
EVS-06-18e

## Slide 2: TF #2 Activities
TF leader assembled all relevant supporting technical material for TF review and comment (Primarily the 2013 revision of the US DOE Electrical Safety Handbook and details from the supporting IEEE technical paper).
Material was sent out to the TF for review and comment.
To date, there have not been any formal comments received regarding this information.
One member of the TF has indicated that it is still evaluating the information and may provide comments in the future.
Once these comments are received the TF will schedule a meeting to discuss them and determine next steps.
At the October 2014 Task Force #2 meeting, OICA proposed a modification to the low electrical energy calculation formulas to modify the integration limits for the total energy calculation from the post impact voltage of the capacitor to zero.
Task Force #2 approved the proposed OICA modification of the low electrical energy calculation and brings this modification to the EVS GTR for consideration.

## Slide 3: Proposed Modification to EVS GTR Text
6.1.5.2.3. Assessment procedure for low electrical energy
  Prior to the impact a switch S1 and a known discharge resistor Re is connected in parallel to the relevant capacitance (ref. Figure 8).
  Not earlier than 5 seconds and not later than 60 seconds after the impact the switch S1 shall be closed while the voltage Vb and the current Ie are measured and recorded. The product of the voltage Vb and the current Ie shall be integrated over the period of time, starting from the moment when the switch S1 is closed (tc) until the voltage Vb falls below the high voltage threshold of 60 V DC (th), to zero. The resulting integration equals the total energy (TE) in joules.
    When Vb is measured at a point in time between 5 seconds and 60 seconds after the impact and the capacitance of the X-capacitors (Cx) is specified by the manufacturer, total energy (TE) shall be calculated according to the following formula:
  TE = 0.5 x Cx x(Vb2 – 3 600)
  When V1 and V2 (see Figure 8) are measured at a point in time between 5 seconds and 60 seconds after the impact and the capacitances of the Y-capacitors (Cy1, Cy2) are specified by the manufacturer, total energy (TEy1, TEy2) shall be calculated according to the following formulas:
  TEy1 = 0.5 x Cy1 x (V12 -3 600)
    TEy2 = 0.5 x Cy2 x (V22- 3 600)
  This procedure is not applicable if the test is performed under the condition where the electric power train is not energized.