## Slide 1
Task Force 3: Electrolyte leakage
Last update- 11/11/2014
EVS-06-19e

## Slide 2
Organization of Task force
Issues raised during China EVS meeting
Present requirement and purpose
Approach of Task Force
Definitions
Aqueous Electrolytes
  Issues
  Proposal
Non-Aqueous Electrolytes
  Issues
  Proposal
Conclusion and future work
Content:

## Slide 3
Scope:
  Issues related to electrolyte leakage (except venting)
Objective :
  Reply all the queries on this issue , provide justification for the requirements in GTR draft and if required propose test procedure.
Organization of Task force: Scope & Objective

## Slide 4
China (CATARC)
European Union (JRC)
USA (NHTSA)
South Korea ( KATRI)
France (UTAC)
OICA (Alliance, Daimler, JLR, PSA, GM, Toyota, Nissan, JAMA, VW, Scania, SK Continental , Volvo, Renault)
Organization of Task force: Members
Contributions
Research data /analysis: JRC
Comments: JRC, NHTSA, KATRI, CATARC , OICA

## Slide 5
End of January 2014: Initial comments on the issue by exchange of emails
28th February 2014: 1st meeting with co-sponsors on progress of task force
11th March 2014: 1st audio meeting of TF to discuss the initial proposals
21st March 2014: 1st face to face meeting in Paris
11th April 2014: 2nd audio meeting of TF to finalize the task force conclusion on aqueous electrolyte REESS
25th April 2014: 2nd meeting with co-sponsors on progress of task force
8th of May 2014: Comments on the ‘status report’ by exchange of emails
12th May 2014: 2nd face to face meeting in Washington (validation of conclusion)
13th May 2014: Presentation of task force progress report in the 5th GTR-EVS meeting
15th October 2014: 3rd face to face meeting in Brussels
18th November 2014: Presentation of task force progress report in the 6th GTR-EVS meeting
Organization of Task force: Work plan

## Slide 6
Electrolyte Leakage: Issues raised during last EVS meeting
Three category of questions
Leakage detection:
  How to distinguish leakage?
  What is an appropriate coating?
Leakage (spillage) amount measurement :
  How is leakage measured?
  How to quantify electrolyte leakage amount (7 % volume or 5 litters)?
  How to differentiate ‘electrolyte leakage’ from ‘coolant’?
  How to measure the electrolyte vapor (in case required to)?
  Electrolyte leakage currently defined as liquid leakage. This poses possible difficulty for batteries using volatile electrolytes (e.g. Li-ion). How is liquid electrolyte leakage measured and distinguished from electrolyte lost due to vapors or evaporation of spilled electrolyte?
Venting gas:
  How to differentiate smoke from combustion with electrolyte vapors at venting, for example in the thermal cycling test?

## Slide 7
Acceptance criteria in present GTR draft :
Test item | Leakage | Rupture | Fire | Explosion | Isolation Resistance | Retention
Vibration | √ | √ | √ | √ | √ | -
Thermal choc | √ | √ | √ | √ | √ | -
Fire resistance | - | - | - | √ | - | -
External short circuit | √ | √ | √ | √ | √ | -
Over discharge | √ | √ | √ | √ | √ | -
Over charge | √ | √ | √ | √ | √ | -
Mechanical shock | √ | √ | √ | √ | √ | √
Mechanical integrity | √ | √ | √ | √ | √ | √
Post-crash Vehicle | √ | √ | √ | √ | √ | √
The fire test does not require leakage criteria and hence out of scope of this TF
The ‘flammability aspect’ and the ‘electric choc aspect’ of electrolyte is already covered in the GTR draft
Hence the objective of the task force is to look in to the chemical risk (corrosive & toxic nature of electrolytes)

## Slide 8
Test items | Purpose of the test | Present Requirements
Vibration | -The user is supposed to continue to use the vehicle after the event. -In this case, stringent requirements should be applied | -No evidence of electrolyte leakage
Thermal shock and cycling |  | 
External short circuit protection | -The proposed test procedure is to confirm the operation of protective function. -In this case, stringent requirements should be applied | 
Overcharge protection |  | 
Over-discharge protection |  | 
Over-temperature protection |  | 
Mechanical integrity | -Same as vehicle post-crash | -No evidence of electrolyte leakage
Mechanical shock |  | 
REESS requirements for whole vehicle post-crash | -The user is supposed to stop using the vehicle until certain repair/maintenance is conducted once subject to the event, presuming the battery would not be re-used for any other purpose than vehicle propulsion. -In this case, the requirement relevant to the accident situation, in order to avoid additional risk to the occupants and the surrounding people, should be applied. | -Until 30 min after the impact, there shall be no electrolyte leakage from the REESS into the passenger compartment -no more than 7 % by volume of the REESS electrolyte capacity spilled from the REESS to the outside of the passenger compartment.
Electrolyte Leakage: Present requirement & Purpose
In-use
Post-crash

## Slide 9
  Prepare a list of potential risks associated with existing electrolytes => discussion completed
  TF members agreed to distinguish the REESS in to two categories based on the types of electrolytes
    Aqueous electrolyte
    Non-aqueous electrolyte
  TF member agreed to distinguish in-use and post-crash requirements
  The discussions will be in two steps:
    first complete the discussion on REESS based on aqueous electrolytes (by end March) => discussion completed and final text proposed
    and then discuss the particularities of REESS with non-aqueous electrolytes . => still under discussion
Approach :

## Slide 10
  Aqueous electrolyte: An aqueous electrolyte is an electrolyte based on water solvent for the compounds (e.g. acids, bases) providing conducting ions after its dissociation.
  Non-aqueous electrolyte: A non-aqueous electrolyte is an electrolyte not based on water as the solvent
Definitions :
NEW
Notes: These definitions are provided by Komatsuki-san on 04/06/2014 and modification suggested by Annika

## Slide 11
 | Issue | Potential Risk | Proposed Solution
1 | Leakage in liquid form | Irritant, Corrosive Large amounts, order of liters, expected | No evidence of electrolyte leakage Well understood and documented, e.g. FMVSS 305, UNECE R100.02, UNECE R94/95/12, IEEE 1578 Visual inspection as described in the current GTR text may be used for electrolyte leakage detection
2 | Vapor from leakage | No significant amount expected | No action needed (low volatility of water)
3 | Volatile gas | Expected in normal operation Flammable gas (e.g.H2) | Well understood and documented (e.g. UNECER100.02, EN62485-3, SAEJ1718) Venting (proposal from Japan)
4 | Leakage in liquid form | Irritant, Corrosive Large amounts, order of liters, expected | Until 30 min after the impact, there shall be no electrolyte leakage from the REESS into the passenger compartment No more than 7 % by volume of the REESS electrolyte capacity spilled from the REESS to the outside of the passenger compartment. Visual inspection may be used for electrolyte leakage detection
5 | Vapor from leakage | No significant amount expected | No action needed (low volatility of water)
Aqueous Electrolytes :Issues
In-use
Post-crash
TF3 experts agrees that proposed solutions are adequate for issues related to Aqueous Electrolytes
Notes: Justification (leakage amount): the 7% criteria from present R100.02 is more stringent then the 5 littres

## Slide 12
Add the following clarification on the leakage detection (REESS based tests): [Based on FMVSS 305]
Good engineering judgment should be used to fulfil the requirement of an appropriate coating. One of the possible solutions might be an absorbent paper which surrounds the REESS casing. In this case, if an electrolyte leakage occurs, the absorbent paper would get stains and wetted.
Add the following clarification on leakage measurement (post crash): [Based on FMVSS 305]
The spilled amount of electrolyte can be measured by usual techniques of determination of liquid volumes after collecting the spillage. For containers containing both Stoddard (colored coolant) and electrolyte, the fluids shall be allowed to separate by specific gravity then measured.
Aqueous Electrolytes : Proposal

## Slide 13
 | Issue | Potential Risk | Proposed Solution
1 | Leakage in liquid form | Flammable, Toxic, Corrosive Small amounts, order of millilitres, expected | No evidence of electrolyte leakage
2 | Vapor from leakage | Toxic / flammable gas | No vapors are expected as no electrolyte leakage is allowed [under discussion ]
3 | Volatile gas | Not expected in normal operation | Venting (proposal from Japan)
4 | Leakage in liquid form | Flammable, Toxic, Corrosive Small amounts, order of millilitres, expected | For REESS based on non-aqueous electrolytes, there should not be any leakage ‘outside vehicle’ or ‘inside passenger’ compartment Visual inspection may be used for electrolyte leakage detection
5 | Vapor from leakage | Toxic / flammable gas | Under discussion
Non-Aqueous Electrolytes : Issues
In-use
Post-crash
NEW1
Justification:
  1. JRC analysis shows that 7% criteria for li-ion battery may lead to dangourouse situation. Spilling ca. 1 L of dimethyl carbonate results in a PAC-3 concentration level in a volume of vehicle +3 m-thick layer around it.

## Slide 14
Conclusion and future work
Contribution of TF3 so far:
  New definitions : types of electrolytes (aqueous and non-aqueous)
  Clarification on liquid leakage detection for aqueous electrolyte batteries
  New requirement for non-aqueous electrolytes on liquid leakage: no liquid leakage outside the vehicle (instead of 7%)
Future work :
  Discussions on risk associated with non-aqueous electrolytes => JRC is planning to do some experiment on single cell. Initial results expected after the 6th EVS meeting
  Propose final text for agreed topics
  Required time: April 2015 (tentative)

## Slide 15
Annex

## Slide 16
Electrolyte Leakage: Additional issues raised during TF3 meetings
Topic | Issue | Comments
Observation period: | JRC proposed to increase the observation period from 30 minutes to 60 minutes | This issue is not specific to this task force and need feedback from other experts (TF4 for example )
Roll-over test | Korean proposal: The electrolyte leakage requirement shall be met in case of rollover after vehicle impact tests (same as that of FMVSS 305) | This comments is related to vehicle crash test procedure and this is not part of this GTR-EVS
‘No fire’ requirement | JRC proposed to use ignition source to check potential flammability of the emitted gas from leaked electrolyte | This issue is not specific to this task force and is more related to test procedure
Spillage/leakage | China and JRC proposed to use only one definition | Only leakage will be used