## Slide 1
TF8: Research IF EVS-GTR Battery System Test Project and Test Methods’ Adaption to heavy /commercial Vehicles

## Slide 2
The task of TF8 ： Research if EVS-GTR Battery System Test Project and Test Methods’ Adaption to heavy /commercial Vehicles
October 17, 2014 ，TF8 had the first meeting at Brussels ，all members gave their views for if EVS-GTR Battery System Test Project and Test Methods’ Adaption to heavy/Commercial Vehicles and conclusions as below.
1: Heavy/Commercial Vehicles includes of buses, coacher, trucks, special vehicles and so on. There are big differences layout and the RESS numbers ,size or the location on the vehicles between the heavy vehicles and the passenger vehicles.
2:As an important vehicles standard related to safety performance and RESS, It is possibility for the EVS-GTR to cover the heavy/commercial vehicles or there is another possibility to have a separate GTR for heavy/commercial vehicles.
3: Because of the layout of the RESS difference between the heavy vehicles and the passenger vehicles ,and there is no crash regulations for heavy vehicles ，so the crash requirements can be exempted for heavy /commercial vehicles.

## Slide 3
    4: we categorize the proposed tests and requirements into 3 categories：
    1) Directly applicable to heavy vehicles
    2) Relevant, but need modification/adaptation in order to be applicable on heavy vehicles
    3) Not applicable – exemption required for heavy vehicles

## Slide 4
 | Verified safety performance | Applicability on heavy vehicles | Comments about accessment of applicability
TF1 | Water immersion/water resistance | 1) / 2) | Base on the final requirements
TF2 | Low energy | 1) /3) | Not applicable if it’s based on crash requirements Applicable if it’s based on electric safety
TF3 | Leakage requirements | 1) | 
TF4 | Vibration | 1) | 
 | Thermal shock and cycling | 1) | 
 | Mechanical shock | 3) | First, the layout of heavy vehicles and passenger cars are different; Second, there is no crash regulations for heavy vehicles . Therefore, these two requirements can be exempted for heavy vehicles
 | Mechanical integrity | 3) | 
 | External short circuit protection | 1) | For the principle of voltage platform , electrical system and RESS, there are no difference between heavy commercial vehicles and passenger cars, so these are directly applicable to heavy vehicles
 | Overcharge protection | 1) | 
 | Over discharge protection | 1) | 
 | Over temperature protection | 1) | 
 | Thermal propagation | 1) | 
TF5 | Cell/Module safety | 1) | But If one of the test methods among "vehicle" or "REESS" or "sub system equivalent to REESS" can prove the safety, other cell/module tests are not necessary anymore
TF6 | SOC during test: EV/PHEV and HEV | 1) | 
TF7 | Fire resistance | 1) | 
 | Venting | 1) | 
The view of China

## Slide 5
The view of Japan
Verified safety performance | Applicability on heavy vehicles | Comments about assessment of applicability
Vibration | 1) | 
Thermal shock and cycling | 1) | 
Mechanical shock | 1) | 
Mechanical integrity | 3) | Passenger cars approach can't directly apply to HD vehicles due to the fact that there is no vehicle crash regulations for HD vehicles like R12/R94/R95.
Fire resistance | 1) | 
External short circuit protection | 1) | 
Overcharge protection | 1) | 
Overdischarge protection | 1) | 
Overtemperature protection | 1) | 
Water immersion/water resistance | 2) | HD vehicles needs the exemption for the vehicle equipped with an isolation resistance monitoring system from the view that many kinds of rear body variants might affect the water-crossing test result. And "HV power-off requirement" when the isolation resistance is failed shall not be adopted.
Low energy | 1) | 
Thermal propagation | 1) | 
Cell/Module safety | 3) | If one of the test methods among "vehicle" or "REESS" or "sub system equivalent to REESS" can prove the safety, other cell/module tests are not necessary anymore from the certification view.
SOC during test: EV/PHEV and HEV | 1) | 
Leakage requirements | 1) | 
Venting | 1) | 

## Slide 6
The views of other manufactures (European) :
Verified safety performance | Applicability on heavy vehicles | Comments about assessment of applicability
Vibration | 2) | 
Thermal shock and cycling | 1) | 
Mechanical shock | 1) | 
Mechanical integrity | 3) | .
Fire resistance | 1) | 
External short circuit protection | 1) | 
Overcharge protection | 1) | 
Overdischarge protection | 1) | 
Overtemperature protection | 1) | 
Water immersion/water resistance | 2) | 
Low energy | 1) | 
Thermal propagation | 1) | 
Cell/Module safety | 3) | 
SOC during test: EV/PHEV and HEV | 1) | 
Leakage requirements | 1) | 
Venting | 1) | 

## Slide 7
1 :Water immersion/water resistance:
——Applicable if the requirements are for vehicles ；
——Not applicable if the requirements are for base on components.
2 :Low energy:
——Not applicable if base on crash requirements
——Applicable if base on electric safety
3 :Leakage requirements: Applicable
4:Vibration: Applicable ,but may be the heavy/Commercial should meet special requirements because of the Vehicle type.
5:Mechanical shock and cycling/Mechanical integrity:
view of china: the two requirements both crash requirements, so can be exempted for heavy vehicles
view of Japan/OICA/ Scania:Thermal shock and cycling is applicable,
Mechanical integrity can be exempted for heavy vehicles.
conclusions

## Slide 8
6: External short circuit protection/ Over discharge /Over charge protection/ Over temperature protection / Thermal propagation : Applicable
7: Cell/Module safety : If one of the test methods among "vehicle" or "REESS" or "sub system equivalent to REESS" can prove the safety, other cell/module tests are not necessary anymore
8: SOC : Applicable
9: Fire resistance: Applicable
10:Venting: Applicable
conclusions

## Slide 9
suggestion:
“propose a separate annex for the EVS-GTR specifying the application of the regulation on commercial/heavy vehicle. The tests that are directly applicable can be referred to the main document. When modifications are needed, these should be specified and motivated in the annex. The annex should also motivate exemptions from any test requirements.
If the proposed approach is taken ,then the task of TF8 is to draft this annex.”