## Slide 1: AVC-09-12 UK input to support discussion
9th TF-AVC meeting, 01 October 2024

## Slide 2: Speed limitation of category X / Y
  6 km/h (fast walking pace) is an appropriate speed to set as the threshold
  Below this speed various existing approval requirements related to manual driving can be considered unnecessary
  Operation of ADS vehicles at this speed is likely to be under exceptional circumstances, and ensuring sufficient control, field of view, etc can be adequately managed by in-use regulations. This is already the case in many markets for e.g. non-road mobile machinery, pedestrian-controlled vehicles, certain agricultural vehicles, etc.
  There is already a precedent for including speed thresholds in certain L-categories.
  Protection against tampering could be considered, but this would be for separate regulation.
  Restricting these categories to ‘no manual driving’ would be impractical, as we expect most AVs to need a limited manual mode for the purposes of breakdown recovery etc.

## Slide 3: Carriage of occupants
  ‘Designed not to carry occupants’ is sufficient text for the definition of Category Y in RE3. Compare with:
    Category N: “used for the carriage of goods”
    Category M2/3, Class III: “constructed exclusively for the carriage of seated passengers”
  If any design constraints are deemed necessary to regulate category Y, these can be placed in national/regional approval frameworks as they are for category N.
  We do not see a conflict between ‘designed not to carry occupants’ and ‘can be manually driven up to 6 km/h’ for category Y.
    Such vehicles could be manually driven from off-board
    Like the carriage of persons in the load area of N-category vehicles or in O-category vehicles, enforcement of carriage of occupants in category Y is for national in-use regulation

## Slide 4: Dual Mode
  We have not seen a strong need for a definition of ‘dual mode’, since for a vehicle with both a manual mode and an ADS mode simply needs to meet all requirements in a given regulation.
  However, we can see how a definition may make the drafting of some provisions easier.
  Whether transition demands are issued or not is related to the ADS Feature, not to the vehicle. A vehicle may have multiple features.
    A Dual Mode vehicle as defined in AVC-09-02 could also have an ADS feature which does issue transition demands.
    Therefore it cannot be determined that a ‘D’ category vehicle needs a driver or fallback user at any given time.
  For this reason we do not see the need for a (sub)category ‘D’, but would support a definition if it helps with drafting regulatory amendments.

## Slide 5: L-category
  Screening task forces have not yet begun considering amendments for L-category regulations.
  We do not see the harm in including L-category now, but can understand the concerns of IMMA in document AVC-09-11.
  We therefore propose not to include L-category in the definitions of X and Y at this stage.
  Once the definitions of X and Y have been adopted for M/N category, it will be known exactly what these definitions are and so screening task forces can begin they work on L-category regulations with this in mind.
  It will be a simple task to further amend RE3 at the point an L-category regulation needs to refer to these categories.