## Slide 1
Analysis of Normalization Report
With Focus On Rotational Masses
Geneva, 14th of January 2015
Christoph Lueginger
BMW
WLTP-09-25e

## Slide 2
Analysis of Normalization Report
Introduction to correction functions
  Improving measurement quality is welcomed in general.
  WLTP should focus on being representative and repeatable by avoiding unnecessary burden at the same time.
  Correction functions are welcomed, as long as they fulfill at least the following criteria:
      tolerance bigger than measurement tolerance
      significant influence
      measureable
      physical meaning of correction function
      save operation of the vehicle
      improves result
      validated
page 2

## Slide 3: Rotational masses, analysis
Fact box check for correction function.
Measurement tolerance of weight in Annex 4 is +/- 10 kg, in general the error is smaller than that. Additionally the error is divided in half on a 1-axle dyno.
3%-rule is more on the worst case side.
Average error: 3%-rule: -0.8..+3.4 kg (depending on vehicle weight) 60%-rule: -2.3 kg
Maximum error is bigger for the 60%-rule (-11.1 kg) than for the 3%-rule (+9 kg).
See examples on the following slides.
60%-rule increases effort on dyno in an unnecessary way without improving the result.
page 3
TNO proposal for rotational masses: 60% of wheel-weight.
property of correction | fulfilled?
tolerance > measurement tolerance | 
significant influence | 
measureable | 
physical meaning of correction func. | 
improves result | 

## Slide 4: Rotational masses, examples (1)
Examples are taken from current BMW vehicles.
Tires are typical ones (high customer take rate), apart from "basic-tire".
10 kg is the weighting tolerance in the GTR.
page 4

## Slide 5: Rotational masses, examples (2)
Examples are taken from current BMW vehicles.
Tires are typical ones (high customer take rate), apart from "basic-tire".
10 kg is the weighting tolerance in the GTR.
page 5

## Slide 6: Overview of proposed corrections
None of the corrections is at a level to be implemented, many of them are only increasing effort without improving the result, sometimes they are even wrong.
Note: On request a more detailed analysis by ACEA available for most of the issues.
Proposal EU Commission / TNO report |  | ACEA
Correction type (reference in the report) | Prio | comment
2.2 Deviation from target speed (including battery SOC correction) | A | SOC biggest influence and already included, target speed small part. No solution for electrified vehicles. No solution for gearshift event deviation. No detailed proposal available.
2.3 Quality of reference fuel | B | Impact not clear.
2.4 Inlet air temperature and humidity | B | No clear proposal.
2.6 Temperature from preconditioning and soak | D | Already dropped due to small influence.
2.7 Inaccuracy of road load setting on the chassis dyno | B | No data basis, that shows the need. Correction in the order of measurement tolerance, no improvement. Can be solved by improving the GTR text.
2.9 Deviation from designated gear shift points | C | No proposal available. Small effect anyway.
4.1 Vehicle preparation for coast down, toe-in prescription | A | Not a normalization issue, text proposal in discussion.
4.1 Vehicle conditioning for coast down: tyre pressure monitoring/control | B or C | Technical wrong analysis, poor data, proposal may lead to dangerous requirements (underfilling of tyre!), double corrects with already implemented temperature correction, etc.
5.1 Ambient weather conditions at coast down: temperature, air pressure, water content of the air | B or C | No proposal available.
5.2 Wind corrections at coast down | B or C | No proposal available.
5.3 Road condition of coast down test track (surface roughness, gradient, undulation) | C | Even science has no conclusion or solution. Proposed correction obviously wrong, several studies and measurements show no
6.2 Rotational inertia correction (when evaluating the coast down test) | A | Result does not improve compared to current regulation, but workload and complexity increases in an unnecessary way.
page 6

## Slide 7: Conclusion
Proposal:
Do not include the 60%-rule.
Add as an option of the manufacturer the possibility to use 3% of test mass instead of 3% of (Miro+25kg), which adds another ~ 6 kg but simplifies dyno operation.
Justification:
60%-rule increases effort without improving the result.
Using 3% of TM is even more on the worst case side and reduces potential errors in dyno handling.
None of the corrections is at a level to be implemented (neither on GTR level nor on European level), many of them are only increasing effort without improving the result, sometimes they are even wrong from a technical perspective.
No validation and no concrete proposals available. Therefore no final assessment possible.
page 7

## Slide 8
European Automobile Manufacturers Association
www.acea.be
Thank you!
Notes: Thank you very much,
We are now be happy to take your questions