## Slide 1: GTR Corrections, Open Points, Expert Proposals and Confirmations in GTR 15
WLTP-09-26e

## Slide 2: Comments: 1. These PowerPoint slides summarise all GTR corrections, open points, expert proposals and confirmations in the GTR. 2. The slides incorporate comments from experts received since 10.07.2014 including those related to the 31.08.2014 and 31.10.2014 deadlines, and new items since publication of the GTR on September 14, 2014.

## Slide 3: Some examples of items to be processed by the drafting sub-group

## Slide 4: II. Text of the global technical regulation, §5.6.1.
EXPERT PROPOSAL: 01.11.2014: From C. Lueginger and A. Feucht.
GTR Text:
Approval of additional text

## Slide 5: Definitions (mass)
3.2.5. "Mass in running order" means the mass of the vehicle, with its fuel tank(s) filled to at least 90 per cent of its or their capacity/capacities, including the mass of the driver and liquids, fitted with the standard equipment in accordance with the manufacturer’s specifications and, when they are fitted, the mass of the bodywork, the cabin, the coupling and the spare wheel(s) as well as the tools when they are fitted
Proposal from W. Coleman: "Mass in running order" means the mass of the vehicle, with its fuel tank(s) filled to at least 90 per cent of its or their capacity/capacities, including the mass of the driver and liquids, fitted with the standard equipment in accordance with the manufacturer’s specifications and, when they are fitted, the mass of the bodywork, the cabin, the coupling and the spare wheel(s) as well as the tools when they are fitted.
Reason: align with 692/2008
Deletion of text to align with existing legislation

## Slide 6: Definitions (mass)
TASK: Approval of proposed deletion in red.
Reason: To align with EU legislation the mass of optional equipment needs to be defined. Once this is done the reference to vehicle H becomes redundant and potentially confusing
3.2.7. "Maximum vehicle load" means in this GTR the difference between the technically permissible maximum laden mass and the sum of the mass in running order, 25 kg and the mass of the optional equipment of vehicle H.
Approval of deletion of technically relevant text (first example)

## Slide 7: Definitions
Current GTR Text:
3.3.1. "All-electric range" (AER) means in the case of an off-vehicle charging hybrid electric vehicle (OVC-HEV) the total distance travelled from the beginning of the charge-depleting test over a number of complete WLTCs to the point in time during the test when the combustion engine starts to consume fuel.
Proposal from W. Coleman:
3.3.1. "All-electric range" (AER) means in the case of an off-vehicle charging hybrid electric vehicle (OVC-HEV) the total distance travelled from the beginning of the charge-depleting test over a number of complete WLTCs to the point in time during the test when the combustion engine starts to consume fuel.
Approval of deletion of technical text (second example)

## Slide 8: Definitions (mass)
TASK: Approval of proposed text. Proposal from W. Coleman.
PROPOSAL:
3.2.a. "Mass of the optional equipment" means the mass of the equipment which may be fitted to the vehicle in addition to the standard equipment, in accordance with the manufacturer’s specifications.
Reason: Although this definition is only valid in the context of application for and granting of an approval, it is essential to operate the combined approach.
Approval of new text

## Slide 9: Definitions (see also next slide)
GTR Text:
3.8.1. "Periodically regenerating system" means an exhaust emissions control device (e.g. catalytic converter, particulate trap) that requires a periodical regeneration process in less than 4,000 km of normal vehicle operation. During cycles where regeneration occurs, emission standards can be exceeded. If a regeneration of an anti-pollution device occurs at least once during vehicle preparation cycle, it will be considered as a continuously regenerating system which does not require a special test procedure.
Proposal: deletion of the last 2 sentences “During cycles where regeneration occurs, emission standards can be exceeded. If a regeneration of an anti-pollution device occurs at least once during vehicle preparation cycle, it will be considered as a continuously regenerating system which does not require a special test procedure.” and integrate this in the technical annex without the reference to “continuously regenerating system which is not defined in light duty legislation.
Text yet to be processed (written, approved) by the appropriate experts

## Slide 10: Annex 4, Road load and dynamometer setting
EXPERT PROPOSAL: 01.11.2014: From C. Lueginger, A. Feucht and Daimler. Value in square brackets.
GTR Text: 3.1.(j)
Open technical point to be processed by experts

## Slide 11: Reference to Annex 6, Test procedure, §1.2.6.5. Use of the Transmission: proposal from drafting coordinator
Drafting coordinator proposal: 20.11.2014. Move paragraphs §1.2.6.5. up to and including §1.2.6.5.3.2. on the use of a manual and automatic transmission from Annex 6 to Annex 2.
GTR Text:
Move §1.2.6.5. to Annex 2??
Moving text to simplify and/or clarify the GTR

## Slide 12: Annex 7, Calculations, §3.2.3.2.2.5. & 3.2.3.2.2.6.
OPEN POINT: 13.01.2015: Could these calculations not be entered here? It would make for a connection between this paragraph and the next more logical.
Making the GTR more logical

## Slide 13: Annex 3, Fuels
TASK: Are ICE vehicles powered by hydrogen fuel to be taken into consideration in the GTR?
Open technical question

## Slide 14: Annex 8, Pure and HEVs, §1.6.
OPEN POINT. 02.09.2014: Question from I. Riemersma: GSIs (= technical gear shift instrument) are not included in the GTR but rather the shift points described in Annex 2 are to be used. This point to be discussed in the appropriate meeting.
GTR Text:
1.6. OVC-HEVs. NOVC-HEVs and PEVs with manual transmissions shall be driven according to the manufacturer’s instructions, as incorporated in the manufacturer's handbook of production vehicles and indicated by a technical gear shift instrument.
Open technical point

## Slide 15: Annex 4, Road load and dynamometer setting, paragraph 3.2.8.
EXPERT PROPOSAL: 30.10.2014. Equation changed to read that the absolute value of the quotient minus one shall be less than or equal to 1 per cent. Input from C. Lueginger and A. Feucht.
GTR Text:
Reworking equations to make more logical/simpler

## Slide 16: Annex 4, Road load and dynamometer setting
EXPERT PROPOSAL: 03.11.2014: proposed by Road Load task force (C. Lueginger, A. Feucht). The task force is not convinced that the paragraph is necessary.
GTR Text:
Possible deletion of a complete paragraph

## Slide 17: Annex 4, Road load and dynamometer setting (mass)
CURRENT GTR:
4.5.4.2. Test vehicle L
The correction factor for the test mass of test vehicle L shall be determined as follows:
(44)
where:
is a constant term, N;
is test mass of test vehicle L, kg;
is the actual test mass of the test vehicle L (the average mass , see paragraph 4.3.1.4.4. of this Annex), kg.
PROPOSAL:
4.5.4.2. Test vehicle L
The correction factor K1 for the test mass of test vehicle L shall be determined as follows:
where:
fo is a constant term, N;
TML is the target test mass of the test vehicle L, kg;
TML,actual is the actual test mass of test vehicle L (the average mass ; (see paragraph 4.3.1.4.4. of this Annex), kg.
TASK: Approval of proposed text in red.
STATUS AS OF 22.09.2014: Entered in the GTR requesting comments < 31.10.2014.
Consistency in usage of certain terms

## Slide 18: Annex 6, Appendix 2, Test procedure for electric power supply system monitoring (page 1 of 2)
STATUS AS OF 22.09.2014: Entered in the GTR requesting comments < 31.10.2014.
EXPERT PROPOSAL: 29.07.2014: Dr. Ligterink (TNO) and his colleague, Gerrit Kadijk, highlights inconsistencies within the GTR concerning units used in Annex 6, Appendix 2 (Test procedure for electric power supply system monitoring). The problem is whether (a) kW.h, joules or megajoules should be used in equations, and, (b), whether kW.h, joules or megajoiules should be used in the Willans factors, and (c) whether the equations are all correct. This applies also to Annex 7 (Calculations) and to Annex 8 (Evs).
Consistency in the use of units

## Slide 19: Various annexes (page 2 of 2)
GTR Text:
Should energy content of fuel be in joules, megajoules, Wh or kWh?
May the CO2 correction factor (g/km)/(Wh/km) be written as (g/Wh) (see Table A8/2 in Annex 8)? See also §3.1.1. in Annex 8, Appendix 2.
May the fuel consumption correction factor (l/100 km/(Wh/km) be written as l/100/Wh (see Table A8/2 in Annex 8)? See also §2.1.1. in Annex 8, Appendix 2.
Consistency in the use of MJ or other units

## Slide 20: Annex 8, Pure and HEVs, §2.3.3.
EXPERT PROPOSAL: 30.10.2014. Japan proposes replacing "shall" with "may"..
GTR Text:
Language item with possible repercussions

## Slide 21: Annex 8, Appendix 2, Pure and HEVs, §3.1.1., REESS charge balance correction
OPEN POINT: 30.10.2014: ACEA believes that this should be "is". Japan believes it should remain as "are" as separate emissions and fuel consumption correction factors shall be calculated for each phase of the WLTC and corrected to zero over each WLTC
GTR Text:
Language item with possible repercussions

## Slide 22: Additional slides as of 14.12.2014

## Slide 23: Annex 7, Calculations, §3.2.3.2.2.4.
GTR CORRECTION: 13.01.2015: This is essentially the same title as 3.2.3.2.2. (see below). Can both nevertheless remain?
Eliminating repetitions, in this case, of headings

## Slide 24: General comment
EXPERT PROPOSAL FROM A. FEUCHT
Regarding the renaming of “CO2-family” it is proposed to refer to an “energy interpolation family” or, in case of EVs where there is another parameter to interpolate, just “interpolation family”.
Proposal for new terminology

## Slide 25: End