| E/ECE/324/Add.6/Rev.6−E/ECE/TRANS/505/Add.6/Rev.6 |
| --- |
| Second draft for Regulation 7 to demonstrate the application of the HRD |  | 19 December 2014 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be fitted and/or be used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 6: Regulation No. 7

Revision 6

Incorporating all valid text up to:

Supplement 16 to 02 series of amendments: Date of entry into force: 19 August 2010

Supplement 17 to 02 series of amendments: Date of entry into force: 30 January 2011

Corrigendum 1 to Supplement 15 to 02 series of amendments: Date of entry into force: 09 March 2011

Supplement 18 to 02 series of amendments: Date of entry into force: 23 June 2011

Supplement 19 to 02 series of amendments: Date of entry into force: 28 October 2011

Supplement 20 to 02 series of amendments: Date of entry into force: 26 July 2012

Revision 6 - Amendment 1 Supplement 21 to the 02 series of amendments - Date of entry into force: 15 July 2013

Revision 6 - Amendment 2 Supplement 22 to the 02 series of amendments - Date of entry into force: 3 November 2013

Revision 6 - Amendment 3 Supplement 23 to the 02 series of amendments - Date of entry into force: 9 October 2014

Uniform provisions concerning the approval of front and rear position lamps, stop-lamps and end-outline marker lamps for motor vehicles (except motor cycles) and their trailers

_________

UNITED NATIONS

Regulation No. 7

Uniform provisions concerning the approval of front and rear position lamps, stop-lamps and end-outline marker lamps for motor vehicles (except motor cycles) and their trailers

Contents

Page

Scope			5

1.	Definitions		5

2.	Application for approval		5

3.	Markings		6

4.	Approval		6

5.	General specifications		7

6.	Intensity of light emitted		8

7.	Test procedure		10

8.	Colour of light emitted		10

9.	Modifications of a type of direction indicator for motor vehicles and their trailers and extension of approval			13

10.	Conformity of production		11

11.	Penalties for non-conformity of production		11

12.	Production definitively discontinued		11

13.	Names and addresses of Technical Services responsible for conducting approval tests, 
and of Type approval Authorities		12

14.	Transitional provisions		12

Annexes

1	Examples of arrangements of the approval marks		14

2	Communication		17

3	Photometric measurements		19

4	Front and rear position lamps, end-outline marker lamps and stop-lamps: minimum angles 
required for light distribution in space of these lamps		22

5	Minimum requirements for conformity of production control procedures		Fehler! Textmarke nicht definiert.

6		Minimum requirements for sampling by an inspector		Fehler! Textmarke nicht definiert.

Scope

This Regulation applies to:

Front and rear position lamps and stop lamps for vehicles of categories L, M, 		N, O and T; and,

End-outline marker lamps for vehicles of categories M, N, O and T.

1.	Definitions

For the purpose of this Regulation,

all the definitions including the definition of type given in Part II of Regulation 48  (Horizontal Reference Document (HRD)) shall apply to this Regulation;

2.	Application for approval

2.1. 		The applicant shall follow instructions as stated in paragraph 3. in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

2.2.	In addition to the requirements in paragraph 3. in Part II of Regulation 48  (Horizontal Reference Document (HRD)) shall also specify:

2.2.1.	The purpose or purposes for which the device submitted for approval is intended and whether it may also be used in an assembly of two lamps of the same kind/type;

2.2.2.	In the case of an end-outline marker lamp, whether it is intended to emit white or red light;

2.2.3.	In the case of a category S3 or S4 stop lamp, whether it is intended to be mounted outside or inside (behind the rear window) the vehicle;

2.2.4.	Whether the device produces steady luminous intensity (category R, R1, RM1, S1 or S3) or variable luminous intensity (category R2, RM2, S2 or S4);

2.3.	The drawings shall also showing

in what geometrical position(s) the device (and if applicable for category S3 or S4 lamps the rear window) may be mounted on the vehicle; the axis of observation to be taken is the axis of reference in the tests (horizontal angle H = 0°, vertical angle V = 0°); and the point to be taken as the centre of reference in the said tests;

2.4.	In addition to the brief technical description stating,

in the case of a category S3 or S4 stop lamp, which is intended to be mounted inside the vehicle, the technical description shall contain the specification of the optical properties (transmission, colour, inclination, etc.) of the rear window(s);

2.5.	In the case of a category S3 or S4 stop lamp which is intended to be mounted inside the vehicle, a sample plate or sample plates (in case of different possibilities) having the equivalent optical properties corresponding to those of the actual rear window(s).

3.		Markings

Devices submitted for approval:

The applicant shall follow instructions stated in paragraph 4. in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

In addition to the instructions in paragraph 4 in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

Lamps operating at voltages other than the nominal rated voltages of 6 V, 12 V or 24 V respectively, by the application of an electronic light source control gear or a variable intensity control being not part of the lamp, or having a secondary operating mode, must also bear a marking denoting the rated secondary design voltage;

4.		Approval

4.1.	General

The applicant shall follow instructions stated in paragraph 5. in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

4.2. 	In addition for the composition of the approval mark, the approval mark has also to include following additional symbol or symbols.

4.2.1.	On devices meeting the requirements of this Regulation in respect of the front position lamps, the letter "A";

4.2.2.	On devices meeting the requirements of this Regulation in respect of the rear position lamps, the letter "R" followed or not by the Figure "1" when the device produces steady luminous intensity and by the Figure "2" when the device produces variable luminous intensity.

4.2.3.	On devices meeting the requirements of this Regulation in respect of the front end-outline marker lamps, the letters "AM";

4.2.4.	On devices meeting the requirements of this Regulation in respect of the rear end-outline marker lamps, the letters "RM" followed by the Figure "1" when the device produces steady luminous intensity and by the Figure "2" when the device produces variable luminous intensity;

4.2.5.	On devices meeting the requirements of this Regulation in respect of the stop-lamps, the letter "S" followed by the figure:

"1"	When the device produces steady luminous intensity;

"2"	When the device produces variable luminous intensity;

"3"	When the device meets the specific requirements for category S3 stop-		lamps 	and produces steady luminous intensity;

"4"	When the device meets the specific requirements for category S4 stop-		lamps 	and produces variable luminous intensity;

4.2.6.	On devices comprising both a rear position lamp and a stop- lamp meeting the requirements of this Regulation in respect of such lamps, the letters "R" or "R1" or "R2" and "S1" or "S2" as the case may be, separated by a horizontal dash;

4.2.7	On front or rear position lamps of which the visibility angles are asymmetrical with regard to the reference axis in a horizontal direction, and on front or rear end-outline marker lamps, a horizontal arrow pointing towards the side on which the photometric specifications are met up to an angle of 80° H;

4.2.8.	On devices which may be used as part of an assembly of two lamps, the additional letter "D" to the right of the symbol mentioned in paragraphs 4.2.2.1. and 4.2.2.6;

4.2.9.	On devices with reduced light distribution in conformity to paragraph 2.3. in Annex 4 to this Regulation a vertical arrow starting from a horizontal segment and directed downwards.

4.2.10.	On interdependent lamps, which may be used as part of an interdependent lamp system, the additional letter "Y" to the right of the symbol mentioned in paragraph 4.2.2.1. to 4.2.2.6. shall be marked on each device.

5.		General specifications

5.1.	Each device supplied shall conform to the specifications set forth in in paragraph 6 and 7. in Part II of Regulation 48  (Horizontal Reference Document (HRD)) and paragraphs 6. and 8. below.

5.2.	In addition to paragraph 5.1. above:

5.2.1.	Lamps having been approved as front or rear position lamps, are deemed being also approved end-outline marker lamps.

5.2.2..	Front and rear position lamps which are grouped or combined or reciprocally incorporated may also be used as end-outline marker lamps.

5.2.3.	Position lamps, which are reciprocally incorporated with another function, using a common light source, and designed to operate permanently with an additional system to regulate the intensity of the light emitted, are permitted.

5.2.3.1.	However, in the case of rear position lamp reciprocally incorporated with a stop lamp, the device shall either:

(a)	Be a part of a multiple light source arrangement, or

(b)	Be intended for use in a vehicle equipped with a failure monitoring system for that function.

In either case, a note shall be made within the communication document.

5.3.	If the front position lamp incorporates one or more infrared radiation generators, the photometric and colour requirements for this front position lamp shall be met with and without the operation of the infrared radiation generator(s).

5.4.	In case of failure of the variable intensity control of:

(a) 	A rear position lamp category R2 emitting more than the maximum value of category R or R1;

(b)	A rear end-outline marker lamp category RM2 emitting more than the maximum value of category RM1;

(c)	A stop lamp category S2 emitting more than the maximum value of category S1;

(d)	A stop lamp category S4 emitting more than the maximum value of category S3;

Requirements of steady luminous intensity of the respective category shall be fulfilled automatically.

6.		Intensity of light emitted

6.1.	The light emitted by each of the two devices supplied shall be in the reference axis, of not less than the minimum intensity and of not more than the maximum intensity specified below:

|  | Minimum luminous intensity in cd | Maximum luminous intensity in cd when used as |
| --- | --- | --- |
|  |  | Single lamp | Lamp (single) marked "D" (paragraph 4.2.2.6.) |
| 6.1.1. Front position lamps, front end-outline marker lamp A or AM | 4 | 140 | 70 |
| 6.1.2. Front position lamps incorporated in a headlamp | 4 | 140 | - |
| 6.1.3. Rear position lamps, rear end-outline marker lamp |  |  |  |
| 6.1.3.1. R or R1 or RM1 (steady) | 4 | 17 | 8.5 |
| 6.1.3.2. R2 or RM2 (variable) | 4 | 42 | 21 |
| 6.1.4. Stop-lamps | 60 | 260 | 130 |
| 6.1.4.1. S1 (steady) |  |  |  |
| 6.1.4.2. S2 (variable) | 60 | 730 | 365 |
| 6.1.4.3. S3 (steady) | 25 | 110 | 55 |
| 6.1.4.4. S4 (variable) | 25 | 160 | 80 |

6.1.5.	For an assembly of two or more lamps the total intensity shall not exceed the maximum value prescribed for a single lamp.

6.2.	Outside the reference axis and within the angular fields defined in the diagrams in Annex 3 to this Regulation, the intensity of the light emitted by each of the two devices supplied must:

6.2.1.	In each direction corresponding to the points in the light distribution table reproduced in Annex 4 to this Regulation, be not less than the product of the minimum specified in the table of paragraph 6.1. above, by the percentage specified in the said table of the direction in question;

6.2.2.	In no direction within the space from which the light-signalling device is visible, exceed the maximum specified in the table of paragraph 6.1. above;

6.2.3.	However, a luminous intensity of 60 cd shall be permitted for rear position lamps reciprocally incorporated with stop-lamps (see paragraph 6.1.3. above) below a plane forming an angle of 5° with and downward from the horizontal plane;

6.2.4.	Moreover,

6.2.4.1.	Throughout the fields defined in the diagrams in Annex 3, the luminous intensity of the light emitted must be not less than 0.05 cd for front and rear position lamps and end-outline marker lamps, not less than 0.3 cd for stop-lamps;

6.2.4.2.	If a rear position lamp is reciprocally incorporated with a stop-lamp producing either steady or variable luminous intensity, the ratio between the luminous intensities actually measured of the two lamps when turned on simultaneously at the intensity of the rear position lamp when turned on alone should be at least 5: 1 in the field delimited by the straight horizontal lines passing through ±5° V and the straight vertical lines passing through ±10° H of the light distribution table.

If the rear position lamp or the stop lamp or both contain more than one light source and are considered as a single lamp, the values to be considered are those obtained with all sources in operation;

6.2.4.3.	The provisions of paragraph 2.2. of Annex 4 to this Regulation on local variations of intensity must be observed.

6.3.	The intensities shall be measured with the filament lamp(s) continuously alight and, in the case of devices emitting red light, in coloured light.

6.4.	In the case of devices of categories R2, RM2, S2 and S4 the time that elapses between energising the light source(s) and the light output measured on the reference axis to reach 90 per cent of the value measured in accordance with paragraph 6.3. above shall be measured for the extreme levels of luminous intensity produced by the device.  The time measured to obtain the lowest luminous intensity shall not exceed the time measured to obtain the highest luminous intensity.

6.5.	The variable intensity control shall not generate signals which cause luminous intensities:

6.5.1.	Outside the range specified in paragraph 6.1. above and

6.5.2.	Exceeding the respective steady luminous intensity maximum specified in paragraph 6.1. for the specific device:

(a)	For systems depending only on daytime and night time conditions: under night time conditions;

(b)	For other systems: under standard conditions.

6.6.	Annex 4, to which reference is made in paragraph 6.2.1. above, gives particulars of the methods of measurement to be used.

7.		Test procedure

Follow instructions in Annex 5 in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

8.		Colour of light emitted

The colour of the light emitted inside the field of the light distribution grid defined in paragraph 2. of Annex 3 shall be red or white.  Outside this field, no sharp variation of colour shall be observed. To check these colorimetric characteristics, the test procedure described in paragraph 7. of this Regulation shall be applied.

However, for lamps equipped with non-replaceable light sources (filament lamps and other), the colorimetric characteristics should be verified with the light sources present in the lamp, in accordance with the relevant sub-paragraph of Annex 5 in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

. 	The colour of the light emitted shall lie inside the chromaticity areas defined by the boundariesin Annex 4 in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

In the case of a category S3 or S4 stop lamp, which is intended to be mounted inside the vehicle, the colorimetric characteristics shall be verified with the worst case combination(s) of lamp and rear window(s) or sample plate(s).

These requirements shall also apply within the range of variable luminous intensity produced by:

(a)	Rear position lamps of category R2;

(b)	Rear end-outline marker lamps of category RM2;

(c)	Stop lamps of categories S2 and S4.

9.		Modifications of a type of direction indicator for
		motor vehicles and their trailers and extension of 
		approval

Paragraph 10 of Part II of Regulation 48  (Horizontal Reference Document (HRD)) shall apply.

10.		Conformity of production

The conformity of production procedures shall comply with those set out in the Agreement, Appendix 2 (E/ECE/324-E/ECE/TRANS/505/Rev.2), with the following requirements:

10.1.	Lamps shall be so manufactured as to conform to the type approved under this regulation. The compliance with the requirements set forth in paragraphs 6 and 8 above shall be verified as follows:

10.1.1.	The procedure of Paragraph 11 of Part II to Regulation 48  (Horizontal Reference Document (HRD)) shall apply.

10.2.	In addition to paragraph 1.2.1. in Annex 2 of Part II to Regulation 48  (Horizontal Reference Document (HRD)) for the minimum values required throughout the fields specified in Annex 4 to this Regulation the respective maximum deviations of the measured values shall correspond to the values shown in the table below:

| Required minimum value | Equivalent 20 per cent | Equivalent 30 per cent |
| --- | --- | --- |
| cd | cd | cd |
| 0,3 | 0,2 | 0,1 |
| 0,05 | 0,03 | 0,02 |

10.3.	The authority which has granted type approval may at any time verify the conformity control methods applied in each production facility. The normal frequency of these verifications shall be once every two years.

The Contracting Parties to the Agreement to which this Regulation is annexed are not precluded by Article 3 of that Agreement from prohibiting, for devices installed on vehicles registered by them, certain colours for which provision is made in this Regulation, or from prohibiting for all categories or for certain categories of vehicles registered by them stop-lamps having only steady luminous intensity.

11.		Penalties for non-conformity of production

Paragraph 12 of Part II of Regulation 48  (Horizontal Reference Document (HRD)) shall apply.

12.		Production definitively discontinued

Paragraph 13 of Part II of Regulation 48  (Horizontal Reference Document (HRD)) shall apply.

13.		Names and addresses of Technical Services 
		responsible for conducting approval tests, and of 
		Type approval Authorities

Paragraph 14 of Part II of Regulation 48  (Horizontal Reference Document (HRD)) shall apply..

14.		Transitional provisions

14.1.	Signalling lamps not equipped with filament lamps and category S3 stop lamps intended to be mounted inside a vehicle.

14.1.1.	As from the date of entry into force of Supplement 6 to the 02 series of amendments, no Contracting Party applying this Regulation shall refuse to grant approvals under this Regulation as amended by Supplement 6 to the 02 series of amendments.

14.1.2.	As from 36 months after the date of entry into force of Supplement 6 to the 02 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the type of lamps as described in paragraph 14.1. above meets the requirements of this Regulation as amended by Supplement 6 to the 02 series of amendments.

14.1.3.	Contracting Parties applying this Regulation shall not refuse to grant extensions of approvals to the preceding series of amendments to this Regulation.

14.1.4.	Contracting Parties applying this Regulation shall continue to grant approvals to those types of lamps as described in paragraph 14.1. above which comply with the requirements of this Regulation as amended by the preceding series of amendments during the 36 months' period which follows the date of entry into force of Supplement 6 to the 02 series of amendments.

14.2.	Fitting of lamps described in paragraph 14.1. above on a vehicle.

14.2.1.	As from the date of entry into force of Supplement 6 to the 02 series of amendments, no Contracting Party applying this Regulation shall prohibit the fitting on a vehicle of lamps described in paragraph 14.1. above approved under this Regulation as amended by Supplement 6 to the 02 series of amendments.

14.2.2.	Contracting Parties applying this Regulation shall continue to allow the fitting on a vehicle of lamps described in paragraph 14.1. above approved to this Regulation as amended by the preceding series of amendments during the 48 months' period which follows the date of entry into force of Supplement 6 to the 02 series of amendments.

14.2.3.	Upon the expiration of a period of 48 months after the date of entry into force of Supplement 6 to the 02 series of amendments, Contracting Parties applying this Regulation may prohibit the fitting of lamps described in paragraph 14.1. above which do not meet the requirements of this Regulation as amended by Supplement 6 to the 02 series of amendments on a new vehicle for which type approval or individual approval was granted more than 24 months after the entry into force of Supplement 6 to the 02 series of amendments to this Regulation.

14.2.4.	Upon expiration of a period of 60 months after the date of entry into force of Supplement 6 to the 02 series of amendments, Contracting Parties applying this Regulation may prohibit the fitting of lamps as described in paragraph 14.1. above which do not meet the requirements of this Regulation as amended by Supplement 6 to the 02 series of amendments on a new vehicle first registered more than 60 months after the date of entry into force of Supplement 6 to the 02 series of amendments to this Regulation.

Annex 1

Principal Examples of arrangements of the approval marks

1.	Front position lamp

The device bearing the approval mark shown above is a front position lamp approved in the Netherlands (E4), under approval number 221 pursuant to Regulation No. 7.

The number mentioned close to the symbol "A" indicates that approval was granted in accordance with the requirements of Regulation No. 7 as amended by the 02 series of amendments. The horizontal arrow indicates the side on which the required photometric specifications are met up to an angle of 80° H. The vertical arrow starting from a horizontal segment and directed downwards indicates a permissible mounting height of equal to or less than 750 mm from the ground for this device.

2.	Rear position lamp

The device bearing the approval mark shown above is a rear position lamp approved in the Netherlands (E4) under approval number 221 pursuant to Regulation No. 7, which may also be used in an assembly of two rear position lamps.

The number mentioned below the symbol "R1D" indicates that approval was granted in conformity with the requirements of Regulation No. 7 as amended by the 02 series of amendments.

The absence of an arrow means that, both right and left, the required photometric specifications are met up to an angle of 80° H.

3.	Front end-outline marker lamp

The device bearing the approval mark shown above is a front end-outline marker lamp approved in France (E2) under approval number 125 pursuant to Regulation No. 7.

The number mentioned below the symbol "AM" indicates that approval was granted in conformity with the requirements of Regulation No. 7 as amended by the 02 series of amendments. The horizontal arrow indicates the side on which the required photometric specifications are met up to an angle of 80° H.

4.	Rear end-outline marker lamp

The device bearing the approval mark shown above is a rear end-outline marker lamp with variable luminous intensity approved in Italy (E3) under approval number 122 pursuant to Regulation No. 7.

The number mentioned below the symbol "RM" indicates that approval was granted in conformity with the requirements of Regulation No. 7 as amended by the 02 series of amendments. The horizontal arrow indicates the side on which the required photometric specifications are met up to an angle of 80° H.

5.	Stop-lamp

The device bearing the approval mark shown above is a stop-lamp with one level of illumination approved in the Netherlands (E4) under approval number 221 pursuant to Regulation No. 7.

The number mentioned below the symbol "S1" indicates that the approval was granted in conformity with the requirements of Regulation No. 7 as amended by the 02 series of amendments.

6.	Interdependent lamps

| Marking of an interdependent lamp comprising part of an interdependent lamp system providing: A rear direction indicator lamp (category 2a) approved in accordance with the 01 series of amendments to Regulation No. 6, A red rear position (side) lamp (R1) approved in accordance with the 02 series of amendments to Regulation No. 7. This is also marked Y as it is an interdependent lamp forming part of an interdependent lamp system, A stop-lamp with variable luminous intensity (S2) approved in accordance with the 02 series of amendments to Regulation No. 7. |  | Marking of an interdependent lamp comprising part of an interdependent lamp system providing: A red rear position (side) lamp (R1) approved in accordance with the 02 series of amendments to Regulation No. 7. This is also marked Y as it is an interdependent lamp forming part of an interdependent lamp system, A reversing lamp (AR) approved in accordance with Regulation No. 23 in its original version. |
| --- | --- | --- |

For further examples Annex 1 of Part II to Regulation 48  (Horizontal Reference Document (HRD)) shall apply.

Annex 2

Communication

(Maximum format: A4 (210 x 297 mm))

concerning: 	Approval granted

Approval extended

Approval refused

Approval withdrawn

Production definitively discontinued

of a type of device pursuant to Regulation No. 7

Approval No...........	Extension No...........

1.	Trade name or mark of the device:

2.	Manufacturer's name for the type of device:

3.	Manufacturer's name and address:

4.	If applicable, name and address of the manufacturer's representative:

5.	Submitted for approval on:

6.	Technical Service responsible for conducting approval tests:

7.	Date of report issued by that Service:

8.	Number of report issued by that Service:

9.	Concise description:

9.1.	By category of lamp:

For mounting either outside or inside or both2

Colour of light emitted: red/white2

Number, category and kind of light source(s):

Voltage and wattage:

Light source module specific identification code:

Only for installation on M1 and/or N1 category vehicles: yes/ no2

Only for limited mounting height of equal to or less than 750 mm above
	the ground: yes/no2

Geometrical conditions of installation and relating variations, if any:

Application of an electronic light source control gear/variable intensity control:

(a)	Being part of the lamp: yes/no2

(b)	Being not part of the lamp: yes/no2

Input voltage(s) supplied by an electronic light source control gear/variable 
	intensity control:

Electronic light source control gear/variable intensity control manufacturer
	and identification number (when the light source control gear is part of 
	the lamp but is not included into the lamp body):

Variable luminous intensity:  yes/no2

9.2.	Function(s) produced by an interdependent lamp forming part of an 
	interdependent lamp system:

Front position lamp 	yes/ no2

R1 Rear position lamp	yes/ no2

R2 Rear position lamp 	yes/ no2

S1 Stop lamp 	yes/ no2

S2 Stop lamp 	yes/ no2

S3 Stop lamp 	yes/ no2

S4 Stop lamp 	yes/ no2

End-outline marker lamp 	yes/ no2

10.	Position of the approval mark: ................................................................................

11.	Reason(s) for extension (if applicable):

..................................................................................................................................

12.	Approval granted/extended/refused/withdrawn2: ...................................................

13.	Place: .......................................................................................................................

14.	Date: ........................................................................................................................

15.	Signature: ................................................................................................................

16.	The list of documents deposited with the Type Approval Authority which has granted approval is annexed to this communication and may be obtained on request.

Annex 3

Photometric measurements

1. 	In addition with the following paragraph the photometric measurements are carried out according to Annex 5 in Part II of Regulation 48  (Horizontal Reference Document (HRD)).

2.	Table of standard light distribution

# Table of light distribution for category S3 and S4 stop-lamps

|  | Horizontal |
| --- | --- |
| Vertical | 10° | 5° | 0° | 5° | 10° |
| 10° | 32 | - | 64 | - | 32 |
| 5° | 64 | 100 | 100 | 100 | 64 |
| 0° | 64 | 100 | 100 | 100 | 64 |
| 5° | 64 | 100 | 100 | 100 | 64 |

2.1.	The direction H = 0° and V = 0° corresponds to the reference axis. (On the vehicle it is horizontal, parallel to the median longitudinal plane of the vehicle and oriented in the required direction of visibility.) It passes through the centre of reference. The values shown in the table give, for the various directions of measurement, the minimum intensities as a percentage of the minimum required in the axis for each lamp (in the direction H = 0° and V = 0°).

2.2.	Within the field of light distribution of paragraph 2., schematically shown as a grid, the light pattern should be substantially uniform, i.e. the light intensity in each direction of a part of the field formed by the grid lines shall meet at least the lowest minimum value being shown on the grid lines surrounding the questioned direction as a percentage.

2.3.		However, in the case where a device is intended to be installed at a mounting height of equal to or less than 750 mm above the ground, the photometric intensity is verified only up to an angle of 5° downwards.

Annex 4

Front and rear position lamps, end-outline marker lamps and stop-lamps: minimum angles required for light distribution in space of these lamps

In all cases, the minimum vertical angles of light distribution in space are 15° above and 15° below the horizontal for all categories of devices included in this Regulation, except:

(a)	For lamps with a permissible mounting height ( 750 mm above the ground, for which they are 15° above and 5° below the horizontal;

(b)	For category S3 or S4 stop lamp for which they are 10° above and 5° below the horizontal.

Minimum horizontal angles of light distribution in space

Front end-outline marker lamp (AM)

Rear end-outline marker lamp

(RM1, RM2)

Rear position lamps

Stop lamps (S1 and S2)

Annex 5 deleted

Annex 6 deleted

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

As defined in the Consolidated resolution on the Construction of vehicles (R.E.3), 
document ECE/TRANS/WP.29/78/Rev.2, para.2.

Good visibility (meteorological optical range MOR > 2,000 m defined according to WMO, Guide to Meteorological Instruments and Methods of Observation, Sixth Edition, ISBN: 92-63-16008-2, pp 1.9.1/1.9.11, Geneva 1996 ) and clean lens.

Distinguishing number of the country which has granted/extended/refused/withdrawn approval (see approval provisions in the Regulation).

Strike out what does not apply.

The angles shown in these diagrams are correct for devices to be mounted on the right side of the vehicle. The arrows point to the front of the vehicle.

# Text boxes

SLR-03-05

E2

125

AM

02

E3

122

RM2

02

issued by: 		Name of Administration:

......................................

......................................

......................................

Front position lamps. 
On and above the H plane

for all lamps.

Under the H plane for

lamps intended for M2,M3, N2 or N3 category vehicles

Front position lamps,

Under the H plane for M1
or N1 category vehicles

H plane: "horizontal plane going through the reference centre of the lamp"

Driving direction

Driving direction

Driving direction

Reference axis

20°

80°

Driving direction

Driving direction

Reference axis

20°

45°

Driving direction

Stop-lamps (S3)

Driving direction