Find below the formal proposal for R61 intended for the 108th session of GRSG

|  | United Nations | ECE/TRANS/WP.29/GRSG/2015/xx |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 29 January 2015 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

108th session

Geneva, 4–8 May 2014

Item yy of the provisional agenda

Regulation No. 61 (External projections cabs of commercial vehicles) –

Proposal for amendments to Regulation No. 61 (External projections cabs of commercial vehicles)

Submitted by the chair of the informal group IGCMS-II *

The text reproduced below has been prepared by the informal group on camera-monitor systems (IGCMS-II) to align the provisions of Regulation 61 with the proposed amendments of Regulation 46 (devices for indirect vision) for the replacement of rear-view mirrors by camera monitor systems. The modifications to the current text of UN Regulation No. 61 are marked strikethrough for deleted text and bold for new characters. This proposal for a supplement to Regulation 61 and the proposal for the replacement of rear-view mirrors by camera monitor systems should be handled by GRSG and WP.29 in parallel.

Proposal for amendments to UN Regulation No. 61 (External projections of commercial vehicles)

I. Proposal

Paragraph 1.1, amend to read:

“1.1	This regulation applies to the external projections of goods vehicles of categories N1, N2 and N3, limited to the “external surface” as defined below. 
It does not apply to the exterior rearview mirrors devices for indirect vision, including their support, or to the accessories such as aerials and luggage racks.”

II. Justification

The proposal of the IGCMS-II amends the provisions on the scope such that the exemption does not only apply to exterior rearview mirrors but to devices for indirect vision in general, including camera-monitor systems.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.