Find below the formal proposal for R26 intended for the 108th session of GRSG

|  | United Nations | ECE/TRANS/WP.29/GRSG/2015/yy |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 29 January 2015 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

108th session

Geneva, 4–8 May 2015

Item yy of the provisional agenda

Regulation No. 26 (External projections)

Proposal for amendments to Regulation No. 26 (External projections)

Submitted by the chair of the informal group IGCMS-II *

The text reproduced below has been prepared by the informal group on camera-monitor systems (IGCMS-II) of GRSG to align the provisions of Regulation 26 with the proposed amendments of Regulation 46 (devices for indirect vision) for the replacement of rear-view mirrors by camera monitor systems. The modifications to the current text of UN Regulation No. 21 are marked in bold for new characters; deleted text is given strikethrough. This proposal and the proposal for Regulation 46 for the replacement of rear-view mirrors by camera monitor systems should be handled by GRSG and WP.29 in parallel.

Proposal for amendments to UN Regulation No. 26 (external projections)

I. Proposal

Paragraph 1. amend to read:

“1.	Scope and purpose

1.1.	This Regulation applies to external projections of category M1 vehicles.  It does not apply to exterior rear-view mirrors devices for indirect vision or to the ball of towing devices.

1.2.	The purpose of this Regulation is to reduce the risk or seriousness of bodily injury to a person hit by the bodywork or brushing against it in the event of a collision. This is valid both when the vehicle is stationary and in motion.

II. Justification

This editorial proposal of the IGCMS-II amends the provisions on external projections according Regulation 26 such that all devices of indirect vision are excluded from the scope including conventional mirrors and Camera Monitor devices.

____________

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.