Find below the formal proposal for R107 intended for the 108th session of GRSG

|  | United Nations | ECE/TRANS/WP.29/GRSG/2015/yy |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 29 January 2015 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on General Safety Provisions

108th session

Geneva, 4–8 May 2015

Item yy of the provisional agenda

Regulation No. 107 (category M2 or M3 vehicles with regard to their general construction)

Proposal for amendments to Regulation No. 107 (category M2 or M3 vehicles with regard to their general construction)

Submitted by the chair of the informal group IGCMS-II *

The text reproduced below has been prepared by the informal group on camera-monitor systems (IGCMS-II) of GRSG to align the provisions of Regulation 107 with the proposed amendments of Regulation 46 (devices for indirect vision) for the replacement of rear-view mirrors by camera monitor systems. The modifications to the current text of UN Regulation No. 107 are marked in bold for new characters; deleted text is given strikethrough. This proposal and the proposal for Regulation 46 for the replacement of rear-view mirrors by camera monitor systems should be handled by GRSG and WP.29 in parallel.

Proposal for amendments to UN Regulation No. 107 (category M2 or M3 vehicles with regard to their general construction)

I. Proposal

## Paragraph 7.7.1.8. amend to read:

“7.7.1.8. 	However, one or more folding seat(s) for use by the crew may obstruct the access passage to a service door when in the position of use provided that:

7.7.1.8.1. 	It is clearly indicated, both in the vehicle itself and on the communication form (see Annex 1), that the seat is for the use of crew only,

7.7.1.8.2. 	When the seat is not in use it folds automatically as necessary to enable the requirements of paragraphs 7.7.1.1. or 7.7.1.2. and 7.7.1.3., 7.7.1.4. and 7.7.1.5. of this annex to be met;

7.7.1.8.3. 	The door is not considered to be a mandatory exit for the purpose of paragraph 7.6.1.4. of this annex,

7.7.1.8.4. 	When the seat is in the position of use, and when it is in the folded position, no part of it shall be forward of a vertical plane passing through the centre of the seating surface of the driver’s seat in its rearmost position and through the centre of the exterior rear-view mirror mounted on the opposite side of the vehicle or any monitor used for camera-monitor devices, whatever applicable.”

II. Justification

This proposal of the IGCMS-II amends the provisions on the category M2 or M3 vehicles with regard to their general construction according Regulation 107 to include vehicles equipped with devices for indirect vision such as camera-monitor devices.
A folding seat for use by the crew, in position of use and when folded, may not obstruct the driver’s view on the exterior rear-view mirror. This also applies for the view on the monitor used for camera-monitor devices, if fitted.

____________

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.