## Slide 1: Definition of a Vehicle Type for IWVTA + Extension of Approvals
SGR0-16-12
Transmitted by OICA

## Slide 2: Agenda
Part 1: Type definition for IWVTA
Part 2: Proposal for the approval number for IWVTA
Part 3: Extension of an IWVTA changing the level of conformity

## Slide 3: Type definition for IWVTA: general considerations
1 type of vehicle is expected to be covered by 1 IWVTA
U-IWVTA and L-IWVTA should be clearly distinguished no mix of approval levels within 1 approval no mix of conformity levels within 1 type?
However, intuitively, one would rather identify vehicle types by a “common overall appearance” than by conformity criteria
with ESC
with ESC
without ESC
Same type
Different body variants
Different types
?

## Slide 4: Proposal for reconciliation: Create an additional order scheme
A vehicle type can contain all variants regardless of their level of conformity  it corresponds to what we are used to
Within a vehicle type every single IWVTA type defines one level of conformity
Manufacturer identifies the IWVTA types within a vehicle type by a unique type designation
Vehicles within one vehicle type get approval numbers that are related (see below)
Approvals for all IWVTA types within 1 vehicle type shall be handled by the same approval authority
IWVTA type 1:
“Beetle with ESC”
IWVTA type 2:
“Beetle without ESC”
Vehicle type Beetle

## Slide 5: Proposed definitions (1 of 2)
A vehicle type is defined like the vehicle type in EC-WVTA
1.1 | Vehicle type
1.1.1 | A “vehicle type” shall consist of vehicles which have all of the following features in common: (a) the manufacturer’s company name. A change in the legal form of ownership of the company does not require that a new approval has to be granted; (b) the design and assembly of the essential parts of the body structure in the case of a self-supporting body. The same shall apply mutatis mutandis to vehicles the bodywork of which is bolted on or welded to a separate frame.
1.1.2 | By way of derogation from the requirements of paragraph 1.1.1(b), when the manufacturer uses the floor portion of the body structure as well as the essential constituent elements forming the front part of the body structure located directly in front of the windscreen bay, in the construction of different kinds of bodywork (for example a saloon and a coupe), those vehicles may be considered as belonging to the same vehicle type. Evidence thereof shall be provided by the manufacturer.
1.1.3 | A vehicle type shall consist of at least one IWVTA type.

## Slide 6: Proposed definitions (2 of 2)
An IWVTA type is defined using the “level of conformity” criterion
1.2 | IWVTA type
1.2.1 | A “IWVTA type” shall consist of vehicles which have all of the following features in common: (a) The vehicle type (b) the level of conformity with respect to the UN Regulations listed in Annex 4 which are applicable to the variants and versions within the type.
1.2.2 | The level of conformity cited in paragraph 1.2.1 (b) is understood the following way (a) If a UN Regulation listed in Annex 4 is applicable to different variants or versions within a vehicle type then all these variants and versions need to comply with the same version of that UN Regulation. (b) Some of the UN Regulations listed in Annex 4 may be applicable not to all variants or versions within the same IWVTA type (e.g. high voltage protection is relevant only for electric or hybrid variants). (c) In the process of extending an IWVTA the level of conformity can be raised as an existing type can be amended to meet the requirements of a later version of this Regulation. However, such amendment needs to cover all variants and versions within the IWVTA type at the same time.
1.2.3 | The manufacturer shall assign a unique type designation to each IWVTA type within a vehicle type.
1.2.4 | An IWVTA type shall consist of at least one variant and one version.
1.2.5 | All variants and versions within one IWVTA type shall be covered by the same IWVTA approval.
1.2.6 | Approvals for all IWVTA types within one vehicle type shall be handled by the same approval authority.

## Slide 7: Agenda
Part 1: Type definition for IWVTA
Part 2: Proposal for the approval number for IWVTA
Part 3: Extension of an IWVTA changing the level of conformity

## Slide 8: Approval Number for IWVTA according to Schedule 4
E4*0R00/00*0004*02
Observations:
The supplement number seems obsolete since the update process of UN-R0 foresees series of amendments
The letters U or L are foreseen in the approval mark. It seems appropriate to include them in the approval number as well
A 4-digit sequential number may be restrictive if it has to identify both vehicle and IWVTA types
Section 4: Number of the extension
Section 3: sequential number of the approval
Section 2: Regulation #, # of series of amendments / # of supplement
Section 1: # of CP

## Slide 9: Approval Number for IWVTA new proposal
E4*0R00/U*0004/01*02
Explanation of changes:
The letters U or L are included in section 2 after the number of the series of amendments
A 6-digit number for Section 3 is proposed which is construed as follows:
  First 4 digits identify the vehicle type : a new sequential number is assigned by the approval authority once the manufacturer applies for the first approval of a new vehicle type
  / followed by 2 last digits which sequentially number the different type approvals within a vehicle type starting with 01. They correspond to different IWVTA types
Section 4: Number of the extension
Section 3: sequential number of the approval
Section 2: Regulation #, # of series of amendments /
letter U for universal, L for limited
Section 1: # of CP

## Slide 10: Agenda
Part 1: Type definition for IWVTA
Part 2: Proposal for the approval number for IWVTA
Part 3: Extension of an IWVTA changing the level of conformity

## Slide 11: Why change the level of conformity
New requirements enter into force and the manufacturer technically upgrades the vehicles
New requirements enter into force and the manufacturer does not upgrade the vehicles: an existing U-IWVTA has to be downgraded to become a L-IWVTA
The manufacturer wants to build vehicles (which are otherwise the same, i.e. “belong to the same vehicle type”) according to different compliance specifications for different markets, e.g. U-IWVTA and L-IWVTA
How shall these processes be handled?
When and how to extend existing approvals?
When and how to issue new approvals?

## Slide 12: The cases when changing the level of conformity
Before modification:
1 type of vehicle having 1 IWVTA
Modification due to:
New requirements for existing type
Technical changes of the vehicles
Case A
After the modification all vehicles have the same level of conformity
Case B
After the modification vehicles with different levels of conformity are produced

## Slide 13: Case A: After the modification all vehicles have the same level of conformity
If the modification is such that the vehicles before and after no longer belong to the same vehicle type a new IWVTA has to be issued.
If the modification is such that the vehicles before and after belong to the same vehicle type and there is no change of status between U and L the existing IWVTA can be extended:
  Section 3 of the approval number remains unchanged
  Section 2 of the approval number has to be changed if necessary (i.e. if the approval is to another series of amendments)
If the modification is such that the vehicles before and after belong to the same vehicle type and there is a change of status between U and L a new IWVTA shall be issued:
  In the last 2 digits of Section 3 of the approval number the next free number is assigned
  Section 2 of the approval number has to be changed as necessary:
    Approval to other series of amendments
    Change of status between L-IWVTA and U-IWVTA
  Approval markings have to be changed as necessary
In both preceding cases the same rules apply to the handling of transitional provisions
  For systems and components already covered by the pre-existing IWVTA the requirements for existing type approvals shall be applied
  For systems and components not yet covered by the pre-existing IWVTA the requirements for new type approvals shall be applied

## Slide 14: Case B: After the modification vehicles with different levels of conformity are produced
If the modification for some or all vehicles covered by the IWVTA is such that these vehicles before and after no longer belong to the same vehicle type completely new IWVTAs for these vehicles have to be issued.
If the modification is such that the vehicles before and after belong to the same vehicle type the existing IWVTA has to be split, i.e. the existing IWVTA can be extended plus a new IWVTA within the same vehicle type has to be issued:
  The first 4 digits of section 3 of the approval number remain unchanged for both approvals
  The last 2 digits of section 3 of the approval number remain unchanged for the approval that is extended whereas the new IWVTA gets the next free sequential number
  For both approvals section 2 of the approval number has to be changed as necessary:
    Approval to other series of amendments
    Change of status between L-IWVTA and U-IWVTA
  Approval markings have to be changed accordingly
  For both approvals for systems and components already covered by the pre-existing IWVTA the requirements for existing type approvals shall be applied
  For both approvals for systems and components not yet covered by the pre-existing IWVTA the requirements for new type approvals shall be applied

## Slide 15: Case B: proposed way of splitting an IWVTA
Question: if an IWVTA has to be split into 2 approvals according to the procedure described in the last slide: which portion vehicles shall be covered by the extended approval, and for which shall the new approval be issued
Proposed principle:
If the pre-existing IWVTA was a U-IWVTA and one of the approvals resulting from the split remains universal then this shall be the extension
If the pre-existing IWVTA was a L-IWVTA and one of the approvals resulting from the split is universal then this shall be the new approval
Whenever there is a change in approval levels between U and L a new approval shall be issued.
All other cases shall be decided at the discretion of the approval authority
The manufacturer has to assign different type designations to the 2 types. He shall continue to use the pre-existing designation for the type the approval of which is extended
When repeatedly splitting existing approvals care shall be taken that no vehicle could belong to 2 different IWVTA types at the same time.
U-IWVTA
Section 3+4: 0021/01*01
U-IWVTA
Section 3+4: 0021/01*02
L-IWVTA
Section 3+4: 0021/02*00
1.
L-IWVTA
Section 3+4: 0021/01*01
L-IWVTA
Section 3+4: 0021/01*02
U-IWVTA
Section 3: 0021/02*00
2.

## Slide 16: Example 1 (of 4)
Before
vehicle type covered by U-IWVTA
What happens
New requirements enter into force
Manufacturer performs technical changes in order to meet new requirements (involves no change in vehicle type characteristics)
What to do
Extend existing U-IWVTA
Sections 1-3 of the approval number and marking remain unchanged (unless the change is such that it fully covers all additional requirements of the next series of amendments)
U-IWVTA
E4*0R01/U*0021/01*01
U-IWVTA
E4*0R01/U*0021/01*02

## Slide 17: Example 2 (of 4)
Before
vehicle type covered by U-IWVTA
What happens
New requirements enter into force
Manufacturer leaves vehicles unchanged
What to do
Issue a new L-IWVTA
Approval number and marking are changed accordingly
U-IWVTA
E4*0R01/U*0021/01*01
L-IWVTA
E4*0R01/L*0021/02*00

## Slide 18: Example 3 (of 4)
Before
vehicle type covered by U-IWVTA
What happens
New requirements enter into force
Manufacturer performs technical changes in order to meet new requirements (involves no change in vehicle type characteristics) but only for part of the vehicles
What to do
Extend existing U-IWVTA, here Sections 1-3 of the approval number and marking remain unchanged (as in example 1)
Create a new L-IWVTA under a new type designation
Note: example 3 simply combines the outcomes of examples 1+2
U-IWVTA
E4*0R01/U*0021/01*01
U-IWVTA
E4*0R01/U*0021/01*02
L-IWVTA
E4*0R01/L*0021/02*00

## Slide 19: Example 4 (of 4)
Before
vehicle type covered by L-IWVTA
What happens
Manufacturer performs technical changes in order to meet requirements for U-IWVTA (involves no change in vehicle type characteristics) but only for part of the vehicles
What to do
Extend existing L-IWVTA, here Sections 1-3 of the approval number and marking remain unchanged
Create a new U-IWVTA under a new type designation
L-IWVTA
E4*0R01/L*0021/01*01
L-IWVTA
E4*0R01/L*0021/01*02
U-IWVTA
E4*0R01/U*0021/02*00

## Slide 20: Necessary changes in draft UN-R0
If the proposed concept is accepted the following changes in draft UN-R0 are required:
Annex 7: inclusion/revision of the definitions for vehicle type and IWVTA type
Annex 2: inclusion of the composition of the type approval number, corresponding adaptation for the examples of the approval marking
Annex 5: inclusion of IWVTA type and type designation into the information document
Annex 1: inclusion of IWVTA type and type designation in section I of the communication form; also the possibility of changing between U-IWVTA and L-IWVTA has to be eliminated
Annex 6: inclusion of IWVTA type / type designation into Appendix 1
Article 7: either rewording of the Article based on the proposal from NL+OICA or creation of a separate Annex specifying in more detail the procedures specified in Part 3 of this presentation
Article 2: inclusion of a generic definition of IWVTA type