## Slide 1: WLTP-11-6e
1
25.05.2015
Proposal
Crawler gear requirements based on transmission parameters

## Slide 2: Basis of the Development
2
Basis of the development of crawler gear requirements was a database of vehicles consisting of 42 vehicles taken from the WLTP in-use database, the validation 2 database and a database for high powered vehicles from previous research projects.
This data was complemented by 45 vehicle configurations, whose technical data including the transmission was modified in order to include also extreme cases or to assess the influence of parameter variations.

## Slide 3: Basis of the Development
3
Examples: in some cases was the number of gears modified between 5 (4) and 7 in that way, that the n/v ratio for the highest gear was kept constant and the ratios for the other gears were set to higher values with increasing number of gears (see WLTP-GS-TF-26).
Another parameter, which was varied is the rated speed value. The complete list of the vehicles from the two WLTP databases is shown in WLTP-GS-TF-26.
The maximum speed and the gear number, in which the max. vehicle speed is reached were calculated for the 87 vehicles with the new gearshift calculation tool using road load values, which were based on expert guesses by the author.

## Slide 4: Development of crawler gear requirements
4
From table 1 in WLTP-GS-TF-26 could be concluded, that the only requirements, that would work properly and would fulfil the side condition to prevent the application for high powered sports cars, are thresholds for the ratio between the n/v rations in 1. and 2. gear and the n/v ratio in that gear, in which the maximum vehicle speed is reached.
The proposed thresholds are 7 for the 1st gear and 4 for the 2nd gear.
Some of the N1 vehicles and even one of the M1 vehicles from the WLTP databases fulfill the requirement for the 1st gear, but none of them fulfill the requirement for the 2nd gear.

## Slide 5: Development of crawler gear requirements
5
This underlines the importance for the 2nd gear requirement, which prevents misuse for high powered M1 vehicles.
But all 7speed versions of the modified vehicles as well as the two N1 vehicles, that were modified in order to comply fulfill both requirements.
The reason for the compliance of the 7speed versions is, that the n/v ratio for the highest gear was kept constant and the ratios for the other gears were set to higher values with increasing number of gears, as mentioned before, so that the 1st gear for the 7speed versions becomes really a crawler gear.

## Slide 6: Development of crawler gear requirements
6
The gear ratio spread requirements were then tested for 229 vehicles from the WLTP in-use database and from the WLTP validation 2 database.
The results are summarized in table 1.
These requirements were also supported by corresponding transmission design data for N2 and N3 vehicles, that are shown in table 3 of WLTP-GS-TF-26 and covers 6speed to 16speed transmissions.
This proposal was accepted by the TF members except the Japanese colleagues, who sent examples of vehicle configurations to Nick Arden and the chairman, which have a crawler gear, but would not qualify, when applying the proposed ratio spread criteria.

## Slide 7: Development of crawler gear requirements
7
Table 1

## Slide 8: Development of crawler gear requirements
8
These examples were assessed by the chairman.
The engine power versus vehicle speed diagrams in figures 1 to 3 show examples, that shall illustrate the proposal of the chairman for a correction factor, that would take care of the concerns of the Japanese colleagues.
Figure 1 shows an example of a N1 vehicle from Japan, which fulfils the requirements for the 1st gear being a crawler gear.
Figure 2 shows another example of a N1 vehicle from Japan, which does not fulfil the requirements for the 1st gear being a crawler gear, but with a similar transmission design as in figure 1.

## Slide 9: Engine power vs vehicle speed, N1
9
Figure 1

## Slide 10: Engine power vs vehicle speed, N1
10
Figure 2

## Slide 11: Development of crawler gear requirements
11
Figure 3 shows the same vehicle as in figure 2, but with a different transmission design. The gearing is so short, that the maximum speed of the vehicle is determined by the engine speed limitation and is much lower than the maximum speed determined by the driving resistance power.
For this vehicle the 1st gear should be a crawler gear, but it does not meet the ratio spread criteria.
But when the ratio spreads are multiplied by the correction factor
  vmax(Pres=Prated) / v_s_gvmax
the ratio spread criteria would be fulfilled for this example. The two other examples would remain as before.

## Slide 12: Engine power vs vehicle speed, N1
12
Figure 3

## Slide 13: Development of crawler gear requirements
13
vmax(Pres=Prated) is the (theoretical) maximum vehicle speed, where the driving resistance power equals rated power for optimal gearing.
  v_s_gvmax is the vehicle speed at rated engine speed in the gear, where the maximum vehicle speed is reached.
  Since v_s_gvmax = nrated / n/v(gvmax), the correction factor can also be expressed as
    vmax(Pres=Prated) * n/v(gvmax) / nrated

## Slide 14: Proposal for crawler gear requirements
14
Finally, this proposal was adopted by the task force.
The proposal is as follows:
The 1st gear of a transmission is a crawler gear and can be disregarded for the gear use calculation as well as when driving the cycle on a chassis dynamometer on request of the manufacturer, if the following requirements are fulfilled:
  The vehicle does not have a two-range transmission,
  The vehicle is homologated to tow a trailer,
  ((n/v1)/(n/vgvmax))*(vmax(Pres=Prated)/v_s_gvmax) > 7,
  ((n/v2)/(n/vgvmax))*(vmax(Pres=Prated)/v_s_gvmax) > 4,

## Slide 15: Proposal for crawler gear requirements
15
  The vehicle can pull away five times within 4s in a total of 5 min on a gradient of 12% in 2nd gear at a mass of mr + 25 kg + (GTM – mr – 25 kg)*0.28
  n/v1 is the ratio between engine speed in min-1 and vehicle speed in km/h in 1st gear.
  n/vgvmax is the ratio between engine speed in min-1 and vehicle speed in km/h in 2nd gear.
  mr is the mass in running order.
  GTM is the gross train mass. This is the gross vehicle mass plus maximum trailer mass as homologated by the manufacturer.
  A proposal for the integration of these requirements in annex 2 of the GTR is provided in WLTP-11-7e.

## Slide 16: Development of crawler gear requirements
16
This concludes the proposal for crawler gear requirements.