## Slide 1: OI #17: Default Road Load
  Handed over from phase 1a:
  as an alternative for determining road load with the coast down or torque meter, a calculation method for default road load parameters may be used
  (based on future data) the parameters can be reviewed.
  Situation:
  No new data has been made available (so far)
  On request of IWG#7 RDW (André Rijnders) took initiative to develop an alternative methodology
  At IWG#8 (Pune) an initial proposal was presented and discussed
  At IWG#9 the ACEA Task Force LCV offered to develop the methodology jointly with RDW/TNO
  At IWG#10 a new initial proposal was presented
WLTP-11-17e

## Slide 2: OI #17: Default Road Load
  Aim and principles of new proposal:
  Alternative for coast down and torque meter method
  But also alternative for calculation method (table values)
  Scope: multi-stage vehicles and low-volume, heavy LCVs
  Reduce test burden
  Appropriate road load values
  No loophole (coast down and torque meter preferred approach)
André Rijnders RDW / The Netherlands – Wouter Vandermeulen ACEA-LCV

## Slide 3: OI #17: Default Road Load
  Outcome IWG#10:
  Agreement to proceed under Annex 4 TF
  Guidance:
  Timeline: initial gtr proposal at IWG#11, adoption IWG#12
  Conservative approach (safeguard)
  (For the moment) Scope: multi-stage vehicles and low-volume, heavy LCVs.
  (For the moment) Restrict scope purely on objective criteria (like maximum laden mass)
  Present comparison of RL determination options
  Secure adequate link to CO2 calculations (Annex 7)
André Rijnders RDW / The Netherlands – Wouter Vandermeulen ACEA-LCV

## Slide 4: OI #17: Default Road Load
  Updated To Do List (as of IWG#10):
  Appropriate name
  Confirmation of least square methodology to determine F0 and F2
  Selection of Upward and Downward correlation factors (conservative)
  Validation calculations new proposal
  Define selection representative Multi Stage Vehicle
  Definition of Multi Stage Vehicle in GTR or regional legislation
  If appropriate include drafting on CO2 calculation (Annex 7)
  Matrix to compare test burden vs. safeguard of RL determination options

## Slide 5: OI #17: Default Road Load
  Proposed name:
Road Load Matrix Family

## Slide 6: OI #17: Default Road Load
  Scope
  Vehicles with technically permissible maximum laden mass ≥ 3 ton (mainly large vans and crew busses)
  Low sales volumes, but large number of variations due to customer demands
  RL family too restrictive
  Table values give unfavorably high worst case road load and CO2 figures
  Category in gtr limited to 3.5 tons. Higher maximum mass may be applied regionally.
  Multi stage vehicles
  Road load determination very extensive - variety of possible bodyworks.
  Even with RL family difficult to obtain the cycle energy demand for all possible bodyworks which could be used by the second stage manufacturers
  Table values very unattractive for first stage OEM’s under EU CO2 legislation
  MSV not recognized in gtr
  Proposal:
  New approach open to all vehicle categories, including multi stage
  General mass-based restriction: 3.0 – 3.5 ton
  Widening scope via regional implementation

## Slide 7: OI #17: Default Road Load
  Scope
II Text of the global technical regulation
5. General Requirements
(new) 5.8 Road load matrix family
The road load matrix family can be applied for vehicles designed for a technically permissible maximum laden mass ≥ 3000 kg.
Unless vehicles are identical with respect to the following characteristics , they shall not be considered to be part of the same road load matrix family:
Transmission type (e.g. manual, automatic, CVT);
Number of powered axles;
[exclusion of Evs?]

## Slide 8: OI #17: Default Road Load
  Approach:
  Single coastdown (or torque meter) test with representative vehicle and estimated worst Cd ( )
  Calculation road load vehicle H and L, based on conservative extension (based on DAf, DTM, DRR) and maximum family range ( , )
  Chassis dyno test with the representative vehicle and settings H and L
  4. CO2 calculation individual vehicle by interpolation
Volume
Road Load
N1 – 7m³
LH2
LH3
Coast Down
N1 – 8m³
N1 – 16m³
N1 – 12m³

## Slide 9: OI #17: Default Road Load
  Selection of representative test vehicle (1)
    Responsible authority shall agree
    Estimated worst Cd
          No simple way to determine Cd of all vehicle configurations
          Extrapolation formulas do not include Cd as a parameter
        Representative body shape, rolling resistance and mass.
        Multi-stage: no representative body shape. Equip chassis-cabin with square box with rounded corners and total vehicle height 3m - Still under discussion

## Slide 10: OI #17: Default Road Load
  Selection of representative test vehicle (2)
4.2.1 Test vehicle
(New) 4.2.1.3: Application of the road load matrix family
A test vehicle fulfilling the criterion of paragraph 5.8 of this GTR and that is representative for the intended vehicles series to be covered by the road load matrix family in terms of estimated worst Cd value, body shape, estimated average tyre rolling resistance, estimated highest n/v ratio and estimated average mass of optional equipment shall be selected to determine the road load. In case no representative body shape can be determined the test vehicle shall be equipped with a square box with rounded corners (radius ≤25 mm) with width equal to the maximum width of the vehicles covered by the road load matrix family and total height of test vehicle 3.0 ± 0.1 m.
The manufacturer and the responsible authority shall agree which vehicle test model is representative.
[The actual test mass of the test vehicle shall be at least 3000 kg.]
    (Note: Vehicles H and L are needed for Mco2-correlation (Annex 7, 3.2.3.2.3, equation (40) – if vehicles H and L are introduced no further modifications to Annex 7 are required)
The vehicle parameters test mass, tyre rolling resistance and frontal area of both a vehicle H and L shall be determined in such a way that vehicle H produces the highest cycle energy and vehicle L the lowest cycle energy from the road load matrix family. The manufacturer and the responsible authority shall agree on the vehicle parameters for vehicle H and L.
The road load of vehicles H and L shall be calculated according to (new) paragraph 5bis of this Annex.

## Slide 11: OI #17: Default Road Load
  Calculation road load coefficients of representative test vehicle
4.3.1.4.5 (coast down) + 4.3.2.5.2 (on-board anemometer) + 4.4.4/5 (torque meter) (+ wind tunnel??)
Add to the end of the paragraphs:
In case the tested vehicle is the representative vehicle of a road load matrix family, the coefficient f1 shall be set to zero and the coefficients f0 and f2 shall be recalculated according to the least squares regression analyses.

## Slide 12: OI #17: Default Road Load
  Extension (1)
  f0 and f2 derived (by least squares regression analysis) from coastdown data set of the tested vehicle
  Conservative approach implies different correlations between road load values and delta’s TM, Af and RR for Upward (H) and Downward (L) extrapolation
  f0_new = (1-X0)*f0 + (X0)(f0*(TM+DTM)/TM+9.81*DRR*(TM+DTM))
  f2_new = (1-X2)*f2 + (X2)*f2* (Af+DAf)/ Af
  Different X0 and X2 values for upward and downward extrapolation to be determined

## Slide 13: OI #17: Default Road Load
  Extension (2) – Additional remarks
  Justification different approach for upward and downward extrapolation
  Real world correlation between road load values and delta’s TM, Af, RR: typically in 85-100% range
  Conservative: in general real world road load should not be higher than the calculated value (worst case, but realistic)
  OEM to some extend free to choose test vehicle
  Formulas are a proper but simplified reflection of real world correlation
    Drivetrain losses and delta Cd not included
    F1 left out
    No calibration checks as exists for interpolation methods

## Slide 14: OI #17: Default Road Load
Observed correlation road load values and Af, TM, RR
Delta Af, TM, RR
Road load
Tested vehicle
Max correlation
Reduced correlation
Real world correlation
bandwidth

## Slide 15: OI #17: Default Road Load
Proposed correlations for upward and downward extrapolation: conservative
Delta Af, TM, RR
Road load
Tested vehicle
Upward correlation
Downward correlation
Real world correlation bandwidth

## Slide 16: OI #17: Default Road Load
Selection vehicles L and H for chassis dyno emissions test
Delta Af, TM, RR
Road load
RL test vehicle
Real world correlation
bandwidth
Vehicle L
Vehicle H
Calculated chassis dyno setting veh H
Calculated chassis dyno setting veh L

## Slide 17: OI #17: Default Road Load
Road load/
cycle energy
CO2
Index M = Coast Down
Index E = extrapolated without x-factor
Index C = calculated with x-factor
VLE
VLC
VHC
VHE
VTM
Safety margin
Worst case Cd and correlation factors determine safety margin

## Slide 18: OI #17: Default Road Load
  Extension (3) – 85%-rule for calculation chassis dyno settings vehicle L
  The equations are a simplified representation of the complex reality: the effects of the included parameters are therefore overrepresented. The separation between rolling resistance and air drag is not as straightforward as the f0 and f2 equations suggest.
  Total rolling resistance is a combination of tyres, driveline and transmission. The latter two are only slightly test mass dependent. Typically drivetrain losses are 10%-20% of the total f0. An EC study yielded 14% for a front wheel drive vehicle with manual transmission. Larger effects for automatic transmissions and all-wheel drive can be expected.
  The rolling resistance typically increases 15% or more above 100 km/h. This is not included in the RRC determination at 80 km/h and it will yield a contribution to f2 rather than f0.
  The results of the default table values study showed an approximately 40% correlation for variations of size and mass for both f0 and f2.
  Remaining unexplained effects occur.
  In general the dependency on the parameters included in the f0 and f2 equations will be weaker than initially assumed for downward extension. This can be captured in a generic “85%-rule” for calculation chassis dyno settings of vehicle L.

## Slide 19: OI #17: Default Road Load
  Extension (4) – 95%-rule for calculation chassis dyno settings vehicle H
  In general same considerations as for downward extension
  95%-rule:
  Safety margin comparable to downward extension would indicate 90%, but is based on analysis of limited data set of similar vehicles. Additional measurements available?
  Correlation might be higher for vehicles with more divergence in RR and body-shape.
  Selection of worst case Cd intended as a safety margin on air drag, but requires good knowledge at responsible authority.
  95% is considered conservative based on both data set, best-known physical dependencies (for upward extension) and uncertainties.
  Discussion in Annex 4 TF on correlation factors is on-going (in 0.9-1.0 range).
  Guidance of IWG on level of safety margin?

## Slide 20: OI #17: Default Road Load
Topic |  | ACEA | Annex 4 | IWG #11
1 | Definition „X-Factor“: |  |  | 
 | Upward | 0,9 | 1,0 | 0,95
 | Downward | 0,85 | 0,85 | 0,85
2 | Adoption of „Ligterink-Formular“ (Least square) |  |  | 
3 | Removal of Matrix in GTR |  |  | 
4 | Designed for GVW 3ton |  |  | 













## Slide 21
Proposed correlations for upward and downward extrapolation: conservative
OI #17: Default Road Load
TM |  | TML | Most selling | TMH
Vehicle Data | Name | NCV3 Nafta Sprinter |  | 
 | Picture |  |  | 
 | Load Volume [m³] | 7,5 m³ | 12 m³ | 17,7 m³
 | Frontal Area [m²] | 4,438 m² | 4,769 m² | 4,91 m²
 | Test Mass [kg] | 2948,348 kg | 3175,144 kg | 3628,736 kg
 | Rolling Resistance [kg/t] | 8,0 kg/t | 8,0 kg/t | 8,0 kg/t
Cycle Energy [MJ] | X= 1,0 | - | - | 29,442 MJ
 | X= 0,95 | - | - | 29,381 MJ
 | X= 0,9 | - | - | 29,320 MJ
 | X= 0,85 | 25,241 MJ | - | 29,259 MJ
 | X= 1,0 (IWG #10) | 24,883 MJ | - | 28,877 MJ
 | Coast Down (Measurement) | 25,051 MJ | 26,921 MJ | 29,087 MJ

## Slide 22
OI #17: Default Road Load
Penalty/ safety margin:
Δ + 0,355 MJ =
+ 3,2 g CO₂/km
TML
TMH
Downward extrapolation
Upward extrapolation
Penalty/ safety margin:
Δ + 0,19 MJ = + 2 g CO₂/km
Coast Down
Downward extrapolation
x = 0,85
Upward extrapolation
x = 1,00
Most selling
Road Load
Upward extrapolation x-Factor (x = 1,00)

## Slide 23
Upward extrapolation x-Factor (x = 0,95)
OI #17: Default Road Load
TML
TMH
Downward extrapolation
Upward extrapolation
Penalty/ safety margin:
Δ + 0,19 MJ = + 2 g CO₂/km
Coast Down
Downward extrapolation
x = 0,85
Upward extrapolation
x = 1,00
Upward extrapolation
x = 0,95
Most selling
Coast Down conditions:
Data coming from NAFTA (EPA-Methodology)
 Representative coast down data
Penalty/ safety margin:
Δ + 0,355 MJ =
+ 3,2 g CO₂/km
New proposal: x = 0,95
Penalty/ safety margin:
Δ +0,294 MJ = + 2,7 CO₂/km

## Slide 24
Upward extrapolation x-Factor (x = 0,95)
OI #17: Default Road Load
Penalty between upward & downward extrapolation guaranteed
TML: +2g CO₂/ km
TMH: +2,7g CO₂/ km

## Slide 25
Chart: 
| TMH - TML | TMH - Most Selling | TML - Most Selling | Most Selling - TML | Most selling - TMH
New(X= 0,85/0,9) | -0.9 | -0.1 | -0.2 | -1 | -1.2
Old
New(X= 0,85/0,95) | -0.9 | -0.1 | -0.4 | -1 | -1.4
New(X= 0,85/0,85)
New(X= 0,85/1,0) | -0.9 | -0.1 | -0.6 | -1 | -1.5
Extrapolation - Accuracy
Cycle Energy Matrix values vs. Coast Down [%]
Old  New (Calculation „Norbert Ligterink“ & Safety margin (0,85/0,95)
Downwards
Downwards
Downwards
Upwards
Upwards
Factor 0,85 penalty of 2 g CO₂/km
Factor 0,95 penalty of 2,7 g CO₂/km
Factor 1,0 penalty of 3,2 g CO₂/km
3,2g CO₂/km
Δ + 0,5 g CO₂/km
OI #17: Default Road Load

## Slide 26: OI #17: Default Road Load
  Extrapolation
  Different correlations for Upward (vehicle H) and Downward (vehicle L) extrapolation
  f0_new = (1-X)*f0 + (X)*(f0*(TM+DTM)/TM + 9.81*DRR*(TM+DTM))
  f2_new = (1-X)*f2 + (X)*f2*(Af+DAf) /Af
  Correlations:
  Xup = [0.95], for vehicle H
  Xdown = [0.85], for vehicle L

## Slide 27: OI #17: Default Road Load
  Calculation road load of vehicles H and L for chassis dyno setting and testing (1)
(New) 5bis Method for calculation of road load for vehicles H and L of a road load matrix family
5bis.1 For the calculation of the road load of vehicles H and L of a road load matrix family the vehicle parameters determined in paragraph 4.2.1.3 of this Annex and the road load coefficients of the representative test vehicle determined in paragraph 4.3 or 4.4 of this Annex shall be used.
5bis.2 The road load force for vehicle H shall be calculated using the following equation:
Fc = f0 + f1 x v + f2 x v2
where:
is the calculated road load force as a function of vehicle velocity, N;
is the constant road load coefficient, N, defined by the equation:
fo = [0.05] * f0r + [0.95] * ( f0r * TM/TMr + (RR - RRr)* 9.81 * TM)
is the first order road load coefficient and shall be equal to zero;
is the second order road load coefficient, N·(h/km)², defined by the equation:
f2 = [0.05] * f2r + [0.95] * f2r * Af / Afr

## Slide 28: OI #17: Default Road Load
  Calculation road load of vehicles H and L for chassis dyno setting and testing (2)
Continuation 5bis.2
V is vehicle speed, km/h;
TM test mass of vehicle H (determined in paragraph 4.2.1.3)
TMr test mass of the representative vehicle of the road load [matrix family]
Af …
Afr …
RR …
RRr …
f0r …
f2r …
5bis.3 The road load force for vehicle L shall be calculated using the following equation:
Fc = f0 + f1 x v + f2 x v2
where:
is the calculated road load force as a function of vehicle velocity, N;
is the constant road load coefficient, N, defined by the equation:
fo = [0.15] * f0r + [0.85] * ( f0r * TM/TMr + (RR - RRr)* 9.81 * TM)
is the first order road load coefficient and shall be equal to zero;

## Slide 29: OI #17: Default Road Load
  Calculation road load of vehicles H and L for chassis dyno setting and testing (3)
Continuation 5bis.3
is the second order road load coefficient, N·(h/km)², defined by the equation:
f2 = [0.15] * f2r + [0.85] * f2r * Af / Afr
V is vehicle speed, km/h;
TM test mass of vehicle L (determined in paragraph 4.2.1.3)
TMr test mass of the representative vehicle of the road load [matrix family]
Af …
Afr …
RR …
RRr …
f0r …
f2r …

## Slide 30: OI #17: Default Road Load
  Additional provisions – work in progress
Annex 6
1.2.3.1. General
Add to the end of paragraph 1.2.3.1: ….
1.2.3.2 CO2 interpolation range
Add to the end of paragraph 1.2.3.2: ….
Annex 7
3.2.4. Calculation of the CO2 value for an individual vehicle in a road load matrix family
Definitions of TM, RR, Af of both reference and individual vehicle
RL formulas
CO2 formulas

## Slide 31
 |  | Coastdown | Torque Meter | Wind Tunnel & Chassis Dynamometer, Flat Belt | Road Load Matrix Family | Default Road Load Formula | Tabulated dyno load settings (ECE R83)
Principle |  | Measurement |  |  | Measurement & Calculation | Calculation | 
Available in WLTP |  |  |  |  |  |  | -
Available in NEDC |  |  |  | - | - | - | 
Influence parameters | RR |  |  |  |  | - | -
 | TM |  |  |  |  |  | 
 | A |  |  |  |  |  | -
 | CD |  |  |  | Estimated worst case CD | - | -
WLTP trade-off test effort accuracy for heavy LCVs |  |  |  |  |  |  | -
Practical for heavy LCVs |  | Pos. | Pos. | Pos. |  |  | 





























accuracy
effort
accuracy
effort
accuracy
effort
RR: Rolling Resistance; TM: Test Mass; A: Frontal Area; CD: drag coefficient
accuracy
effort
accuracy
effort
OI #17: Default Road Load

## Slide 32: OI #17: Default Road Load
Option | Range covered | # of coast-down tests | Approach | Safeguard
Individual | 3% (time based statistical accuracy – §4.3.1.4.2) | 1 | Direct measurement | General test accuracy requirements
RL family | 5 MJ, 35% (38 g/km) | 2 (H,L) | Test + Least square fit + Interpolation: F0=f(ΔTM,ΔRR) F1=F1 F2=f(ΔCd*Af) | Correlation based on interpolation [can OEM give indication of correlation factors??]
RL matrix family | Limited by scope (3-3,5 ton) = approx. 60 g/km | 1 (represen- tative) | Test + Least square fit + ‘Extra’polation: F0=f(ΔTM,ΔRR) F1=0 F2=f(ΔAf) | Estimated worst case Cd Best available scientific insight f(ΔTM,ΔRR, ΔAf) Conservative correlation Chassis dyno testing H,L
Default calculation (Annex 4, § 5) | unlimited | 0 | Calculation F0=f(TMind) F1=0 F2=f(TMind, Afind) | Worst case (95%)

## Slide 33: OI #17: Default Road Load
  Time schedule:
  IWG#10: decision to proceed
  May 2015: preparation proposal in Annex 4 TF (Contracting Parties involved)
  IWG#11: initial draft gtr
  IWG#12: adoption

## Slide 34: OI #17: Default Road Load
  Updated To Do List (as of IWG#10):
  Appropriate name
  Confirmation of least square methodology to determine F0 and F2
  Selection of Upward and Downward correlation factors (conservative)
  Validation calculations new proposal
  Define selection representative Multi Stage Vehicle
  Definition of Multi Stage Vehicle in GTR or regional legislation
  If appropriate include drafting on CO2 calculation (Annex 7)
  Matrix to compare test burden vs. safeguard of RL determination options
Work in progress
All issues considered

## Slide 35: OI #17: Default Road Load
  Back-up slides

## Slide 36: OI #17: Default Road Load
 | Small |  |  | Medium |  |  | Large |  | 
Examples (small selection) | Peugeot Partner |  |  | Mercedes Vito |  |  | Mercedes Sprinter |  | 
 | VW Caddy |  |  | VW Transporter |  |  | VW Crafter |  | 
 | Mercedes Citan |  |  | Renault Trafic |  |  | Iveco Daily |  | 
 | Many more |  | . . . | Many more |  | . . . | Many more |  | . . .
Transport Volume | Low (2-5 m³) |  |  | Medium (5-7,5 m³) |  |  | High ( 7,5-17 m³) |  | 
Transport Payload | Low (< 1 ton) |  |  | Medium (0,5-1,2 ton) |  |  | High (1 - 5 ton) |  | 
TDL (ECE R83) | No |  |  | No |  |  | Yes |  | 
Certification | M1 - EURO6 | N1 Gr I, II - EURO6 |  | M1 - EURO6 | N1 Gr II, III EURO6 |  | M1,N1 Gr III EURO6 & EUROVI | M2,N2 EURO6 & EUROVI | 
The LCV Market:
Mercedes Sprinter Panel VAN : app. 4000 combinations are available
(Multistage vehicles not included)

## Slide 37: OI #17: Default Road Load
The LCV Market – Volume:
Chart: 
| M1 | M1 - ECE R83(³) | N1 - Coast Down | N1 - ECE R83(³) | N1/M1 - MSV - ECE R83(³)
Verkauf | 12 | 0.01 | 0.95 | 0.24 | 0.05
Remarks:
Data from 2013 im Mio
ECE R83 = tabulated dyno load settings (TDL)
Estimate TDL by Daimler:
  •Mercedes Sprinter
  •Renault Master
  •Ford Transit
  •VW Crafter
  •Citroen Jumper
  •Fiat Ducato
  •Iveco DAILY
0,95
0,24
0,05
N1 1,25
0,01
LCVs with tabulated dyno load settings (TDL), relative small market and segmented in 3 main groups:
TDL N1 Group III - Goods carrier
TDL N1,M1 - Multistage – Special Purpose vehicles
TDL M1 – Crew bus
2,3% Market Share
(0,3Mio vs 13,3 Mio)

## Slide 38: Multistage vehicles
OI #17: Default Road Load
Notes: [PLACEHOLDER TEXT]

## Slide 39: OI #17: Default Road Load
  Selection representative
  Multi Stage test vehicle
  List of topics:
  Build artificial vehicle or select completed vehicle?
  Selected Cd. [estimated worst case (completed vehicle) or square box (artificial vehicle)??]
  Selected TM. [TM = (M in running order of base vehicle with engine (chassis-cabin) + declared technically permissible laden mass)/2 ; >= 3000 kg]
  Selected Af and RR. [estimated average Af and RR ??]
  Maximum # of axis??
  Extrapolation range. [unlimited; 3-3.5 ton; widening regionally]