## Slide 1
RCDA for OVC-HEV (PHEV)
03.06.2015

## Slide 2
RCDA for OVC-HEV (PHEV).
Introduction and Current state.
► Background:
Requested to include an additional range in WLTP phase 1A – the actual charge-depleting range – RCDa.
RCDa is content of the current GTR 1A and would have to be calculated for the test cycle in EU (L+M+H+exH) and JP (L+M+H).
Additional request to calculate a RCDa,phase for each phase of the test cycle in phase 1B
RCDa,phase is not part of the GTR at the moment but the calculation was discussed and validated within SG EV.
As this value could mislead and/or confuse the customer, the proposal is to delete RCDa again.
► Objective:
Agreement whether the value RCDa is required by a contracting party or not.
► Extract from SG EV meeting minutes:
„[...] Position from EC and JP is expected to be available at the next meeting 22nd of June, there is a suggestion to discuss the issue before the next Subgroup EV meeting. [...]”

## Slide 3
RCDA for OVC-HEV (PHEV).
Overview of available ranges.
Values | WLTC (Low + Mid + High + exHigh) | WLTC JP (Low + Mid + High) | WLTC city (Low + Mid) | Low | Mid | High | exHigh | Explanation
RCDC | x | x |  |  |  |  |  | Charge-depleting cycle range is the distance driven over the amount of whole test cycles in the charge-depleting test. This value is only needed for further calculations.
AER | x | x | x |  |  |  |  | All electric range is the driven distance in the charge-depleting test until the ICE starts consuming fuel.
EAER | x | x | x | x | x | x | x | Equivalent all electric range represents the pure electrically driven distance under charge-depleting conditions until the electric storage is empty.
RCDA | ? | ? |  | ? | ? | ? | ? | Actual charge-depleting range represents the distance driven under charge-depleting conditions until the electric storage is empty.
The EAER and the RCDA are not determined by using a measured distance but are derived from the CO2 emission ratio under charge-depleting and charge-sustaining conditions.

## Slide 4
RCDA for OVC-HEV (PHEV).
Explanation of available ranges - pure electric type.
SOC
FC
ICE
On/Off
Chart: speed [km/h]
Chart: 
Chart: 
Chart: 
Transition cycle
First CD cycle
“CS confirmation cycle”
(n-1)th cycle
RCDC
AER
EAER
RCDA

## Slide 5
RCDA for OVC-HEV (PHEV).
Explanation of available ranges - blended type.
SOC
FC
ICE
On/Off
RCDC
AER
1
1
2
2
EAER1
EAER2
EAER3
EAER
RCDA
RCDA in case of blended vehicles can be higher than for pure electric type under charge depleting conditions. It is even higher than the EAER. This could mislead and/or confuse the customer.
Chart: speed [km/h]
Chart: 
Chart: 
Chart: 
Transition cycle
First CD cycle
“CS confirmation cycle”
(n-1)th cycle