## Slide 1: TASK FORCE ON AUTOMATED VEHICLE CATEGORISATION (TF-AVC)
Submitted by the Chairs of the Task Force on Automated Vehicle Categorisation (TF-AVC)
Informal document GRSG-128- XX
Informal 128th GRSG, 07 to 11 October 2024
Provisional agenda item XX
GRSG STATUS REPORT & INFORMAL DOCUMENT
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de

## Slide 2: TF-AVC progress
Established by 191st WP.29 (Nov 2023)
Meeting 1: Jan 2024 (online)
Meeting 2: Feb 2024 (online)
Meeting 3: March 2024 (hybrid)
  GRSG status report 1 presentation
Meeting 4: April 2024 (online)
Meeting 5: May 2024 (online)
  GRVA status report 1 presentation
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Meeting 6: June 2024 (hybrid)
  WP.29 status report 1 presentation
Meeting 7: July 2024 (online)
Meeting 8: September 2024 (online)
Meeting 9: October 2024 (hybrid)
  GRSG status report & informal document presentation
All relevant documents can be found on the TF-AVC UNECE Wikipage.
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 3: TF-AVC future look
Monthly meetings continue, planned until July 2025
Next meeting: hybrid in Shanghai, China (7th & 8th November 2024)
  Status report presentation to 194th session of WP.29 in November 2024
  Informal document to 21st session of GRVA in January 2025
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 4: R.E.3 – Category X
Categories, previously Category A, text remains unchanged
New section, aligned with text and format of R.E.3:
2.9. Category X
2.9.1. Definition.
Category X vehicles are vehicles of categories M, N, L and T meeting all of the following conditions:
(a) They are equipped with an ADS
(b) They are not capable of being driven manually at speeds exceeding 6 km/h
(c) They are designed to carry occupants
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 5: R.E.3 – Category Y
Categories, previously Category B
New section, aligned with text and format of R.E.3:
2.10. Category Y
2.10.1. Definition.
Category Y vehicles are vehicles of categories N, L and T meeting all of the following conditions:
(a) They are equipped with an ADS
(b) They are not capable of being driven manually at speeds exceeding [6] km/h.
(c) They are not designed to carry occupants at any time
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 6: R.E.3 – Combined designation
New section, aligned with text and format of R.E.3:
2.11. Combined designations
Symbols M, N, L and T may be combined with symbols G, X and Y, as applicable. For example, a vehicle of category N2 which meets the criteria of 2.10.1 may be designated as N2Y; a vehicle of category M1 which meets the criteria of 2.9.1 and is suited for off road use may be designated as M1GX.
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 7: R.E.3 – New Definitions
ADS and DDT definitions taken from FRAV/VMAD IWG
Definitions in [ ] are still to be discussed
1.16. "Automated Driving System (ADS)" means the vehicle hardware and software that are collectively capable of performing the entire Dynamic Driving Task (DDT) on a sustained basis.
1.17. "Dynamic Driving Task (DDT)" means the real-time operational and tactical functions required to operate the vehicle.
1.18. "Driver" means [...]
1.19. "Fallback user" means [...]
1.20. "Passenger" means [...]
1.21. "Occupant" means [...]
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 8: R.E.3 – Definition amendments
Minimal amendments required
References to ‘passengers’ replaced with ‘occupants’
Change references to the number of seating positions and passengers
Remove references to 'the driver'
2.2. Category M - Power-driven vehicles having at least four wheels and used for the carriage of passengers occupants
2.2.1. "Category M1": Vehicles used for the carriage of passengers occupants and comprising not more than eight seats in addition to the driver’s seat nine seats.
2.2.2. "Category M2": Vehicles used for the carriage of passengers occupants, comprising more than eight seats in addition to the driver’s seat nine seats, and having a maximum mass not exceeding 5,000 kg.
2.2.3. "Category M3": Vehicles used for the carriage of passengers occupants, comprising more than eight seats in addition to the driver’s seat nine seats, and having a maximum mass exceeding 5,000 kg.
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 9: R.E.3 – Mass of a vehicle in running order
Category X vehicles may have a driver in the vehicle (limited circumstances, at speeds not exceeding 6 km/h
Text is still to be discussed
2.2.5.4. "Mass of a vehicle in running order" means the mass of an unladen vehicle with bodywork, and with coupling device in the case of a towing vehicle, or the mass of the chassis with cab if the manufacturer does not fit the bodywork and/or coupling device, including coolant, oils, 90 per cent of fuel, 100 per cent of other liquids except used waters, tools, spare wheel, driver (75 kg) [if applicable], and, for buses and coaches, the mass of the crew member (75 kg) if there is a crew seat in the vehicle.
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 10: S.R.1 – Definition Amendments
Minimal amendments required
Change references to the number of seating positions and passengers
Remove references to 'the driver'
1. POWER DRIVEN VEHICLES WITH FOUR OR MORE WHEELS
1.1. "Category 1 vehicle" means a power driven vehicle with four or more wheels designed and constructed primarily for the carriage of (a) person(s).
1.1.1. "Category 1-1 vehicle" means a category 1 vehicle comprising not more than eight nine seating positions in addition to the driver’s seating position. A category 1-1 vehicle cannot have standing passengers.
1.1.2. "Category 1-2 vehicle" means a category 1 vehicle designed for the carriage of more than eight nine passengers, whether seated or standing, in addition to the driver.
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 11: S.R.1 – Category X and Y
New section, aligned with text and format of S.R.1:
4. [CATEGORY X AND Y] VEHICLES
4.1. “Category X vehicle” means a vehicle of category 1, 2 or 3 which:
i) is equipped with an ADS and
ii) is not capable of being driven manually at speeds exceeding 6 km/h and
iii) is designed to carry (a) person(s)
4.2. “Category Y vehicle” means a vehicle of category 2 or 3 which:
i) is equipped with an ADS and
ii) is not capable of being driven manually at speeds exceeding 6 km/h and
iii) is not designed to carry (a) person(s) at any time
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Notes: Future look:
Monthly meetings
First outcomes to WP.29 in June 2024
Next meeting online, 30 April
Agreed meeting schedule until June 2024, provisional meeting schedule until December 2024.

## Slide 12
Thank you, any questions?
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de

## Slide 13
Nov 24
Jul 24
Oct 24
7th Meeting
22nd July
(Online only)
8th Meeting
16th September
(Online only)
9th Meeting
1st & 2nd October
(Hybrid | Hamburg)
10th Meeting
7th & 8th November
(Hybrid | Shanghai)
Sep 24
Status Report and informal document presentation to
GRSG
7th – 11th October
Dec 24
11th Meeting
2nd December
(online)
Confirmed Meeting Schedule / Deliverables: Nov - Dec 2024
Status Report to
GRVA
23th – 27th September
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
Status Report to
WP.29
11th – 15th November

## Slide 14: Provisional Meeting Schedule / Deliverables: Jan - June 2025
May 25
Jan 25
Mar 25
12th Meeting
8th & 9th January
(hybrid)
13th Meeting
10th February
(online)
14th Meeting
10th March
(online)
Informal document
WP.29 - 195
(March)
Feb 25
Informal document to
GRVA
(20th – 24th Jan)
Formal document to GRSG (10th Jan)
Formal document
GRSG
(7th – 11th April)
Apr 25
Formal document
GRVA
(? - ? June)
15th Meeting
1st & 2nd April
(online)
16th Meeting
12th &13th May
(online)
17th Meeting
3rd & 4th June
(online)
Formal document to
GRVA
(14th Feb)

## Slide 15
Copyright 08/10/24, Chairs of TF-AVC, all rights reserved. For reproduction permission and all other issues, please contact geena.rait@dft.gov.uk and thies.weinand@kba.de
X: Informal document
X: Formal document
197
196