## Slide 1: Battery Master Switch (BMS)
and vehicles carrying explosives

## Slide 2: BMS and EX Vehicles Contents of Presentation
ADR: EX vehicles and the BMS.
Purpose of the BMS.
Electronic vehicle systems.
(Battery) Electric Vehicles.
Discussion and recommendations.

## Slide 3: ADR: EX vehicles and the BMS
ADR- two categories EX/II and EX/III – difference in max load mass.
Only EX/III requires a Battery Master Switch.
Requirement for BMS is going back a long time.
Background for BMS (probably) not retrievable.
IWG-Electric system:
– attempt to harmonize all vehicle provisions between all Cat. ->
- BMS not extended to EX/II due to uncertainties cost/benefits,
- difficult to implement on light commercial vehicles.

## Slide 4: Purpose of the BMS
Background (probably) not retrievable.
For FL vehicles the BMS is used to be safe in an area where an explosive atmosphere may occur.
For EX/III only compatibility group “J”may create such an atmosphere.
It is believed that the purpose for EX/III is safety against electrical fire when the vehicle is not driven.
This is supported by the provisions in 9.2.2.9 (Perman. energized): -9.2.2.9.2 (EX/III) only requires an unrestricted fuse or circuitbreaker.
-9.2.2.9.1 (FL) current limiter/very light fuse/circuit breaker.

## Slide 5: Electronic vehicle systems
Modern vehicles have an increasing number of electronic systems
Switching off these systems may created problems (memory)
Starting up these systems take time and may introduce faults.
Compliance with modern vehicle systems (e.g.Camera Monitoring systems/electric parking brake application).
Some systems need to maintain working.
- Anti theft devices - Tracking equipment

## Slide 6: Battery Electric Vehicles and Hydrogen Fuel Cell Vehicles
Battery Electric Vehicles (BEV) change the situation.
BEV’s have a Battery Management System – safety item to keep operational.
Temperature of battery needs to be controled (heated in cold climats).
Charging the Battery overnight.
High voltage traction system will disconnect when vehicle stops.
A low voltage system will remain (at least for the coming years).
Hydrogen Fuel cells need longer afterrunning time (in cold climates)

## Slide 7: Discussion and recommendations
Do we really need the BMS on EX vehicles?
Electrical installations improved – lower fire risks (GMC era)
Electronics are sensitive for de-energizing/re-energizing
Add on BMS (Light Commercial Vehicles/EX/II) after construction troublesome (CANBUS systems)
Justification EX/II no / EX/III yes.
Discussion and recommendation Explosives Group -> WP.15

## Slide 8
Thank you for your attention and input
Kees de Putter
kdeputter@rdw.nl
+31651582297