## Slide 1: Secondary LCA data selection
SG3 Meeting 10.9.2024
Notes: Short update on Secondary Data

## Slide 2: Overview data set selection criteria
Data set selection criteria’s secondary data :
  method consistency
  Selection based on data quality metrics
Not covered in the proposal :
  Source of data base to be preferred (e.g. whitelist, prescriptive, …)
  Primary vs. secondary data
Remark : presented in SG2 25.7.2024

## Slide 3: Criteria for Secondary Datasets
Proposal: method consistency + metric on data quality rating
Starting point – Data quality-requirements following ISO 14044/14067
According to 4.2.3.6.2 ISO 14044 The data quality requirements should address the following:
time-related coverage: age of data and the minimum length of time over which data should be collected;
geographical coverage: geographical area from which data for unit processes should be collected to satisfy the goal of the study;
technology coverage: specific technology or technology mix;
precision: measure of the variability of the data values for each data expressed (e.g. variance);
completeness: percentage of flow that is measured or estimated;
representativeness: qualitative assessment of the degree to which the data set reflects the true population of interest (i.e. geographical coverage, time period and technology coverage);
consistency: qualitative assessment of whether the study methodology is applied uniformly to the various components of the analysis;
Notes: Now what is meant when we speak about defined data quality criteria…
Relevant data criteria identified in the Catena-X Rulebook
Next method consistency

## Slide 4: Data set selection criteria
Method consistency :
Consistent Recycling /secondary material allocation, here: cut-off (input and output), no credits, no burden (not consistent: PCFs according to Battery regulation due to CFF)
• Infrastructure is not included in system boundary
• No use of consequential data
• Flow list compatible with IPCC AR6
• Compliance according to the standards below
  ISO 14040 and ISO 14044
  ISO 14067

## Slide 5: Data set selection criteria
The selection of secondary data shall be guided by the representativeness criteria
In cases of uncertainty, priority should be given to technology coverage, as it is the most critical factor for ensuring data representativeness.
Examples:
  Steel: route-specific data sets (BOF / EAF, DRI)
  Alu: differentiation primary/secondary route

## Slide 6: Decision Tree DATA SET
Level of accuracy
Selection of secondary LCA data
Best case scenario:
SM <= 3 ?
Select dataset
Yes
No
Appropriate
SM <= 3 ?
Select dataset
Yes
No
Choose alternative data with appropriate data quality as proxy
> 2
low
High
Notes: Draft decision Tree

## Slide 7: Secondary DATA metrics
Criteria addressing data quality | ISO 14040 / 14067 | Catena-X (v3.0) WBSC PACT 2.0 DQR | This proposal For DQR and selection criteria of dataset
time-related coverage: | X | X | X
geographical coverage | X | X | X
technology coverage: | X | X | X (prioritization as fall back - see decision tree)
completeness: | X | - | -
representativeness: | X | - | -
consistency: | X | - | X
DQR | - |  |