## Slide 1: Regulatory fitness for Automated Driving Systems
Status report
GRBP TF AVRS — GRE TF AVSR — GRE IWG EMC — GRPE TF AVRS — GRSG TF AVRS — GRSP TF AVRS — GRVA TF FADS
Informal document WP.29-194-xx
194th WP.29, 12 to 15 November 2024
Agenda item 2.3
Transmitted by the chairs of the expert groups on regulatory fitness for Automated Driving Systems

## Slide 2: Context and purpose (1/2)
ADS Regulatory readiness
Non-ADS Regulations
Relevant for ADS
Not relevant for ADS
ADS Regulations
Amendments needed
Amendments not needed
Contracting Parties and the industry need a regulatory environment for automated vehicles, including non-ADS Regulations
Which existing Regulations are relevant for automated vehicles? Which ones need to be amended before being applicable to ADS vehicles?
The WP.29 expert groups on regulatory fitness for ADS are screening and amending these relevant UN Regulations and GTRs
WP.29
GRBP
TF AVRS
GRE
IWG EMC
GRPE
TF AVRS
GRSP
TF AVRS
GRSG
TF AVRS
GRVA
TF FADS
IWG ADS
TF AVSR
Expert groups on regulatory fitness for ADS
TF AVC

## Slide 3: Context and purpose (2/2)
Report to WP.29 (WP29/2023/86):
Contains global results, summary sheets for each screened Regulations
Adopted by WP.29 (and GRVA/2023/18 endorsed by GRVA)
Has been updated and submitted as an informal document to the 192nd session of WP.29
Guidance received at the 192nd WP.29 session in March 2024
WP.29 welcomed the timeline presented for amending relevant Regulations by 2026
All groups may start drafting amendments to proposed “priority Regulations”
Coordination between groups shall continue for common definitions, translations and solutions to cross-GR issues, and the work should be coordinated with the IWG ADS and the TF AVC

## Slide 4: Activities since March 2024
Individually
GRBP TF AVRS proposed first informal documents for R28 and R138; now finalised for submission as working documents
GRE IWG EMC is starting preliminary work on the 8th series of amendments to R10, which will further improve ADS fitness
GRE TF AVSR submitted a working document for R48 to the 91st session of GRE
GRPE TF AVRS completed the screening of most Regulations under its purview
GRSG TF AVRS started amendments activities for R107 and R116
GRSP TF AVRS started amendment activities for its priority Regulations
GRVA TF FADS has prepared first full drafts of amendment proposals for R13 and R79
Collectively
Multiple joint meetings between leaders of the expert groups (June, September and October 2024)
Frequent participation and reporting of FADS and other expert groups to IWG ADS and TF AVC

## Slide 5: Reminder on screened Regulations – Updated screening results
GRBP | R9 | R28 | R30 | R41 | R51 | R54 | R59 | R63 | R64 | R75 | R92 | R106 | R108 | R109 | R117 | R124 | R138 | R141 | R142 | R164 | R165 | GTR16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
GRE | R1 | R3 | R4 | R5 | R6 | R7 | R8 | R10 | R19 | R20 | R23 | R27 | R31 | R37 | R38 | R45 | R48 | R50 | R53 | R56 | R57 | R65 | R69 | R70 | R72 | R74 | R76 | R77 | R82 | R86 | R87 | R88 | R91 | R98 | R99 | R104 | R112 | R113 | R119 | R123 | R128 | R148 | R149 | R150
GRPE | R24 | R40 | R47 | R49 | R68 | R83 | R84 | R85 | R96 | R101 | R103 | R115 | R120 | R132 | R133 | R143 | R154 | R168 | GTR2 | GTR4 | GTR5 | GTR10 | GTR11 | GTR15 | GTR17 | GTR18 | GTR19 | GTR21 | GTR22 | GTR23 | GTR24 |  |  |  |  |  |  |  |  |  |  |  |  | 
GRSG | R18 | R26 | R34 | R35 | R36 | R39 | R43 | R46* | R52 | R55 | R58 | R60 | R61 | R62 | R66 | R67 | R71* | R73 | R81* | R93 | R97 | R102 | R105 | R107 | R110 | R116 | R118 | R121 | R122 | R125* | R144 | R147 | R151* | R158* | R159* | R160 | R161 | R162 | R163 | R166* | R167* | R169 | GTR6 | GTR12
GRSP | R11 | R12 | R14 | R16 | R17 | R21 | R22 | R25 | R29 | R32 | R33 | R42 | R44 | R80 | R94 | R95 | R100 | R111 | R114 | R126 | R127 | R129 | R134 | R135 | R136 | R137 | R145 | R146 | R153 | R170 | GTR1 | GTR7 | GTR9 | GTR13 | GTR14 | GTR20 |  |  |  |  |  |  |  | 
GRVA | R13 | R13-H | R78 | R79 | R89* | R90 | R130* | R131* | R139 | R140* | R152* | R155 | R156 | R157 | R171 | GTR3 | GTR8* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | : | Regulation relevant and ready for fully automated vehicles (although improvements might be desirable)
 | : | Regulation relevant, not ready, and requires minor changes
 | : | Regulation relevant, not ready, and requires major changes
 | : | Regulation relevant (vehicles with occupants only), not ready, and requires minor changes
 | : | Regulation relevant (vehicles with occupants only), not ready, and requires major changes
 | : | Regulation not relevant for fully automated vehicles (*: must be handled by the ADS)
 | : | Regulation waiting to be screened
 | : | Regulation that entered into force after the end of the initial screening phase (June 2023)

## Slide 6: Reminder on screened Regulations – Priority Regulations
GRBP | R9 | R28 | R30 | R41 | R51 | R54 | R59 | R63 | R64 | R75 | R92 | R106 | R108 | R109 | R117 | R124 | R138 | R141 | R142 | R164 | R165 | GTR16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
GRE | R1 | R3 | R4 | R5 | R6 | R7 | R8 | R10 | R19 | R20 | R23 | R27 | R31 | R37 | R38 | R45 | R48 | R50 | R53 | R56 | R57 | R65 | R69 | R70 | R72 | R74 | R76 | R77 | R82 | R86 | R87 | R88 | R91 | R98 | R99 | R104 | R112 | R113 | R119 | R123 | R128 | R148 | R149 | R150
GRPE | R24 | R40 | R47 | R49 | R68 | R83 | R84 | R85 | R96 | R101 | R103 | R115 | R120 | R132 | R133 | R143 | R154 | R168 | GTR2 | GTR4 | GTR5 | GTR10 | GTR11 | GTR15 | GTR17 | GTR18 | GTR19 | GTR21 | GTR22 | GTR23 | GTR24 |  |  |  |  |  |  |  |  |  |  |  |  | 
GRSG | R18 | R26 | R34 | R35 | R36 | R39 | R43 | R46* | R52 | R55 | R58 | R60 | R61 | R62 | R66 | R67 | R71* | R73 | R81* | R93 | R97 | R102 | R105 | R107 | R110 | R116 | R118 | R121 | R122 | R125* | R144 | R147 | R151* | R158* | R159* | R160 | R161 | R162 | R163 | R166* | R167* | R169 | GTR6 | GTR12
GRSP | R11 | R12 | R14 | R16 | R17 | R21 | R22 | R25 | R29 | R32 | R33 | R42 | R44 | R80 | R94 | R95 | R100 | R111 | R114 | R126 | R127 | R129 | R134 | R135 | R136 | R137 | R145 | R146 | R153 | R170 | GTR1 | GTR7 | GTR9 | GTR13 | GTR14 | GTR20 |  |  |  |  |  |  |  | 
GRVA | R13 | R13-H | R78 | R79 | R89* | R90 | R130* | R131* | R139 | R140* | R152* | R155 | R156 | R157 | GTR3 | GTR8* |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pending final review of GRPE Regulations
R107
R11
R16
R21
R29
R17
R14
R28
R51
R138
R165
R10
R48
R13
R13H
R79
R94
R95
R100
R43
R160
R116
R141

## Slide 7: SUMMARY FOR REGS
GRBP: Bidirectional vehicles, is it too early to include in amendments? Should it first be taken to TF AVC?
PLEASE GIVE ANY RELEVANT SUMMARY FOR YOUR IMPORTANT REGS OR OTHER TOPICS OF INTEREST

## Slide 8: Horizontal topic 1 – Categories X/Y and scope of Regulations (1/6)
 | X (manual controls inside) | X (manual controls outside) | X (no controls) | Y (manual controls outside) | Y (no controls)
R12 |  |  |  |  | 
R35 |  |  |  |  | 
R39 |  |  |  |  | 
R43/GTR6 |  |  |  |  | 
R46 |  |  |  |  | 
R94 |  |  |  |  | 
R121 |  |  |  |  | 
R125 |  |  |  |  | 
Categories X and Y are currently defined as follows by the GRSG–GRVA TF AVC:
Category X | Category Y
Equipped with an ADS | 
Cannot be driven manually above 6 km/h | 
Designed to transport occupants | Not designed to transport occupants
Compatible with L, M, N and T | Compatible with L, N and T
Categories X and Y have been defined to allow for innovative, yet safe designs of automated vehicles.
ADS vehicles may offer a wide range of designs for limited manual controls compatible with these new categories: concealed or disabled traditional controls, joysticks, controllers, remote (within line of sight) control, etc.
Some UN Regulations and GTRs may exempt all vehicles of Category X and/or Y from their scope, while other Regulations may be partly applicable to X/Y vehicles depending on the kind of manual controls that can be used to control them at low speeds.
 | Fully applicable
 | Partly applicable
 | Not applicable

## Slide 9: Horizontal topic 1 – Categories X/Y and scope of Regulations (2/6)
Option 1: X and Y vehicles may apply for approvals to partly applicable Regulations, but are only subject to their relevant requirements.
R43
R46
R94
R13-H
M1
M1X
N1Y
R43 (simplified)
R46 (simplified)
R94
R13-H
R94 (leakage/spillage only)
R13-H
R137
R137
R137 (leakage/spillage only)
R43
R43 IF
R43 IF
Partial list for illustration purposes
Notes: R43 IF = If the vehicle is equipped with glazings, each glazing must comply (as an individual component) to the requirements of R43, even though transparency requirements of R43 are irrelevant for X and Y vehicles.

## Slide 10: Horizontal topic 1 – Categories X/Y and scope of Regulations (3/6)
Option 2: A specific General Safety Regulation and Passive Safety Regulation are created to gather basic safety requirements for X and Y vehicles.
R43
R46
R94
R13-H
M1
M1X
N1Y
NEW REG (general safety of vehicles of Category X)
R94
R13-H
NEW REG (crashworthiness of vehicles of Category Y)
R13-H
R137
R137
R43
R43 IF
R43 IF

## Slide 11: Horizontal topic 1 – Categories X/Y and scope of Regulations (4/6)
 | X | Y | Details
R35 | New Regulation | Exempted | R35 may partly apply to Category X vehicles if standard foot controls are fitted.
R43 |  | Exempted | If fitted on Category X or Y vehicles, glazings should comply with R43. Some basic installation requirements may apply to Category X vehicles with controls inside the vehicle.
R46 |  | Exempted | Vehicles of Category X with controls inside the vehicle should provide basic capabilities for indirect vision, although with a lower level of stringency than R46.
R121 |  | Exempted | Basic control / tell-tale requirements may apply to Category X when manually controlled at low speeds. Tell-tale requirements for other purposes (e.g. communication with passengers) are explored in Horizontal topic 3 of this presentation.
R125 R167 |  | Exempted | Vehicles of Category X with controls inside the vehicle should provide basic capabilities for direct vision, although with a lower level of stringency than R125 and R167.
R39 | Simplified | Simplified | Requirements on speedometer do not apply to X nor Y; requirements on odometer may apply to both X and Y.
R107 | Applies | Exempted | R107, as a Regulation on the general construction of buses and coaches, is not relevant for vehicles of Category Y.
R144 | Applies | Simplified | Some requirements are irrelevant or inapplicable to vehicles of Category Y (manual activation, references to airbags)
GTR6 | Simplified | Simplified? | Only two GTRs are currently under GRSG, so a new GTR may not be appropriate for GTR No. 6.
Recapitulative partial table of Option 2: General Safety Regulations
Notes: This table does not contain all GRSG Regulations, it only highlights some of those that offer the most significant interactions with Categories X and Y.

## Slide 12: Horizontal topic 1 – Categories X/Y and scope of Regulations (5/6)
 | X | Y | Details
R11 GTR1 | Applies | Exempted | The current scope of R11 only considers doors of compartments with occupants.
R12 | Simplified | Exempted | R12 only applies to some Category X vehicles (presence of a steering column).
R14 R16 R17 R25 R44 R80 R129 R145 GTR7 | Applies | Exempted | Regulations on seats, safety belts and their anchorages can only apply to vehicles with occupants.
R21 | Applies | Exempted | Interior fittings are only relevant for vehicles with occupants,
R29 R94 R95 R135 R137 R153 etc. | Applies | New Regulation | Only spillage and leakage requirements are relevant for Category Y. Basic compatibility requirements might also be desirable to ensure the protection of other vehicles and vulnerable road users.
R100 R134 GTR13 GTR14 GTR20 | Applies | Simplified | Requirements on the protection of occupants may not apply to Category Y.
Recapitulative partial table of Option 2: Passive Safety Regulations
Notes: This table does not contain all GRSG Regulations, it only highlights some of those that offer the most significant interactions with Categories X and Y.
The “New Regulation” proposed here is different from that of the previous slide. Additionally, most general and passive safety Regulations would not fall under these 2 new Regulations.

## Slide 13: Horizontal topic 1 – Categories X/Y and scope of Regulations (6/6)
Benefits of Option 1 | Benefits of Option 2
May be managed through supplements, without the need to formally mandate an IWG May reduce the administrative burden for Contracting Parties (no need to change mandatory Regulations in national / regional frameworks) | Reduced administrative burden for OEMs (fewer approvals to manage, clearer Regulations for both conventional and X/Y vehicles) Reduced procedural burden for WP.29 (one Regulation each for GRSG and GRSP) Opportunity to take a bottom-up approach to decide appropriate requirements for X/Y vehicles No misrepresentation of the meaning of approvals (e.g., a R94 approval is only possible when there are occupants to protect)
Based on their previous screening work and current amendment activities, the expert groups recommend the choice of Option 2.
The expert groups wish to highlight the importance of coordination: Option 2 should be chosen for both GRSG and GRSP, or for neither.
Notes: If WP.29 is favorable to Option 2, GRSG and GRSP will be consulted as to how to proceed with the creation of the 2 new Regulations (handled by the existing TF AVRS? Creation of a separate IWG?)

## Slide 14: Horizontal topic 2 – Non-DDT tasks of the driver (1/7)
Regulations contain many provisions where the role of the driver extends beyond the simple operation of the vehicle:
Regulation | Examples of non-DDT tasks of the driver
R11 | 2.9. "Door closure warning system" is a system that will activate a visual signal located where it can be clearly seen by the driver when a door latch system is not in its fully latched position and while the vehicle ignition is activated. 6.3.2. Each rear side door shall be equipped with at least one locking device which, when engaged, prevents operation of the interior door handle or other interior latch release control […]
R16 | 2.41. "Safety-belt reminder", means a system dedicated to alert the driver when any of the occupants do not use the safety-belt. The system is constituted by a detection of an unfastened safety-belt and by two levels of driver's alert: a first level warning and a second level warning.
R21 | 5.8.4.2. All rear-window, roof-panel and partition switches intended for use by occupants in the rear of the vehicle shall be capable of being switched off by a driver-controlled switch which is located forward of a vertical transverse plane passing through the R points of the front seats.
R100 | 6.14. Warning in the case of a thermal event within the REESS. The REESS or vehicle system shall provide a signal to activate the warning specified in paragraph 5.2.3. in the case of a thermal event in the REESS
These requirements mainly focus on informing the driver, or on making easier a task that is performed or initiated by the driver.

## Slide 15: Horizontal topic 2 – Non-DDT tasks of the driver (2/7)
Regulations contain many provisions where the role of the driver extends beyond the simple operation of the vehicle:
Regulation | Examples of non-DDT tasks of the driver
R107 Annex 3 | 7.5.7.1. […] in the event of activation of an alarm system: […] B) After a single positive action of the driver on any of the door controls in the driver’s compartment, all power-operated doors […] shall open and shall remain in the opened position. […]
 | 7.6.5.5. Where controls are provided for the driver to open and close a power-operated service door, they shall be such that the driver is able to reverse the movement of the door at any time during the closing or opening process.
R21 | 7.6.6.4.1. The driver shall be able to inhibit the automatic closing process by actuation of a special control. A passenger shall also be able to inhibit the automatic closing process directly by pressing a special push-button.
R100 | 7.6.10.6. When a passenger is standing on a power-operated retractable step, the corresponding door shall be incapable of being closed. […] This requirement shall not apply to any door within the driver’s direct field of view.*
 | 7.2.3.1. Space shall be provided in the driver's area, in a position clearly visible to the driver in his seating position, for the markings provided for in paragraph 3.3. of Annex 11**.
These requirements mainly focus on informing the driver, or on making easier a task that is performed or initiated by the driver.
*In other words, the driver is responsible for checking for the presence of passengers on retractable steps.
**Such as the maximum number of seated or standing passengers. In other words, the driver or crew member is responsible for checking the number of passengers inside the vehicle.

## Slide 16: Horizontal topic 2 – Non-DDT tasks of the driver (3/7)
Definitions taken from GRVA-18-50r1
“Automated Driving System (ADS)” means the vehicle hardware and software that are collectively capable of performing the entire Dynamic Driving Task (DDT) on a sustained basis.
“Dynamic Driving Task (DDT)” means the real-time operational and tactical functions required to operate the vehicle.
“Tactical function” means a capability to perceive the vehicle environment and control real-time planning, decision, and execution of manoeuvres, including conspicuity of the vehicle and its motion.
“Operational function” means a capability to control the real-time motion of the vehicle.
Currently, an ADS is only defined as a system capable of performing the dynamic driving task of the vehicle.
GRVA IWG ADS documents only require the ADS to “comply with traffic rules in accordance with application of relevant law within the area of operation“
concrete requirements explicitly mention an interaction with passengers:
  “Pursuant to a passenger request, the ADS shall bring the vehicle to a safe stop.*”
  “The ADS shall not initiate motion unless the safety risks to the passenger(s) have been mitigated”
  “An ADS that controls the operation of doors shall provide an emergency override to the user**”
  (another requirement in p. 37 will be developed as a separate horizontal topic)
*R107 may need to be amended to introduce the presence of a button or other user interface to make this stop request.
**This requirement is similar to R107 §7.6.6.4.1.

## Slide 17: Horizontal topic 2 – Non-DDT tasks of the driver (4/7)
Option 1: the ADS* is in charge of both DDT tasks and non-DDT, safety-relevant tasks. The ADS Regulation should contain requirements on how the ADS is evaluated on non-DDT tasks to ensure the safety of relevant vehicle users.
In non-ADS Regulations (e.g., R107), an ADS is assimilated to a human driver and can override non-DDT automatic actions (like the operations of doors).
Option 3: the ADS is in charge of only the DDT. Non-DDT tasks are to be handled through each Regulation as “automatic” functions, the safety of which must be demonstrated as part of the compliance with each Regulation.
In non-ADS Regulations (e.g., R107), an ADS is assimilated to automatic functions, independent from one another.
Option 2: the ADS* is in charge of both DDT tasks and non-DDT, safety-relevant tasks. Each Regulation shall ensure that the ADS reacts appropriately to the information transmitted through requirements of that Regulation.
Benefits of option 1: corresponds to existing requirements of the ADS Regulation (see examples 1 and 3 in the previous slide). Considers the ADS to be a full replacement of the driver in all aspects. Additional requirements that are not present in existing non-ADS Regulations can be created.
Benefits of option 2: a high level of safety is ensured in each Regulation. Each GR may define what is considered to be an “appropriate reaction” depending on the information transmitted to the ADS.
Benefits of option 3: non-DDT aspects of automated vehicles are tackled from the perspective of existing Regulations (a non-compliance in performing the DDT is separated from a non-compliance in operating doors).
Option 4: These tasks shall be covered under regional or national law.
*Including a vehicle user or remote operator designated as responsible in the safety concept of the ADS

## Slide 18: Horizontal topic 2 – Non-DDT tasks of the driver (5/7)
7.5.7.1. […] in the event of activation of an alarm system: […]
B) After a single positive action of the driver on any of the door controls in the driver’s compartment, all power-operated doors […] shall open and shall remain in the opened position. […]
Illustration with the following requirement of UN R107:
R107
Unchanged*
R ADS
New section: Non-DDT safety tasks
“The ADS shall respond appropriately to signals received from other vehicle systems”
Option 1
R107
“For vehicles equipped with an ADS, the manufacturer shall demonstrate that the ADS responds appropriately when the conditions for paragraph 7.5.7.1. are met.”
R ADS
Unchanged
Option 2
*In all four options, R107 should still be amended for ADS fitness purposes

## Slide 19: Horizontal topic 2 – Non-DDT tasks of the driver (6/7)
R107
Existing text of 7.5.7.1. B) +
“For vehicles equipped with an ADS, in the absence of a designated person responsible for the opening of doors, doors shall open automatically in accordance with NEW ANNEX”
NEW ANNEX based on existing annexes for electronic control systems (R79 Annex 6, R13-H Annex 8…)
R ADS
Unchanged
Option 3
R107
Unchanged
R ADS
Unchanged
Option 4
National laws
CP A: “In case of fire, all doors of an ADS vehicle shall open automatically ”
CP B: “In case of fire, the ADS shall open all power-operated doors […] ”
*Provisional shorthand for ”an ADS that does not issue system-initiated deactivation to manual driving”.

## Slide 20: Horizontal topic 2 – Non-DDT tasks of the driver (7/7)
Based on their previous screening work, current amendment activities and consultations with GRVA IWG ADS, the expert groups recommend the choice of Option 1 or Option 2
Option 1 could shift part of the workload from the fitness expert groups to the IWG ADS. Coordination would thus be required, especially regarding R107-adjacent requirements to ensure the safety of ADS used for public transportation.
Option 1 remains the only option that avoids at the same time:
Fragmented national ADS requirements, and
The inclusion of ADS requirements in non-ADS Regulations
Option 1 is also the only option that elaborates on the existing non-DDT requirements in ADS draft documents.
Options 2 and 3 would create a regulatory vacuum for automated vehicles that are not in the scope of R107, as no existing Regulation could be used as a reasonable basis to include some of the expected non-DDT requirements for vehicles of Categories not covered by R107. Furthermore, these options could inelegantly divide the ADS from its non-DDT tasks, even though current industry plans are to create ADS that may operate various aspects of vehicle operation beyond the DDT.

## Slide 21: Horizontal topic 3 – Communication with ADS users (1/4)
Passengers
R16
R48
R100
R121
Centralizes how tell-tales are displayed in the vehicle, what symbols to use, etc.
Each Regulation defines what information should be communicated with a warning / tell-tale, when warnings should be triggered, etc.
Driver
Reaction
Is informed, takes appropriate action when necessary, and gives instructions to passengers as appropriate
In a conventional (non-ADS) vehicle, nearly all information goes to the driver, who has full responsibility to react to regulatory vehicle or safety information (DDT-related or not), but also to communicate to passengers and to give instructions.

## Slide 22: Horizontal topic 3 – Communication with ADS users (2/4)
“The ADS vehicle shall provide safety-related information to the passengers.
Information related to the HMI’s indications:
Visual tell-tales, icons.
Auditory signals.
Haptic signals.”
R16
R48
R100
ADS
Reaction
Passengers
In an automated vehicle, information is transmitted directly to the ADS.
The ADS Regulation requires the ADS to provide safety-related information to passengers, but does not specify what information is relevant, when to provide it, how, and to whom.
GRVA-18-50r1 (p. 29)
Communication from the ADS to users depends on the criticality of the information and on user roles.
There is currently no requirement for the ADS to transmit any specific safety-relevant information defined in an existing Regulation.

## Slide 23: Horizontal topic 3 – Communication with ADS users (3/4)
Option 1: do not define any specific requirements for the transmission of information to users; this should be decided by the ADS, and communication strategies may be different from one ADS to another.
Option 2: each Regulation may introduce requirements for information directly to passengers when no driver is present in the vehicle.
Option 3: a master table defines expected transmission from the ADS to vehicle users. This table could be integrated in the ADS Regulation or a separate Regulation.
Regulation | Paragraph | Description of the information | Type of signal (visual / auditory / haptic) | Relevant users

## Slide 24: Horizontal topic 3 – Communication with ADS users (4/4)
Benefits of Option 1 | Benefits of Option 2 | Benefits of Option 3
No need to amend existing Regulations nor the ADS Regulation. OEMs are free to define any strategy for communicating with vehicle users. Allows for more innovation in ADS operation. | No need to amend a master table each time a new warning or information is added to any Regulation. Requirements for each kind of information can be more precisely drafted in each Regulation, rather than in a master table. Direct communication from the vehicle to the users, without transiting through the ADS. | Clear, harmonised guidance in one location for when and how the ADS should transmit information. Information comes from the ADS and not from the vehicle. Therefore, more advanced methods of delivery of information to users could be considered (vocal messages, etc.) A master table may also include information specific to the ADS performance of the DDT.
Based on their previous screening work, current amendment activities and consultations with GRVA IWG ADS, the expert groups recommend the choice of Option 1, although further research on this topic is desirable.
Furthermore, it remains possible to integrate guidance for communication with users in the future ADS interpretation document.

## Slide 25: Updated provisional planning of ADS-related submissions (Nov-24)
 | Jan-24 | Feb-24 | Mar-24 | Apr-24 | May-24 | Jun-24 | Jul-24 | Aug-24 | Sep-24 | Oct-24 | Nov-24 |  | Dec-24 | Jan-25 | Feb-25 | Mar-25 | Apr-25 | May-25 | Jun-25 | Jul-25 | Aug-25 | Sep-25 | Oct-25 | Nov-25 | Dec-25 | Jan-26 | Feb-26 | Mar-26 | Apr-26 | May-26 | Jun-26 | Jul-26 | Aug-26 | Sep-26 | Oct-26 | Nov-26 | Dec-26
GRBP |  | x |  |  |  |  |  |  | R28 R138 |  |  |  |  |  | x |  |  |  |  |  |  | x |  |  |  |  | x |  |  |  |  |  |  | x |  |  | 
GRE |  |  |  | 10R07 |  |  |  |  |  | x |  |  |  |  |  |  | R48 |  |  |  |  |  | 10R08 |  |  |  |  |  | 10R08 |  |  |  |  |  | x |  | 
GRPE | x |  |  |  | x |  |  |  |  | x |  |  |  | x |  |  |  | x |  |  |  |  | x |  |  | x |  |  |  | x |  |  |  |  | x |  | 
GRSG |  |  |  | R107 |  |  |  |  |  | AVC |  |  |  |  |  |  | R107 AVC |  |  |  |  |  | x |  |  |  |  |  | x |  |  |  |  |  | x |  | 
GRSP |  |  |  |  | x |  |  |  |  |  |  |  | x |  |  |  |  | x |  |  |  |  |  |  | x |  |  |  |  | x |  |  |  |  |  |  | x
GRVA | R13(H) R79 |  |  |  | x |  |  |  | x |  |  |  |  | R13(H) R79 AVC |  |  |  | R13(H) R79 AVC |  |  |  | ADS |  |  |  | x |  |  |  | x |  |  |  | x |  |  | 
WP29 |  |  | 192 |  |  | 193 |  |  |  |  | 194 |  |  |  |  | 195 |  |  | 196 |  |  |  |  | 197 |  |  |  | 198 |  |  | 199 |  |  |  |  | 200 | 
 | Informal document(s) Priority Regulation(s)
 | Working document(s) Priority Regulation(s)
 | Informal document(s) Non-priority Regulation(s)
 | Working document(s) Non-priority Regulation(s)
X symbols mark the usual schedule of GR sessions
Numbers such as 192 indicate WP.29 sessions
Dotted lines indicate usual deadlines for the submission of documents to WP.29
Pending final review of GRPE Regulations

## Slide 26: Summary of guidance requested to WP.29
Decisions or input for the three horizontal topics
  Categories X/Y and scope of Regulations
  Non-DDT tasks of the driver
  Communication with ADS users
Future interactions between the expert groups and IWG ADS (where should horizontal topics 2 and 3 be discussed? Are they part of the ADS mandate and/or FADS/AVRS mandates?)
Date of next update to WP.29: 195th session in March 2025 or 196th session in June 2025?
  Depends on guidance received on the item above

## Slide 27: Contact information
Group | Chair(s) | Secretary
GRBP TF AVRS | Netherlands (Jan Sybren BOERSMA) | oica (Shervin SOLHKONAN)
GRE IWG EMC | Germany (Zissis TSAKIRIDIS) | oica (Jean-Marc PRIGENT)
GRE TF AVSR | Germany (Karl MANZ) | gtb (Lukas Schwenkschuster)
GRPE TF AVRS | Netherlands (Niels DEN OUDEN) | avere (Banita FIDYOVA)
GRSG TF AVRS | Netherlands (Hans LAMMERS) | oica (Olivier FONTAINE)
GRSP TF AVRS | Germany (Rudolf GERLACH) | oica (Ansgar POTT)
GRVA TF FADS (and coordination with other expert groups) | China (Jiajie WU) France (Romain PESSIA) | clepa (Sébastien PATERNOTTE)