## Slide 1
WLTP, result calculation, v6
measured result is corrected by RCB, Ki, 14° test and interpolation.
BMW, Christoph Lueginger
23.09.2015
WLTP-12-08-rev1e

## Slide 2
please provide your feedback on that questions in Tokyo or in advance:
After options are selected and agreement is achieved, implementation and drafting will be done by the taskforce until GTR deadline.
WLTP Result Postprocessing Proposal
Dear Reader,
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
Question | EU | Japan | India | Korea | NGOs | autho-rities | received tendency up to now
Do you prefer to clarify that issue and provide a transparent process by the GTR (a) or do you want to leave it up to OEM and authority to solve that at the stage of the type approval (b)? |  |  |  |  |  |  | a
Do you prefer to simplify the final GTR text (which puts more effort in drafting until the deadline in 2 weeks) (a) or should we do an "endoscopic surgery" (b)? |  |  |  |  |  |  | a
Should HEV and CS be aligned as much as possible with ICE or do we accept a deviation. Option 1 or 2? |  |  |  |  |  |  | 2
Do you agree to leave out CD and OVC-HEVs (a) or should that be solved within phase 1b as well (b)? |  |  |  |  |  |  | a
Do you agree to that priority in the current proposal: 1. criteria emissions and CO2, 2. fuel consumption; (yes/no)? |  |  |  |  |  |  | yes

## Slide 3
WLTP Result Postprocessing Proposal
Current situation
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
 All GTR post-calculations have been developed regardless of other parts and issues.
 Some references are wrong, some results come to nothing, some results are bypassed.
 Also Calculation of EV issues is unclear, especially at which stage and where tests are averaged and how that is aligned with a declared value.

## Slide 4
FC combined value
declared value
WLTP Result Postprocessing Proposal
How values are connected (1)
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
CO2 combined
CO2 phase values
criteria emissions
FC phase values
Ki and regional corrections (e.g. 14° test)
averaging of tests

## Slide 5
FC combined value
declared value
WLTP Result Postprocessing Proposal
How values are connected (2)
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
CO2 combined
CO2 phase values
criteria emissions
FC phase values
Ki and regional corrections (e.g. 14° test)
averaging of tests

## Slide 6
FC combined value
declared value
WLTP Result Postprocessing Proposal
How values are connected (3)
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
CO2 combined
CO2 phase values
criteria emissions
FC phase values
Ki and regional corrections (e.g. 14° test)
averaging of tests

## Slide 7
WLTP Result Postprocessing Proposal
Challenges and open tasks
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
phase specific values
additive corrections
(step exchange will deliver
different results)
averaging of tests
influence of criteria
emissions on FC
declaration (alignment of
values like FC and phases
towards the declared value)
regional options
?
vehicle type | prior to IWG | IWG Tokyo, TARGET | until mid of October | TF-meeting | Final text | Phase II
conventional vehicle | proposal for order of steps, first drafting | agreement on steps | drafting of references and additional formulas | TBA | 18th of October | -
NOVC-HEVs, CS of OVC-HEVs, fuel cell | identification of steps and proposal for order | agreement on principle and steps | drafting of references and if necessary adaptions to Annex 8 | TBA | 18th of October | -
CD and combined values of OVC-HEVs |  | decide, if actions are needed | - | - | - | deal with that issue, if necessary
PEVs | not necessary |  |  |  |  | 
solution

## Slide 8
WLTP Postprocessing, V6: conventional
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
measurement, calculation of mass emissions [Annex 7, 3.]
test
RCB correction [Annex 6, App. 2]
RCB
calculation of fuel consumption values [Annex 7, 6.]
FC
Ki correction [Annex 6, App. 1]
Ki
Regional corrections (EU: ATCT 14°C test, DF) [e.g. EU Sub-Annex 6a]
regional
combined value (3-/4-phases, weighted by distance) [open  in new draft]
comb.
(
)
averaging of tests, declared value (regional?) [Annex 6, Japanese proposal]
AVG
interpolation method, rounding. (Europe  "CoC") [Annex 7, 3.2.3.]
vehicle
alignment of phase values [Annex 6, Japanese text proposal]
align
averaging of emissions L and H (?), final interpolation line [open  in new draft]
approval
phase
CO2
comb.
emiss.
phase
emiss.
phase
CO2
comb.
emiss.
phase
CO2
phase
FC
comb.
emiss.
phase
CO2
comb.
CO2
comb.
emiss.
phase
CO2
comb.
emiss.
phase
CO2
comb.
emiss.
phase
CO2
comb.
CO2
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
phase
FC
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
phase
FC
comb.
emiss.
1
3
8
6
4
5
2
9
7
inter-
mediate
comb. FC
comb.
CO2
comb.
CO2
comb.
CO2
comb.
CO2
10
phase
emiss.

## Slide 9
WLTP Postprocessing, V6: NOVC-HEV/CS OVC-HEV option 1
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
measurement, calculation of mass emissions
[Annex 7, 3.]
test
RCB correction [Annex 8, App. 2]
RCB
calculation of fuel consumption values
[Annex 7, 6.]
FC
Ki correction [no procedure for
NOVC/OVC-HEV defined  skip for HEVs]
Ki
Regional corrections (EU: 14°C test, DF)
[e.g. EU Sub-Annex 6a]
regional
combined value (3-/4-phases, weighted by distance)
[open  in new draft]
comb.
(
)
averaging of tests, declared value (regional?)
[Annex 6, Japanese proposal]
AVG
interpolation method, rounding. (Europe  "CoC")
[Annex 7, 3.2.3.]
vehicle
alignment of phase values
[Annex 6, Japanese text proposal, works for HEV?]
declare
averaging of emissions L and H (?), final interpolation line
[open  in new draft]
approval
phase
CO2
comb.
emiss.
phase
emiss.
phase
CO2
phase
CO2
phase
FC
comb.
emiss.
phase
CO2
comb.
CO2
comb.
emiss.
phase
CO2
phase
CO2
phase
CO2
comb.
CO2
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
phase
FC
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
phase
FC
comb.
emiss.
1
3
8
6
4
5
2
9
7
comb.
CO2
comb.
CO2
comb.
CO2
comb.
CO2
10
GTR rules the development of fuel consumption and CO2 correction coefficients. Hence, the fuel consumption has to be calculated in parallel, but…
1.) … no procedure defined to calculate Ki for NOVC-HEVs and OVC-HEVs.
2.) … no FC correction factor from the 14ºC test.
First an agreement is necessary how to proceed:
First option: Try to get the CS test in line with conventional vehicles. This needs time for agreements and amendments in Annex 8.
Second option: Separate postprocessing procedure.
Additionally we need a postprocessing procedure for:
1.) CD test for OVC-HEVs
2.) weighted values
3.) For ranges of OVC-HEVs and PEVs
4.) OVC-FCHVs?
Construction work: Averaging and declared value
comb.
emiss.
comb.
emiss.
comb.
emiss.
phase
emiss.
For fuel cells whole process is done with fuel consumption instead of CO2.
!

## Slide 10
WLTP Postprocessing, V6: NOVC-HEV/CS OVC-HEV option 2
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
measurement, calculation of mass emissions
[Annex 7, 3.]
test
RCB correction [Annex 8, App. 2]
RCB
calculation of fuel consumption values
[Annex 7, 6.]
FC
Ki correction [no procedure for
NOVC/OVC-HEV defined  skip for HEVs]
Ki
Regional corrections (EU: 14°C test, DF)
[e.g. EU Sub-Annex 6a]
regional
combined value (3-/4-phases, weighted by distance)
[open  in new draft]
comb.
(
)
averaging of tests, declared value (regional?)
[Annex 6, Japanese proposal]
AVG
interpolation method, rounding. (Europe  "CoC")
[Annex 7, 3.2.3.]
vehicle
alignment of phase values
[Annex 6, Japanese text proposal, works for HEV?]
declare
averaging of emissions L and H (?), final interpolation line
[open  in new draft]
approval
phase
CO2
phase
emiss.
phase
CO2
phase
CO2
phase
FC
phase
CO2
comb.
CO2
comb.
emiss.
phase
CO2
phase
CO2
phase
CO2
comb.
CO2
comb.
emiss.
phase
CO2
comb.
CO2
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
phase
FC
comb.
emiss.
phase
CO2
comb.
CO2
comb.
FC
phase
FC
comb.
emiss.
1
4
2
7
5
6
3
9
8
comb.
CO2
comb.
CO2
comb.
CO2
10
phase
FC
comb.
FC
GTR rules the development of fuel consumption and CO2 correction coefficients. Hence, the fuel consumption has to be calculated in parallel, but…
1.) … no procedure defined to calculate Ki for NOVC-HEVs and OVC-HEVs.
2.) … no FC correction factor from the 14ºC test.
First an agreement is necessary how to proceed:
First option: Try to get the CS test in line with conventional vehicles. This needs time for agreements and amendments in Annex 8.
Second option: Separate postprocessing procedure.
Additionally we need a postprocessing procedure for:
1.) CD test for OVC-HEVs
2.) weighted values
3.) For ranges of OVC-HEVs and PEVs
4.) OVC-FCHVs?
Construction work: Averaging and declared value
phase
FC
comb.
FC
phase
FC
comb.
FC
phase
FC
comb.
FC
phase
FC
comb.
FC
!
!
comb.
emiss.
comb.
emiss.
comb.
emiss.
phase
FC
comb.
FC
phase
emiss.
phase
emiss.
For fuel cells whole process is done with fuel consumption instead of CO2.

## Slide 11
WLTP Result Postprocessing Proposal
TODO-List
WLTP Postprocessing, Result Calculation, BMW, 23.09.2015
item | situation | task | status
1 | No agreed postprocessing procedure for ICE. | To be agreed / adopted. | proposal available
2 | No agreed postprocessing procedure for HEVs and CS. | To be agreed / adopted. | two options and proposal available
3 | Also table needed for PM PN? Annex 7, 3.3. Mass of particulate matter emissions Annex 7, 4. Determination of PN | To be clarified. | open
4 | If additive Ki is used for CO2, an alignment ( as for declared value issue) is necessary. | Draft formulas to Annex 6. | open
5 | RCB corrections provides FC correction as well. | Delete requirement, as FC is based on corrected CO2. | open
6 | References and formulas to be adapted to final proposal | Go through any of the paragraphs which are used for post calculation and: 1) change input reference 2) add formulas, if necessary (e.g. combined value instead of phases only) 3) change output reference | open
7 | declared value, alignment and distinction between fuel cell and HEV in that context | Check current draft and apply changes, if necessary. Use Japanese Annex 6 draft as far as possible. | open