## Slide 1: WLTP-12-17e
1
20.09.2015
Status report
about the work of the gearshift issues task force

## Slide 2: Progress made since WLTP IGM #11
2
At IWG #11 was decided to amend annex 1 and annex 2 as follows:
    Annex 1, section 3, add checksums of vehicle speed,
    Annex 1, section 7, add request to report detailed information about downscaling, if applied,
    Annex 2, add request for the calculation of the average gear.
These amendments were sent to the drafting coordinator and are already implemented in the latest draft of the GTR.
In addition to that the figures, showing the cycle traces were modified such as that they now show complete cycle phases per figure.

## Slide 3: Further amendments
3
Further amendments were done by the drafting coordinator:
    Annex 1, section 3.5, the sentence “At the option of the Contracting Party, the WLTC city cycle for Class 3a and 3b vehicles may be excluded” was added.
    Annex 2, section 2 (h), the sentence “The power curve shall be determined according to Regulation No. 85” was added.
Since the speed range for the determination of the WOT power curve is specified by the manufacturer according to ECE R 85, the minimum engine speed is higher than nidle in most cases. Therefore The following sentence needs to be added:

## Slide 4: Further amendments
4
    If the WOT power curve according to regulation 85 does not include nidle, Pwot(nidle) shall be determined by a suitable extrapolation.
Further necessary amendments:
  Annex 2, section 3.2 reads: “For each vj ≤ 1 km/h, it shall be assumed that the vehicle is standing still and the engine speed shall be set to n_idle. The gear lever shall be placed in neutral with the clutch engaged except 1 second before beginning an acceleration phase from standstill where first gear shall be selected with the clutch disengaged.”
The word “phase” needs to be deleted for clarity reasons, so that the 1. gear will be selected for the last second of a stop phase with v = 0.

## Slide 5: Further amendments
5
The gearshift calculation tool will be modified accordingly.
After IWG #11 the following issues remained on the OIL:
    Annex 1, section 1, vehicle classification, replace kerb mass by test mass,
    Annex 2, amendment of n_min_drive definition.
    According to point 1 it was agreed, that test mass and kerb mass data for a broad variety of vehicles should be sent to the task force leader for further analysis.
    The results for the data delivered so far are shown in figure 1. For each vehicle the range of the kerb mass and TML and TMH were delivered. The lowest kerb mass was combined with TML and the highest with TMH.

## Slide 6: Prated/mtest versus Prated/mkerb
6
Figure 1

## Slide 7: Vehicle classification
7
For M1 vehicles there is a quite good correlation between test mass and kerb mass with a common curve for TML and TMH.
The current borderlines between the vehicle classes (22 W/kg and 34 W/kg) could be replaced by 21 W/kg and 32 W/kg for the rated power to test mass ratio.
But this needs to be further evaluated by data from other OEMs.
Furthermore, the correlation curves for N1 vehicles are different for TML and TMH and the number of vehicles is by far not high enough in order to derive a sound solution.

## Slide 8: Vehicle classification
8
This means that the GS TF cannot provide a sound proposal to replace kerb mass by test mass for the vehicle classification.
And the replacement of kerb mass related borderlines by test mass related borderlines would not solve the problems of N1 manufacturers for vehicles with TMH around 3000 kg and a difference of up to 750 kg between TML and TMH.
These problems could be solved, if the application of downscaling would be decided based on vehicle H and not on vehicle L.

## Slide 9: Vehicle classification
9
There is one class 3 N1 vehicle in the gearshift prescription development database, where vehicle L woud not get any downscaling but vehicle H would get a downscaling factor of 8,6%.
Following the current GTR draft, vehicle H would have to drive the unmodified class 3b cycle, but would not be able to follow the trace, which would lead to a high percentage of WOT operation.
For such cases the downscaled cycle for vehicle H should be used in order to avoid unjudged burden.

## Slide 10: n_min_drive
10
The amendment of the determination of n_min_drive for gears > 2 was discussed in the GS TF since June 2014.
WLTP-GS-TF-31_n_min_drive_18082015m.pptx gives an overview of the discussions related to this issue till end of August 2015.
Unfortunately the GS TF could not agree upon a common amendment proposal.
Therefore the current definition of n_min_drive for gears > 2 should remain unchanged.

## Slide 11: Gearshift issues task force
11
This concludes the status report about the work of the gearshift issues task force.