## Slide 1: Final??? Review of WLTP Definitions
Bill Coleman – Tokyo Sept./Oct. 2015
WLTP-12-20e

## Slide 2: Agenda
The full set of definitions and proposed amendments are included in documents WLTP-12-11 and -12, these slides contain the points where the author sees a need for clarification.
Road Load
Modes
Electric Ranges
VPSD
Defeat Device
Back up
N.B. In the following slides, „Current“ = Text included in „WLTP-SG-Drafting-04-01e-GTR Version 28.07.2015.docx“

## Slide 3: 1. Road Load
3.2.11. "Road load" means the opposition to the movement of a vehicle. It is the total resistance if using the coastdown method or the running resistance if using the torque meter method.
3.2.13. "Running resistance" means the torque resisting the forward motion of a vehicle measured by torque meters installed at the driven wheels of a vehicle
3.2.14. "Simulated road load" means the road load calculated from measured coastdown data
3.2.18 "Target road load" means the road load to be reproduced on the chassis dynamometer.
3.2.19. "Total resistance" means the total force resisting movement of a vehicle, including the frictional forces in the drivetrain.

## Slide 4: 2. Modes 1a – coastdown, RCDC & UF
3.2.20. "Vehicle coastdown mode setting" means a mode system of operation enabling an accurate and repeatable determination of total resistance and an accurate dynamometer setting.
3.3.4. "Charge-depleting cycle range" (RCDC) means the distance from the beginning of the charge-depleting test to the end of the last cycle prior to the cycle or cycles satisfying the break-off criterion, including the transition cycle where the vehicle may have operated in both depleting and sustaining modes conditions.
3.3.26. "Utility Factors“ are ratios based on driving statistics depending on the […] range achieved in charge-depleting mode conditions and are used to weigh the charge-depleting and charge-sustaining exhaust emission compounds, CO2 emissions and fuel consumption for OVC-HEVs.

## Slide 5: 2. Modes 1b – coastdown, RCDC & UF
Justification
As the coastdown configuration should not be driver selectable (to avoid abuse or safety concerns) the use of the word mode contradicts the definition of mode.
As “setting” can also be a verb it may be possible to find a better term.
Question:
Should the utility factor definition refer to a specific range

## Slide 6: 2. Modes 2a - Predominant
3.5.10. "Predominant mode" for the purposes of this gtr means a single mode that is always selected when the vehicle is switched on regardless of the operating mode selected when the vehicle was previously shut down. It shall not be possible to redefine the predominant mode. The switch of the predominant mode to another available mode after the vehicle being switched on shall only be possible by an intentional action of the driver.
Justification:
The 2nd and 3rd sentences do not fit to a definition and should be integrated in the text of the gtr

## Slide 7: 2. Modes 2b - Predominant
Alternative:
3.5.10. "Predominant mode" for the purposes of this gtr means a single mode that is always selected when the vehicle is switched on regardless of the operating mode selected when the vehicle was previously shut down and cannot be redefined or switched to another mode without an intentional action of the driver.
It shall not be possible to redefine the predominant mode. The switch of the predominant mode to another available mode after the vehicle being switched on shall only be possible by an intentional action of the driver.

## Slide 8: 3. Electric Ranges
3.3.1. "All-electric range" (AER) means in the case of an off-vehicle charging hybrid electric vehicle (OVC-HEV) the total distance travelled by an OVC-HEV from the beginning of the charge-depleting test to the point in time during the test when the combustion engine starts to consume fuel.
3.3.2. "All-eElectric range" (AER) means in the case of a pure electric vehicle (PEV) the total distance travelled by a PEV from the beginning of the charge-depleting test until the break-off criterion is reached.
Justification:
We should not have one term defined with two definitions depending on the type of vehicle.

## Slide 9: 4. VPSD - 1
Proposal (new):
"Propulsion energy converter" means an energy converter of the powertrain, whose output energy is used directly or indirectly for the purpose of vehicle propulsion.“
"Category of propulsion energy converter" means (i) an internal combustion engine, or (ii) an electric machine, or (iii) a fuel cell.
Justification:
In line with VPSD
The term “energy converter” is not used in the gtr outside of definitions and so gives a painless link to VPSD and clear definitions
“Category” helps clarify other terms

## Slide 10: 4. VPSD - 2
Proposal (new):
"Propulsion energy storage system" means an energy storage system of the powertrain, whose output energy is used directly or indirectly for the purpose of vehicle propulsion.
"Category of propulsion energy storage system" means (i) a fuel storage system, or (ii) a rechargeable electric energy storage system, or (iii) a rechargeable mechanical energy storage system.
Justification:
In line with VPSD
Useful in other definitions for robustness but not used in gtr text
An energy storage system is not always part of the powertrain
“Category” helps clarify other terms

## Slide 11: 4. VPSD – 3a
Current:
"Auxiliaries" means additional equipment and/or devices not required for vehicle operation.
Proposal:
"Auxiliary devices" means energy consuming, converting, storing or supplying devices or systems which are installed in the vehicle for purposes other than the propulsion of the vehicle and are therefore not considered to be part of the powertrain.
"Peripheral devices" means energy consuming, converting, storing or supplying devices, where the energy is not primarily used for the purpose of vehicle propulsion, or other parts, systems and control units, which are essential to the operation of the powertrain.

## Slide 12: 4. VPSD – 3b
Current:
"Auxiliaries" ………
Proposal:
"Auxiliary devices" ……….
"Peripheral devices" …………..
Review of gtr to assess implications:
Auxiliaries shall be switched off or deactivated during dynamometer operation.
Propose no amendment necessary
Justification:
In line with VPSD

## Slide 13: 5. Defeat Device
Proposal:
3.5.7. "Defeat device" means any element of design which senses temperature, vehicle speed, engine rotational speed, drive gear, manifold vacuum or any other parameter for the purpose of activating, modulating, delaying or deactivating the operation of any part of the emission control system that reduces the effectiveness of the emission control system under conditions which may reasonably be expected to be encountered in normal vehicle operation and use. Such an element of design may not be considered a defeat device except if:
(a) The need for the device is justified in terms of protecting the engine against damage or accident and for safe operation of the vehicle; or
(b) The device does not function beyond the requirements of engine starting; or
(c) Conditions are substantially included in the Type 1 test procedures.

## Slide 14: Back up

## Slide 15: 6. PX (PM/PN) - 1
Proposal:
Include the following text in the definitions section only for clarification and not as a specific definition:
The term ‘particle’ is conventionally used for the matter being characterised (measured) in the airborne phase (suspended matter), and the term ‘particulate’ for the deposited matter.

## Slide 16: 6. PX (PM/PN) - 2
Current:
"Particle number" (PN) means the total number of solid particles emitted from the vehicle exhaust quantified according to the sampling and measurement methods as specified in this gtr.
Proposal:
"Particle number emissions" (PN) means the total number of solid particles emitted from the vehicle exhaust quantified according to the dilution, sampling and measurement methods as specified in this gtr.
Justification:
Consistency with PM definition

## Slide 17: 6. PX (PM/PN) - 3
Current:
"Particulate matter " (PM) means any material collected on the filter media from diluted vehicle exhaust;
Proposal:
"Particulate matter emissions" (PM) means the mass of any particulate material emitted collected on the filter media from the diluted vehicle exhaust quantified according to the dilution, sampling and measurement methods as specified in this gtr;
Justification:
Matter ≠ Mass
Consistency with PN definition

## Slide 18: 6. PX (PM/PN) - 4
Current:
"Mass of particulate matter" means the mass of PM quantified according to the sampling and measurement methods as specified in this gtr.
Proposal:
Delete
Justification:
No longer needed

## Slide 19: 6. VPSD - 1
Current:
"Electric machine" (EM) means an energy converter transforming electric energy into mechanical energy or vice versa
Proposal:
No change despite deviations from VPSD
Justification:
An electric machine is not always used for propulsion

## Slide 20: 6. VPSD - 2
Current:
"Energy converter" means the part of the powertrain where the form of energy input is different from the form of energy output.
Proposal:
"Energy converter" means a system where the form of energy output is different from the form of energy input.
Justification:
In line with VPSD
An energy converter is not always part of the powertrain

## Slide 21: 6. VPSD - 6
Current:
"Energy storage system" means the part of the powertrain on board a vehicle that can store energy and release it in the same form as it was input.
Proposal:
"Energy storage system" means a system which stores energy and releases it in the same form as was put in.
Justification:
In line with VPSD
An energy storage system is not always part of the powertrain

## Slide 22: 6. VPSD - 5
Current:
-
Proposal:
“Form of energy” means (i) electrical energy, or (ii) mechanical energy, or (iii) chemical energy (including fuels).
Justification:
Conceptually in line with VPSD (although not included)
Helps clarify other terms

## Slide 23: 6. VPSD - 8
Current:
-
Proposal:
"Fuel storage system" means a propulsion energy storage system that stores chemical energy as liquid or gaseous fuel.
Justification:
In line with VPSD
An energy storage system is not always part of the powertrain

## Slide 24: 6. VPSD - 10
Current:
-
Proposal:
"Fuel cell" means an energy converter transforming chemical energy (input) into electrical energy (output) or vice versa.
Justification:
In line with VPSD
An energy storage system is not always part of the powertrain