## Slide 1: TF AVRS-08-04_R51
TF AVRS
Fully depress the accelerator vs full acceleration command
Test mass for AV:s with no driver seat
Definition of AV:s

## Slide 2: Accelerator/acceleration command
3.1.2.1.5. Acceleration test
The manufacturer shall define the position of the reference point in front of line AA' of fully depressing the accelerator. The accelerator shall be fully depressed (as rapidly as is practicable) when the reference point of the vehicle reaches the defined point. The accelerator shall be kept in this depressed condition until the rear of the vehicle reaches line BB'. The accelerator shall then be released as rapidly as possible. The measurement reading shall not end before the rear of the vehicle is 20 m behind the BB' line. The point of fully depressing the accelerator shall be reported in Addendum to the Communication form (Annex 1, Appendix 1). The Technical Service shall have the possibility of pretesting.
Original
Fully depressing the accelerator = full acceleration is applied
The accelerator shall be kept = The full acceleration demand shall be kept
The accelerator shall then be released = The acceleration demand shall then be ended
Are these sentences interchangable?
Could the proposed changes lead to different interpretations compared to the original text when testing regular vehicles?
Current proposal
Introducing def of Accelerator
(acceleration pedal  accelerator
Change main text to cover AV:s and regular vehicles
2.33 “Accelerator” means the acceleration command (f.ex. the acceleration pedal for manually driven vehicles
3.1.2.1.5. Acceleration test
The manufacturer shall define the position of the reference point in front of line AA' from which full acceleration is applied. The full acceleration shall be applied (as rapidly as practicable) when the reference point of the vehicle reaches the defined point. The full acceleration demand shall be kept until the rear plane of the vehicle reaches line BB'. The acceleration demand shall then be ended as rapidly as possible. The measurement reading shall not end before the rear of the vehicle is 20 m beyond behind the BB' line. The point from which full acceleration is applied shall be reported in Addendum to the Communication form (Annex 1, Appendix 1). The Technical Service shall have the possibility of pretesting.

## Slide 3: Accelerator/acceleration command
2.33 “Accelerator” means the acceleration command (f.ex. the acceleration pedal for manually driven vehicles
3.1.2.1.5. Acceleration test
The manufacturer shall define the position of the reference point in front of line AA' from which full acceleration is applied. The full acceleration shall be applied (as rapidly as practicable) when the reference point of the vehicle reaches the defined point. The full acceleration demand shall be kept until the rear plane of the vehicle reaches line BB'. The acceleration demand shall then be ended as rapidly as possible. The measurement reading shall not end before the rear of the vehicle is 20 m beyond behind the BB' line. The point from which full acceleration is applied shall be reported in Addendum to the Communication form (Annex 1, Appendix 1). The Technical Service shall have the possibility of pretesting.
3.1.2.1.5. Acceleration test
The manufacturer shall define the position of the reference point in front of line AA' of fully depressing the accelerator. The accelerator shall be fully depressed (as rapidly as is practicable) when the reference point of the vehicle reaches the defined point. The accelerator shall be kept in this depressed condition until the rear of the vehicle reaches line BB'. The accelerator shall then be released as rapidly as possible. The measurement reading shall not end before the rear of the vehicle is 20 m behind the BB' line. The point of fully depressing the accelerator shall be reported in Addendum to the Communication form (Annex 1, Appendix 1). The Technical Service shall have the possibility of pretesting.
Original
Current proposal
Introducing def of Accelerator
(acceleration pedal  accelerator
Change main text to cover AV:s and regular vehicles
New proposal?
Keep the original text in main body
Add a ”translation table in Annex 10”
Accelerator | The acceleration command
Fully depressing the accelerator | Full acceleration is applied
Keeping accelerator | 

## Slide 4: Mass of the driver for AVs
2.4. "Mass of a vehicle in running order (mro)" means
The mass of the vehicle, with its fuel tank(s) filled to at least 90 per cent of its or their capacity/ies, including the mass of the driver, of the fuel and liquids, fitted with the standard equipment in accordance with the manufacturer's specifications and, when they are fitted, the mass of the bodywork, the cabin, the coupling and the spare wheel(s) as well as the tools;. If there is no driver seat in the vehicle, the mass of the driver shall not be included
Repeated in:
2.2.2.2 …
2.2.2.3.1…
2.2.2.3.2…
2.2.2.3.4
2.4. "Mass of a vehicle in running order (mro)" means
The mass of the vehicle, with its fuel tank(s) filled to at least 90 per cent of its or their capacity/ies, including the mass of the driver, of the fuel and liquids, fitted with the standard equipment in accordance with the manufacturer's specifications and, when they are fitted, the mass of the bodywork, the cabin, the coupling and the spare wheel(s) as well as the tools;. If there is no driver seat in the vehicle, the mass of the driver shall not be included
2.2.2.1
Measurements shall be made on vehicles at the test mass mt specified according to the Table 2 below. If there is no driver seat in the vehicle, the mass of the driver shall not be included in the subsequent calculations
Current proposal
New proposal?

## Slide 5: Definition of AV:s
There is no defintion of AV:s in the current proposal
The term is however used in
  Annex 3, 3.1.2.1.4.1
  Annex 10
Two options:
Introduce a definition in chapter 2. ”AV:s means a vehicle equipped with an ADS”
Use ”vehicles equipped with an ADS” where needed