## Slide 1: Regulatory fitness for Automated Driving Systems
Information
GRBP TF AVRS — GRE TF AVSR — GRE IWG EMC — GRPE TF AVRS — GRSG TF AVRS — GRSP TF AVRS — GRVA TF FADS
ADS-07-13
7th meeting of GRVA IWG ADS,
17 to 21 March 2025
Transmitted by the chairs of the expert groups on regulatory fitness for Automated Driving Systems

## Slide 2: Non-DDT tasks of the driver – Background
Regulations contain many provisions where the role of the driver extends beyond the simple operation of the vehicle:
Regulation | Examples of non-DDT tasks of the driver
R11 | 2.9. "Door closure warning system" is a system that will activate a visual signal located where it can be clearly seen by the driver when a door latch system is not in its fully latched position and while the vehicle ignition is activated. 6.3.2. Each rear side door shall be equipped with at least one locking device which, when engaged, prevents operation of the interior door handle or other interior latch release control […]
R13 | 5.2.1.11.2.1. “It shall be possible to easily assess this wear on service brake linings from the outside or underside of the vehicle, without the removal of the wheels, by the provision of appropriate inspection holes or by some other means. This may be achieved by utilizing simple standard workshop tools or common inspection equipment for vehicles. Alternatively, a sensing device per wheel. […], which will warn the driver at his driving position when lining replacement is necessary, is acceptable […]”
R16 | 2.41. "Safety-belt reminder", means a system dedicated to alert the driver when any of the occupants do not use the safety-belt. The system is constituted by a detection of an unfastened safety-belt and by two levels of driver's alert: a first level warning and a second level warning.
R21 | 5.8.4.2. All rear-window, roof-panel and partition switches intended for use by occupants in the rear of the vehicle shall be capable of being switched off by a driver-controlled switch which is located forward of a vertical transverse plane passing through the R points of the front seats.
R107 | 7.5.7.1. […] in the event of activation of an alarm system: […] B) After a single positive action of the driver on any of the door controls in the driver’s compartment, all power-operated doors […] shall open and shall remain in the opened position. […]
These requirements mainly focus on informing the driver, or on making easier a task that is performed or initiated by the driver.

## Slide 3: Communication with ADS users – Background
“The ADS vehicle shall provide safety-related information to the passengers.
Information related to the HMI’s indications:
Visual tell-tales, icons.
Auditory signals.
Haptic signals.”
R16
R48
R100
ADS
Reaction
Users
In an automated vehicle, all DDT-relevant information is transmitted directly to the ADS.
The ADS Regulation requires the ADS to provide safety-related information to passengers,
but does not specify what information is relevant, when to provide it, how, and to whom.
GRVA-18-50r1 (p. 29)
Communication from the ADS to users depends on the criticality of the information and on user roles.
There is currently no requirement for the ADS to transmit any specific safety-relevant information defined in an existing Regulation.

## Slide 4: Non-DDT tasks and communication with users – Process
UNR ADS
GTR ADS
List of non-DDT tasks
From document FADS-J3-03r1
Expert groups on regulatory fitness for ADS
Small team of experts
Led by EC
List of signals from vehicle systems
From document GRSP-TF-AVRS-10-2
New high-level, general requirements, e.g. (TBD):
“The ADS shall respond appropriately to signals received from other vehicle systems…”
“Any non-DDT task shall be documented…”
“The vehicle shall enable usual PTI operations…”
1
2
Provide experts
Provides experts
3
IWG ADS
If accepted
(Horizontal Topic 3)
(Horizontal Topic 2)
Feb.-Mar. 2025
Apr. 2025
Mar.-Apr. 2025
Transmit proposal

## Slide 5
Reacting to signals received from other vehicle systems | Regulated, directly related to DDT | E.g., Braking, Steering, Lighting, Powertrain, TPMS
 | Regulated, not directly related to DDT | E.g., Fire / smoke in a compartment (bus / coach), Safety belt unfastened (if applicable), Anti-theft, …
 | Not regulated | E.g., Fire / smoke in a compartment (light duty vehicle) or in the batteries system, Sensors, Opening of emergency exits, …
Reacting to signals received from remote systems | E.g., On-board or remote operator stop request, ADS deactivation order from on-board or remote operator, Proposal manoeuvres / execute on-board or remote operator's choice… | 
Strategic functions | E.g., Setting an itinerary, Reacting to on-board or remote operator's modifying an itinerary during operation | 
Giving information to… | Passengers | E.g., Intention to place vehicle in an MRC, Informations for safe operation, Emergency manœuvres (?)
 | Users at the station | E.g., Intention to move, to park, to stop, to close doors…
 | Remote operation centre or on board operator | E.g., Emergency manoeuvres, Intention to place vehicle in an MRC, Status of the vehicle, status of the ADS, …
 | ORU | E.g., Emergency manoeuvres, Intention to place vehicle in an MRC, Status of the ADS
 | Law enforcement & first responders | E.g., Allowing the communication between operators (remote or on-board) and law enforcement officers, Status of the ADS
Providing assistance to passengers | Call and communication with remote intervention operator | 
Checking the correct operating conditions of the vehicle | Before driving (vehicle stopped) | E.g., Brake wear, Tyre wear/tear, pressure, etc., Fluids levels, Lamps operation, angle, Trailer correctly coupled, Energy level, …
 | While driving | E.g., Broken window, body damage or other safety hazard for occupants or other road users, …
Checking passenger / occupant safety | Before starting to drive | E.g., Safety belts fastened (if applicable), Number of passengers compatible with vehicle capacity, …
 | While driving | E.g., Safety belts unfastened (if applicable), Standing passengers (in vehicles not designed for standing passengers), …
Operating safely, non-DDT related tasks | Of the vehicle | E.g., Doors and door locks (doors can be operated automatically, or operated by the on-board or remote operator, or operated locally by the passengers), Windows and window locks, Folding roof, retractable hardtop, panoramic roof, …
 | Outside of the vehicle | E.g., Equipment for loading and unloading, Signalization devices, mobile equipment (fences, doors,..)
Non-DDT tasks and communication with users – Synthesis

## Slide 6: Misc. issue No. 1 – ADS Features of Type 1 and Type 2
3.34. “System-initiated deactivation of the ADS” means a procedure by which the ADS initiates the transfer of performance of the DDT from the ADS to a vehicle fallback user.
5.2.2.6. While active, features that have a system-initiated deactivation of the ADS to a fallback user shall: …
ADS-06-04r1
The expert groups wish to be able to differentiate:
“ADS features that have a system-initiated deactivation of the ADS to a fallback user”
from
“ADS features that do not have a system-initiated deactivation of the ADS to a fallback user”
Given the fact that these definitions are already in ADS-06-04r1, the expert groups simply propose to define them as ‘’Type-1 ADS features’’ (ADSF 1) and ‘’Type-2 ADS features’’ (ADSF 2) respectively.
Regulation | Relevant use of ADSF 1 and 2
R174 (safety belt reminder) | Vehicles equipped with ADSF 2 shall provide the SBR warning to occupants.
R11 (door closure warning) | Vehicles equipped with ADSF 2 shall provide the door closure warning to occupants.
R121 (controls, tell-tales and indicators) | While an ADSF 2 is active, occupants shall not be informed by DDT-related tell-tales and indicators. While an ADSF 1 is active, displaying DDT-related tell-tales and indicators is optional.
R107 (construction of buses & coaches) | For vehicles equipped with an ADSF 2, every door shall be so constructed that its opening movement is not likely to cause injury to passengers in normal conditions of use.
Link to more relevant requirements (GRSP examples)

## Slide 7: Misc. issue No. 2 - Performance of the DDT by ADS and other systems
From ADS-06-04
Current consensus in GRVA TF FADS is that other systems might contribute to the DDT at the same time as the ADS.
This is the case in particular for ESC/ABS, where the industry has indicated that some vehicles will keep an ESC that could override ADS performance of the DDT to maintain vehicle stability. The ESC may be approved to R140 and may be independent from the ADS.
This seems to be incompatible with ADS-06-04 where the entire DDT must be performed by the ADS.
2.7. "Electronic Stability Control (ESC) System" means a system that has all of the following attributes:
2.7.1. That improves vehicle directional stability by at least having the ability to automatically control individually the braking torques of the left and right wheels on each axle to induce a correcting yaw moment based on the evaluation of actual vehicle behaviour in comparison with a determination of vehicle behaviour demanded by the driver;
…
From UN R140

## Slide 8: Misc issue No. 3 – Activation status of ADS and ADS features
Based on the current text of ADS-06-04r1, one can draw the following conclusions:
If a vehicle is equipped with an ADS, the ADS is always active, even if no ADS feature is activated. (ADS-06-04r1 5.2.1.1., etc.)
A vehicle equipped with an ADS must have at least one ADS feature (ADS-06-04r1 5.1.1., etc.)
The possible states of an ADS are therefore ‘’ADS active, but no ADS feature is active‘’ and ‘’ADS active, and an ADS feature is active’’.
However, there seem to be some inconsistencies with other requirements of ADS-06-04r1:
1) 3.2. “ADS fallback response” means a system-initiated deactivation of the ADS or an ADS-controlled procedure…
2) 3.34. “System-initiated deactivation of the ADS” and 3.37. “User-initiated deactivation of the ADS”
3) 5.1.4.4.2. Remote termination of an ADS or ADS feature(s) …
4) 5.2.3.8. The ADS shall provide a specific indication of the completion of the deactivation of the ADS.
5) 5.2.5.1. (c) Instructions for the activation and deactivation of the ADS, with clear explanations of the distinctions between user-initiated deactivation and system-initiated deactivation where applicable
6) 7.2.7.2.1. …or that the ADS cannot be activated outside its ODD, where applicable.
For reference, UN R171 on DCAS has a more detailed management of the different states of the system