## Slide 1: Status update on Chapter 3: Terms and definitions
17-21 March 2025, Petten

## Slide 2: Issues
“ADS feature”
  Proposals for “Type 1” and “Type 2”
Updates to “occurrence” definitions
Deactivation
  “process/procedure”, “initiation”, “transfer”, etc.
Scenarios and situations
  “Scenario” used 150+ times, “situation” 75+ times, interchangeably and variably
  Nominal, critical, and failure scenario categories
    Ambiguous definitions and fitness for purposes
  Complex scenario
Safety case, concept, argument, claim, evidence
  “Case” used 90+ times to mean different things in different contexts
“User” terms
Manufacturer: Definition proposal
“Authority”, “Competent authority”, etc.: Resolve open issue for referring to authorities, assessors, etc.

## Slide 3: ADS feature
FADS-J4-02 (Joint meeting of AV screening groups)
ADS feature of Type 1 (ADSF1)
  ADS feature that has a system-initiated deactivation of the ADS to a fallback user. Only use if needed.
ADS feature of Type 2 (ADSF2)
  ADS feature that does not have a system-initiated deactivation of the ADS to a fallback user. Only use if needed.
3.3. “ADS feature” means an application of an ADS designed specifically for use within an Operational Design Domain (ODD).
Issues
A feature is defined by its ODD. “Feature” defined to address ADS operating in more than one ODD. Could these definitions adversely impact the aim to assess each ADS feature?
Nothing prohibits a feature from operating with or without a fallback user within the ODD. The definitions assume one or the other but not flexibility to do both. Does this violate the principle of technological neutrality?

## Slide 4: Occurrence
Added criteria
  d) Injury/fatality as a result of being in the ADS vehicle or being involved in the event
  e) Normal operations which are relevant to argument specific ADS design choices and/or the safety case.
Issues
Why add more criteria to “occurrence”? It seems that an occurrence is any safety-relevant event and that a “critical occurrence” is an event with a collision, injury, airbag deployment, etc. Are these reportable occurrences only? It seems more logical for “occurrence” to be general and then “critical/significant occurrence” to be a subset of occurrence.
Item (e) introduces new and undefined concepts. What are “normal operations”, “design choices”, and “relevant to…the safety case”? It seems ambiguous and open-ended. How is a “normal operation” an “occurrence”? The definition needs to be grounded in explicit and objective sources (e.g., specific paragraphs where, say, “normal operations” have been identified) that provide the basis for determining whether something qualifies as an “occurrence”.

## Slide 5: Critical Occurrence
Editorial improvements
Added criteria
  (c) Any vehicle involved in the event experiences a deployment of any non-reversible occupant restraint system, vulnerable road user secondary safety system or the delta-V thresholds to be met, whichever occurs first.
Issues
“VRU secondary safety system” needs to be defined.
Where does the regulation specify “delta-V thresholds”?
Why would it matter “whichever occurs first”?

## Slide 6: Significant Occurrence
“Significant Occurrence” means occurrences which are not “Critical Occurrences”, but require to be reported on short term basis due to their relevance on safety
  Replaces “non-critical occurrence”
Issues
Confuses definition with requirement. Where does the regulation provide the list of “significant occurrences” required to be reported? Is there a “significant occurrences” subsection that defines the reporting requirement?
As written, the term is ambiguous. Where is the threshold implicit in “due to their relevance to safety” provided?
Depending upon its use in the regulation, it might be clearer to specific the reporting requirement(s). For example, “Significant occurrence” means an occurrence subject to the reporting requirement under para. 6.4.x.

## Slide 7: Deactivation
“Deactivation process”: 5.1.6.3., 5.2.3.1-3., 5.2.3.5-9.
“Deactivation procedure”: 5.2.2.6., 5.2.3.10.
3.34. “System-initiated deactivation of the ADS” means a procedure by which the ADS initiates the transfer of performance of the DDT from the ADS to a vehicle fallback user.
3.37. “User-initiated deactivation of the ADS” means a procedure by which the user initiates the transfer of performance of the DDT from the ADS to the vehicle user.
“System vs user” is self-evident.
Is this really about the “procedure that initiates the transfer”
Why is this terminology clearer than “transition of control” and “take-over”?
The text indicates that the safety concern is the “process” or “procedure” that results in the “deactivation” (including but not limited to “initiation”).
Is this a “process” or a “procedure”? In either case, the term “deactivation proce____” needs to be defined to understand the requirements.
The term can be defined via reference to one or more requirements (i.e., a requirement to document the “deactivation process/procedure”).

## Slide 8: Scenarios and situations
The text uses “scenario” more than 150 times and “situation” more than 70 times.
The terms are used interchangeably and sometimes refer to testing and sometimes to actual road events.
Proposal to differentiate terms to clarify text.
3.xx “(Driving) Situation” means the actual conditions surrounding a vehicle in use at a point in time that are relevant to performance of the DDT for that vehicle.
3.29. “(Traffic) Scenario” means a temporal representation of a sequence of driving situations.

## Slide 9: Nominal, critical, failure
Current definitions ambiguous and not fit for purposes of the regulations.
Original purpose to differentiate sets of requirements
  ADS capability to drive safely (functional capability to perform the DDT)
  ADS capability to manage safety-critical external conditions (planning/decision-making, collision avoidance)
  ADS capability to safely manage failures in its dependencies (system/vehicle faults, failures in things the ADS relies on for safety)
3.29.1. “Nominal scenario” means [any scenario that is not a critical or failure scenario].
3.29.2. “Critical scenario” means a traffic scenario [where the operating conditions or behaviour of other road users requires a prompt action of the ADS to avoid or mitigate a collision with adverse consequences on human health or property damage].
3.29.3. “Failure scenario” means a traffic scenario representing a system failure that compromises the capability of the ADS to perform the entire DDT.
Definition should state what something is, not what it is not.
“Critical” points towards definition based on ADS response.
“Failure” definition omits use of “failure” in things like fallbacks to an MRC, user responsiveness, etc. mentioned in the text.
How does a functional scenario range from nominal to critical to failure?

## Slide 10: Nominal, critical, failure
3.29.1. “Nominal scenario” means [any scenario that is not a critical or failure scenario].
3.29.2. “Critical scenario” means a traffic scenario [where the operating conditions or behaviour of other road users requires a prompt action of the ADS to avoid or mitigate a collision with adverse consequences on human health or property damage].
3.29.3. “Failure scenario” means a traffic scenario representing a system failure that compromises the capability of the ADS to perform the entire DDT.
3.29.1. “Nominal scenario” means a scenario entirely navigated by the ADS within the boundaries for nominal vehicle motion.
3.29.2. “Critical scenario” means a scenario during which the ADS control inputs result in vehicle motion outside the boundaries for nominal motion and/or in a crash.
3.29.3. “Failure scenario” means a nominal or critical scenario during which the ADS executes a fallback in response to a fault in the system, vehicle, or other dependency necessary for performance of the DDT.
Shifts the perspective from guessing the scenario attributes to categorising the scenario based on the ADS response.

## Slide 11: Safety case, concept, claim, etc.
3.26. “Safety case” means a structured argument supported by a body of evidence that provides a compelling, comprehensible, and valid case that the ADS is or will be free from unreasonable risk for a given application in a given environment.
[3.26.1. “Argument” means a written explanation within a safety case that captures the logical connections between a claim and the evidence for achievement of that claim.]
[3.26.2. “Claim” means a high-level assertion that the behaviour competencies of an ADS will satisfy the DDT performance requirements applicable to one or more scenarios. ]
[3.26.3. “Evidence” means a set of results of analyses, simulations, and physical testing pertinent to demonstrating the validity of an argument within a safety case.]
3.27. “Safety concept” means a description of the measures designed into the ADS so that it operates in such a way that it is free of unreasonable safety risks to the ADS vehicle user(s) and other road users in every operating condition relevant to the ODD.
Issues
“Safety case” used in the Section 6.3. title and in its subsection 6.3.2.
Subsection 6.3.1. concerns the “safety concept” but the provisions set requirements for the “safety case”.
Clearer?: 6.3. Safety case, 6.3.1. Safety concept, 6.3.2. Claims

## Slide 12: ADS users
Defined: Driver, User (100+!), fallback user
Used: Human, occupant, operator, owner, passenger, remote assistant
SAE: (human) user, driver, passenger, DDT fallback-ready user, driverless operation dispatcher, and remote assistant
UK (ADS-07-14)
Also Law Commissions terms such as “user in charge”, other CP regulations, AV screening needs
Issues
Text refers to “roles” and to various terms for human users and use of ADS.
Some terms are not defined and term not structured for clarity (hierarchy, specificity).
Clarity of user-safety provisions and issues with “non-DDT tasks” in conventional regulations.