## Slide 1: ADS-IWG In-Service Monitoring and Reporting Status and open Items
Espedito Rusciano, Riccardo Doná
20/03/2025

## Slide 2: Definitions: Occurrence
3.16. “Occurrence” means a safety-relevant event during which at least one of the following criteria is fulfilled:
  a) Collision involving the ADS vehicle
  b) ADS vehicle system/component failure
  c) ADS vehicle produces a noncompliance with respect to the requirements of this regulation
  d) Injury/fatality as a result of being in the ADS vehicle or being involved in the event
  Normal operations which are relevant to argument specific ADS design choices and/or the safety case.
  New proposal to be discussed in ISMR work-stream (target: 8th ADS IWG, Tokyo)
  “Occurrence” means a safety-relevant event involving an ADS vehicle [Re. Integration Document]

## Slide 3: Definitions: Critical Occurrence
3.16.2. “Critical Occurrence” means an occurrence during which at least one of the following criteria is fulfilled:
  (a) At least one person suffers an injury that requires medical attention or dies as a result of being in the vehicle or being involved in the event.
  (b) The ADS vehicle, other vehicles [road users] or stationary objects sustain physical damage that exceeds a certain threshold.
  (c) Any vehicle involved in the event experiences a deployment of any non-reversible occupant restraint system, vulnerable road user secondary safety system or the delta-V thresholds to be met, whichever occurs first.
  New proposal to be discussed in ISMR work-stream (target: 8th ADS IWG, Tokyo)
Vulnerable road user secondary safety system" means a deployable vehicle system outside the occupant compartment designed to mitigate injury consequences to vulnerable road users during a collision. [ref. EDR]

## Slide 4: Occurrence List
Unknown scenarios encountered by the ADS
Unexpected behaviours of the ADS, including unexpected triggering of the fall back strategy
  New proposal to be discussed in ISMR work-stream (target: 8th ADS IWG, Tokyo)
Deviation of behavioral competencies of the ADS from the ones identified and documented in the safety case

## Slide 5: Occurrence List (By Tokyo)
Events where an activated ADS feature required interaction with a remote assistant to navigate a driving situation (if applicable)3
3This event does not cover remote driving, but rather events in which the ADS will require remote assistance to cope with very specific situations.
New proposal to be discussed in ISMR wotk-stream (target: 8th ADS IWG, Tokyo)
Not ready yet

## Slide 6: Assessment Section
7.1.4.6. The documentation review shall provide evidence that, at least:
…….
(c) ADS safety performance will be verified in reference to the safety performance indicators and safety performance targets as indicated in the Safety Case
(d) [the risk assessment, including residual risks, will be evaluated regularly through the information coming from the monitoring activities]
New proposal to be discussed in ISMR work-stream (target: 8th ADS IWG, Tokyo)
Not ready yet, but it will merge c with d

## Slide 7: Assessment Section (By Tokyo)
7.4.1. (UNR) The Type Approval Authority or its Technical Service shall receive and review confirmatory evidence produced by that the information provided by the manufacturer during the ADS during its operations (e.g. Notification, short term and periodic reports) is in compliance with and assess that it is in accordance with capabilities described in the manufacturer’s SMS [ref. 7.4.1.7-7.4.1.10].
New proposal to be discussed in ISMR work-stream (target: 8th ADS IWG, Tokyo)
The Type Approval Authority or its Technical Service shall receive information provided by the manufacturer and assess that it is in accordance with the manufacturer’s SMS [ref. 7.4.1.7-7.4.1.10].

## Slide 8: Occurrence list: Emergency/complex manoeuvres
FR: The table with “Occurrence and safety-relevant event” should include this safety-related event: “Emergency/complex maneuvers to prevent a collision”.
Current proposal: Emergency/complex
  1) Maneuvers performed to reach MRC
  2) Maneuvers linked to a prompt action of the ADS to avoid or mitigate a collision.
  Status: Discussion on the current proposal will continue in the ISMR (target: 9th/10th ADS IWG)

## Slide 9: Assessment: Authority actions
7.4.6. (UNR) If an serious unreasonable safety risk is identified, the Type Approval Authority may inform the Contracting Party on the need of recommend temporary safety measures, including immediately restricting or suspending the relevant operations via remote termination, and on the need to require actions to restore an acceptable level of safety as per the applicable laws.
Alternative for UNR
If an serious unreasonable safety risk is identified, the Contracting Party may recommend temporary safety measures, including immediately restricting or suspending the relevant operations via remote termination, and may require to take actions to restore an acceptable level of safety as per the applicable laws
(GTR) If a serious unreasonable safety risk is identified, the Contracting Party may recommend temporary safety measures, including immediately restricting or suspending the relevant operations via remote termination, and may require to take actions to restore an acceptable level of safety as per the applicable laws.
Alternative proposal UNR/GTR
[If an unreasonable risk to safety is identified, the Contracting Party may carry out its enforcement authorities to the maximum extent under applicable law. Depending on national law, options could include ordering remedies, suspending relevant operations, and recommending or requiring actions to remedy the safety risk]
Status: Discussion on the current proposal will continue in the ISMR (target: 9th/10th ADS IWG)

## Slide 10: Annexes
Status: Discussion on the Annexes will continue in the ISMR (target: 9th/10th ADS IWG)

## Slide 11: Other Topics
Recommendations beyond the scope of the Regulation
Implementation of ISMR
  What happens to 'non confidential' information
  What, if any, information is made public
  What authority to share to
  What information sharing happens between authorities
  Scenario work, what info is shared
  Possibility from other TAAs to have access to reports
  What happens after reporting? Recall, TAA’s role/possibility
  Is the discussion on the above topics needed?
  Status: This topics will be discussed as part of the interpretation document activities

## Slide 12: Thank you
© European Union 2025
Unless otherwise noted the reuse of this presentation is authorised under the CC BY 4.0 license. For any use or reproduction of elements that are not owned by the EU, permission may need to be sought directly from the respective right holders.
Notes: Update/add/delete parts of the copy right notice where appropriate.
More information: https://myintracomm.ec.europa.eu/corp/intellectual-property/Documents/2019_Reuse-guidelines%28CC-BY%29.pdf

## Slide 13: Keep in touch
EU Spotify
ec.europa.eu/
europa.eu/
@EU_Commission
@EuropeanCommission
European Commission
europeancommission
@EuropeanCommission
EUTube
Notes: Delete/update as appropriate