## Slide 1: Topic
Children Left in Vehicles (CLIV)
An Australian bus perspective and solution
October 2024

## Slide 2: Agenda
Background
Jurisdictional Action
System Function
Advantages
Questions
Bus Industry Confederation (Australia) – October 2024 Children Left in Vehicles : Australian Perspective and solutions

## Slide 3: Australian Background
Up to 120kms
Per trip one way
45 minutes
Average trip time
1.3 Million
Children travel by bus each day
68 Children
left on a bus, last 5yrs
5-18yrs
Average Age range
Temperature
Inside an unattended bus
Heatstroke possible 10 minutes
+60C
-10C
Bus Industry Confederation (Australia) – October 2024 Children Left in Vehicles : Australian Perspective and solutions

## Slide 4: Jurisdictional Action
2013
2022
Mandated
Optional or recommended
A ‘child check system’ was Mandated for School Buses (not other services)
Bus Industry Confederation (Australia) – October 2024 Children Left in Vehicles : Australian Perspective and solutions

## Slide 5: System Function
Automatically with Ignition on or School bus lights
1. System Enabled
A 30 second timer Automatically starts when ignition key is turned off.
2. Check Timer Armed
In the 30-seconds, driver walks to rear of bus checking each seat and under each seat.
3. Physical Driver Check
Driver presses button at rear of bus to acknowledge bus checked.
This turns system off.
4. Check Confirmation
**If driver fails to presses button this activates a 95dB alarm.
It sounds until button is pressed
**5. Alarm**
Bus Industry Confederation (Australia) – October 2024 Children Left in Vehicles : Australian Perspective and solutions

## Slide 6: Advantages / Consideration
Fitment: Can be easily fitted & Retrofitted.
Cost: $900 - $2000 AUD, (€550 - €1200 or CNY4200 – CNY9500)
Technology: Robust, simple, low maintenance, Readily available, Not Unique
Application: Fitment to all buses?
Bus Industry Confederation (Australia) – October 2024 Children Left in Vehicles : Australian Perspective and solutions
Notes: Avoids multiple systems on different age vehiucles

## Slide 7: Thank you
Bus Industry Confederation (Australia) – October 2024 Children Left in Vehicles : Australian Perspective and solutions

## Slide 8: Annex A – Supportive Information
BIC Paper Sleeping Child Safety Systems
Bus Industry Confederation (Australia) – October 2024 Children Left in Vehicles : Australian Perspective and solutions