## Slide 1: Countermeasures for Light Vehicles
IWG-CLIV (2024.10)
JINSEOP PARK, Chief Researcher
Korea Transporation Safety Authority
Korea Automobile Testing & Research Institute(KATRI)
* This is based on the study of KNCAP R&D project and Korea’s R&D project for enhancing safety of school buses [RS-2022-00143581]

## Slide 2: Institutional Countermeasures
Voluntary obligation - USA (2019) · “leading automakers’ commitment to implement rear seat reminder system” · DOT NHTSA X 22 OEMs
Consumer testing - Euro NCAP/ANCAP · introduced CPD(Child Presence Detection) assessment in 2023 · scores are awarded to a car based on the performance - Others (KNCAP, CNCAP, JNCAP) · to include the similar assessment* (or possibly introduced)
*based on 2023 Global NCAP meeting presentations
[Euro NCAP CPD presentation]
(source: GRSP-70-30)
[USA automakers’ commitment]
(source: provided by Hyundai Motors Group)

## Slide 3: Technical countermeasures
Categorization
Encourage the drivers to check there is no children left in vehicles - reminder (to the driver)
Indirect detection of left children in vehicles - door opening & closing, seat-occupancy
Direct detection of left children in vehicles - radar sensor, ultrasonic sensor, camera

## Slide 4: Encourage the drivers to check no children left
Check no children left on the van !
Reminder - message to the driver after the end of a journey - audible/visual signal may be provided - may be incorporated with the indirect detection of left children in vehicles (e.g. door opening & closing) - encourages the driver to check no children left in the vehicle
[message to a driver]
* source: Hyundai Motors Blue Link manual
※ All figures/illustrations other than captioned pictures are made by KATRI

## Slide 5: Indirect detection of left children in vehicles
by assumption of child presence based on door opening & closing - low accuracy - door opening & closing ≠ passengers getting on & off
by assumption of child presence based on seat-occupancy - low accuracy - objects on seats may be recognizable as a child occupant by the seat- occupancy sensor (e.g. pressure type sensor)
Occupancy sensor signal
(e.g. pressure sensor)
Door opening & closing signal

## Slide 6: Direct detection of no children left in vehicles
Movement detection - radar sensor · high accuracy · high cost - ultrasonic sensor · lower cost (c.t. radar sensor) · affected by the environment - camera · in line with future tech trends (in-cabin monitoring) · blind spot (behind seat backs / if covered by a blanket)
[Radar sensor on the roof inside]
*source: Korea R&D report [RS-2022-00143581]
ROA
[Rear Occupant Alert]
* source: Hyundai Motors manual

## Slide 7: Direct detection of left children in vehicles
Test tool for the direct detection performance → necessary - test tool: ATD(anthropometric test device)
Test tool status in the market - no standard (e.g. ISO) yet - two ATD manufacturers - ATD types: TBD (0y(newborn), 1y, 3y, 6y)
Test tool specifications - must be included in UNECE WP.29 M.R.1 (like other ATDs) after a sufficient review and discussion of · anthropometric specs. (dimension, weight, etc.) · movement specs. (respiration, extremities, etc.) · other specs. simulating human child body characteristics
[4a systems (newborn)]
[MESSRING (newborn)]
* Picture sources) 4a systems & Messering websites (brochures)

## Slide 8: Discussion & Conclusion
Potentially mandatory countermeasures should be decided for the international regulation establishment after reviewing all countermeasures with stakeholders - encourage the drivers to check no children left in vehicles - indirect detection of the left children on buses - direct detection of the left children on buses
Depending on the decided countermeasures, specific requirements and procedures of the regulation should be discussed - requirements (general and performance) - test procedures - CLIV ATD specifications (if needed), etc.

## Slide 9: Discussion & Conclusion
IWG should reviews conflict with other regulations (e.g. hazard light, horn), and should revise the other regulations if necessary
Further specific discussions (next phase) - warning only or including intervention - warning types · visual: tell-tale(to a driver), hazard light · audible: horn · mobile: text or application - warning requirements: sound volume & duration - durability - deactivation - potential field complaints, etc.

## Slide 10: Attachment - Idea suggestion
Visual warning to the outside - direction indicators alternately flash diagonally · simple, noticeable, distinct · education/campaign friendly
Vertical Parking
Parallel Parking

## Slide 11
고맙습니다.
Thank you for your attention
jspark@kotsa.or.kr