## Slide 1: Proposals for Improvement
TF ADAS -36

## Slide 2: Speed Limit Compliance Assistance
The current provisions in the Speed Limit Compliance Assistance section would prohibit manufacturer’s from continuing to implement well established, effective strategies to achieve improved emissions and fuel efficiency.
These strategies adapt the maximum speed of the vehicle’s longitudinal control to allow to use the existing momentum when going up or down a hill in the most energy efficient way.
DCAS should strive to help improve emissions, not increase them, therefore the current provisions should be amended as proposed below, to continue to allow these control strategies.

## Slide 3: Proposal for Amendment:
5.3.7.4.7.3.3. If the new system-determined road speed limit is lower than the current maximum speed, the current maximum speed shall automatically change to a value not higher than the new system-determined road speed limit.
5.3.7.4.9. The system shall not enable the driver to set a default offset by which the current maximum speed is supposed to exceed the system-determined road speed limit. However, control strategies according to par. 5.3.7.4.10. may be configured by the driver.
5.3.7.4.10. Technically Rreasonable tolerances (e.g., related to speedometer inaccuracy, external disturbances or other control strategies e.g. to achieve better fuel efficiency or reduce emissions) may be applied to the warning thresholds and operational limits the system’s designed speed operational limits and shall be declared by the manufacturer to the Type Approval Authority.
General clarification that a value below the detected limit is of course permitted.
Nowadays the driver can adjust the setting of these fuel saving strategies. This should remain permitted, as this is a configurable tolerance applicable to specific scenarios, e.g. when going down a hill.
Amended to clarify that tolerances required for these control strategies remain permitted.

## Slide 4: Required confirmation by the driver
This paragraph should allow to provide that acknowledgement request in alignment with the general warning and information strategy either at the beginning or the end of a drive cycle. While the first provision only refers to “while the vehicle is in a stopped position”, the last sentence requires “upon initiation of the powertrain”:
5.3.7.2.4.11. A request for the driver to acknowledge that they have read and understood the driver information material outlined in paragraph 5.6 shall be given while the vehicle is in a stopped position. This request shall be given at least once every month. If the vehicle utilises a means of differentiating between users, this may be extended to 3 months for a given user. If the vehicle can identify that a driver has previously acknowledged this request it does not need to be given again for that driver. If the vehicle can identify that the current driver has not acknowledged this request before, then it shall be given upon initiation of the powertrain at the earliest point in time in alignment with the system’s warning and information strategy (e.g. at the beginning or at the end of a drive cycle).