## Slide 1: Survey on the transition time from ACSF to Manual Driving
Toyota Motor Corporation
Informal Document: ACSF-04-14
Submitted by the expert of Japan

## Slide 2: Experimental Condition
Purpose
  To obtain the experimental data of the transition time from ACSF system to Manual driving. To set several conditions of the driver when ACSF on, including doing Sub-task.
  Experimental Set-up
      Simple Driving Simulator (Fixed system with only front screen)
      Sub-task : Watching a movie or playing a game to use the tablet PC.
      Driver put his hands on knees during ACSF on.
      Sudden Audible warning to inform the transition demand.
Experimental System

## Slide 3: Experimental Condition
Steering Angle
Time
Response Time
Beep
  Driver’s Condition
    Sub-task : None, Watching a movie, Playing a game
    Tablet PC’s position
    : Upper (Left upper of Steering), Lower (near Driver’s knee)
    Warning : Beep sound
  Driver’s Response Time
    From the start of Beep sound to Driver’s steering input.
←Upper position (Game)
Lower position (Game)→

## Slide 4: Results of Driver’s response time
Results (10 panels)
None | Movie | Movie | Game | Game
 | (Upper) | (Lower) | (Upper) | (Lower)
Sub-task (Tablet position) |  |  |  | 
Mean Response Time (s)
 | Response Time (sec) |  |  |  | 
 | None | Movie (U) | Movie (L) | Game (U) | Game (L)
Sub-task |  |  |  |  | 
Mean | 1.9 | 1.9 | 2.1 | 1.7 | 1.7
Standard Deviation | 0.25 | 0.12 | 0.29 | 0.09 | 0.14
Min. | 1.4 | 1.5 | 1.3 | 1.5 | 1.2
Max. | 2.9 | 2.6 | 3.6 | 2.4 | 2.4
Mean:1.9sec, Min:1.2sec, Max:3.6sec
Driver’s response time is rather stable whether with Sub-task or without.
Chart: 
 | 1.8689 | 1.9156 | 2.0811 | 1.6989 | 1.7411
Chart: 
 | 2.86 | 2.6 | 3.58 | 2.38 | 2.35
Maximum