## Slide 1: Representative vehicle

## Slide 2: Representative vehicle
Modular Approach
Due to complex nature of production and usage of vehicle, a ‘modular approach’ will be suitable for carbon footprint calculation
Modular approach: Each phase of life cycle of vehicle will be calculated separately and then combined for a given vehicle
This reflects the present practice in industry
Reminder
Representative vehicle
Defines number of calculations to be performed
Calculation burden exponentially increase with exact configuration of vehicle without substantial gain
Hence, irrespective of levels a representative vehicle definition is required to represent a family of vehicle
Should be precise enough for the purpose and less administrative burden

## Slide 3: Modular approach
Down stream:
Use phase
Upstream:
Materials & production
Downstream:
End of life
Reference section | 3 | 4 | 5
Influencing factors | Depends on Country/region of production Vehicle type Powertrain type | Depends on Country/region of usage Powertrain configuration according to regional regulations etc. | Depends on Country/region of recycling Vehicle type Powertrain type
Family | LCA group (as defined in 3.1) | Powertrain group (as defined in 4.1) | End of Life group (as defined in 5.1)
Calculation Approach | Extrapolation method (as defined in 3.2) | Interpolation or inertia approach depending on country/region of usage (as defined in 4.2) | Extrapolation method (as defined in 5.2)
To be confirmed by SG5

## Slide 4: Calculation overview: Level 3
Step 2
Downstream emission: Use phase
Step 3
Upstream
emission
Total Carbon footprint
* Traction Battery’s mass & its carbon footprint to be excluded
**For vehicle with traction batteries
Define a vehicle for LCA declarations
Step 2.1 :
Check in which interpolation family the ‘defined vehicle‘ belongs to
Step 2.2 :
Take the energy consumption value of the ‘vehicle High’ of that interpolation family
Step 2.3 :
Calculate down stream emission (considering service life, deterioration factor etc.)
Step 3.1 :
Check in which ‘LCA group’ the defined vehicle’ belongs to
Step 3.2 :
Consider the mass of the ‘vehicle high’* considered for the ‘downstream emission’
Step 3.3 :
Estimate upstream carbon footprint by extrapolation from ‘representative vehicle of larger ‘LCA group’ using ‘UEF’
Step 4:
Total Vehicle CFP = Upstream CFP + Downstream CFP + EoL CFP + Battery**
Step 4
Downstream : End of Life
emission
Step 4.1 :
Check in which ‘LCA group’ the defined vehicle’ belongs to
Step 4.2 :
Consider the mass of the ‘vehicle high’* considered for the ‘downstream emission’
Step 4.3 :
Estimate EoL carbon footprint by extrapolation from ‘representative vehicle of larger ‘LCA group’ using ‘UEF’
Optional**: Traction battery carbon footprint & weight to be considered separately
Traction battery emission
To be confirmed by SG5

## Slide 5: Upstream emission: Base line approach (SG3 discussion)
Cluster vehicles into a LCA group
LCA group:
  Vehicle type
  Powertrain energy type (petrol, EV etc.)
  Location of production
  Traction battery (for electrified vehicles)
Representative vehicle : Choose heaviest vehicle configuration (in OEM catalogue) in LCA group
Calculate ‘upstream emission’ for RV as defined by SG2 and SG3
Calculate ‘upstream emission factor’
is the upstream emission factor, kg CO2 eq./kg
is the carbon upstream emission of the representative vehicle, CO2 eq. kg;
is the vehicle weight of the representative vehicle, kg;

## Slide 6
Upstream emission: Estimation of required vehicle (SG3 discussion)
Vehicle on which CFP value is required
Worstcase conf. cover other vehicle
Estimate upstream LCA value on same ‘use phase vehicle conf.
Powertrain group (IP-family / inertia class)
LCA group
is the carbon upstream emission of the individual vehicle, CO2 eq. kg;
is the upstream emission factor, kg CO2 eq./kg
is the individual vehicle weight
Vehicle weight

## Slide 7
Downstream emission: Use phase
CO2e Material
CO2e Production
CO2e Use phase
CO2e Recycling
CO2e
=
+
+
CO2e energy cons
CO2e leakage
CO2e maintenance
CO2e use phase
=
+
+
+
Energy consumption
Service
Life
Conversion factor
well-to-Wheel
X
X
CO2e energy cons
=
CO2e Secondary use
Not in Scope
CO2e Second life
+
Not in Scope
Present practice:
Energy consumption is defined for a powertrain group in every region of the world ( IP family etc.)
Representative vehicle are defined in an interpolation or inertia class approach
Proposal :
As they already exist => its better to refer to regional regulations for powertrain group
CO2e Show room
Not in Scope
+
+
Present practice:
Maintenance and leakage are not part of any powertrain group criteria
Proposal :
Impact of leakage & maintenance are reported to be very low and hence variation of these emissions in a powertrain group will be very low
Propose to use the worst-case vehicle of a powertrain group as the representative vehicle (same as energy consumption)

## Slide 8: Downstream emission: Use phase
Energy consumption of individual vehicle calculated by interpolation approach :
Europe
Japan
China ?
…
Energy consumption of individual vehicle calculated by inertia approach :
Korea
US
Brazil
…
Each individual vehicle has ‘energy consumption’ value in the official document ( COC etc.)
Broadly there are two types of approach: Interpolation & Inertia class
Mass
CO2
Cycle Energy Demand
CO2
Reminder

## Slide 9: Downstream emission: Use phase (level 3)
Regions using interpolation approach => vehicle high will cover all other vehicle in that interpolation family
Regions using Inertial class => highest inertia class can cover all other inertia class below in a powertrain group
Worst case energy consumption can cover other vehicles
Mass
CO2
Cycle Energy Demand
CO2

## Slide 10
Downstream emission-Use phase : Level
Level 3
Powertrain group
Level 1 & 2
LCA group
LCA group
Level 4
Individual vehicle
Downstream –Use phase
Upstream

## Slide 11
Downstream emission- Use phase: Maintenance & leakage
parts & consumables
Carbon emission factor
Replacement Frequency
X
X
CO2e maintenance
=
Fixed factor
X
CO2e maintenance
=
OR
Option 1
Option 2
Open question
Level 2: fixed factor (option 2) ?
Level 3: priority for fixed factor (option 2) and if OEM can provide details then can use ‘option 1’
Level 4: priority for ‘option 1’ with OEM data
Two option agreed in SG4

## Slide 12: Downstream emission- Use phase: overview
Grouping of vehicle: (section 4.1)
Group vehicles into powertrain criteria
Selection of representative vehicle: (Section 4.3)
In case of Interpolation: Choose vehicle high
In case of Inertia class: Choose highest inertia class
Calculation of in-use energy consumption : (section Y.Y SG4)
Calculate using ‘representative vehicle definition’
Calculation of maintenance & leakage: (section Y.Z.1 of SG4)
Calculate using ‘representative vehicle definition’
Selection of representative vehicle: (Section 4.4)
In case of Interpolation: individual vehicle
In case of Inertia class: individual inertia class
Calculation of in-use energy consumption : (section Y.Y SG4)
Calculate using ‘individual vehicle definition’
Calculation maintenance & leakage: (section Y.Z.2 of SG4)
Calculate using ‘representative vehicle definition
In-use CFP = in-use energy consumption + maintenance/ leakage
Arrange vehicles according to mass/energy : (section 4.2)
Organize vehicles into different inertia class or interpolation group
Level 3
Level 4