## Slide 1: Accidentology – Blind Spot Accidents N1 vs. N2+
Patrick Seiniger
Martin Pöppel-Decker
Daniel Sander

## Slide 2: Part 1: National Statistics

## Slide 3: Methodology
Germany collects 3-digit accident types for some states
  Niedersachsen, Saarland, NRW, MV, RP, Sachsen-Anhalt
  Aggregated population = 41.7% of total population
Relevant accidents
  In city, following types:
Vehicles
  N1 vs. N2 low, N2 high, N3, Tractors, other N
Years 2019 - 2023
Gkz 1 thru 3500 kg
Gkz 3501 thru 7500 kg
Gkz 7501 thru 12000 kg
Gkz12001 thru hi
ohne zulGG Sattelschlepper
ohne zulGG Gkz m./o. Anh.
ohne zulGG übrige Gkz

## Slide 4: Number of Accidents with Personal Injury
Chart: Relevant accidents with personal injury for 41.7% of Germany
| 2019 | 2020 | 2021 | 2022 | 2023
U(P) N1 | 120 | 99 | 91 | 100 | 116
U(P) N2+ | 140 | 118 | 97 | 131 | 119

## Slide 5: Fatalities N1 vs. N2+
Chart: Relevant accidents for approx. 41.7% of Germany
| 2019 | 2020 | 2021 | 2022 | 2023
N1 Fatalities | 0 | 0 | 0 | 1 | 2
N2+ Fatalities | 8 | 11 | 10 | 6 | 10

## Slide 6: Severe Injuries N1 vs. N2+
Chart: Relevant accidents in approx. 41.7% of Germany
| 2019 | 2020 | 2021 | 2022 | 2023
N1 Severe | 12 | 10 | 8 | 9 | 5
N2+ Severe | 23 | 30 | 20 | 29 | 22

## Slide 7: Economic Costs N1 vs. N2+
Chart: Economic costs for approx. 41.7% of Germany
| 2019 | 2020 | 2021 | 2022 | 2023
Cost N1 | 1546536 | 1288780 | 1031024 | 2444062 | 3212710
Cost N2+ | 13237474 | 17992100 | 15419160 | 11442422 | 15676916
20% for N1
7% for N1

## Slide 8: Part 2: GIDAS

## Slide 9: GIDAS Analysis - Filter Process
GIDAS database July 2024;
Only complete reconstructed cases
33016 accidents
Accident types is 232, 243 Number of involved participants == 2
895 accidents
72 accidents
81 accidents
N1 vs bicycle (with number of collisions == 1)
N2/N3 vs bicycle (with number of collisions == 1)
Accident years 2005-2024

## Slide 10: GIDAS Analysis - Results
Injury severity in accidents involving N2/N3 vehicles considerably higher
Injuries always relate to the cyclist, none of the vehicle occupants sustained an injury
Vehicle Class | Killed | Seriously Injured | Slightly Injured | Accidents
N1 | 0 | 8 | 62 | 72
N2/N3 | 7 | 28 | 47 | 81
Vehicle Class | MAIS4+ | MAIS3 | MAIS2 | < MAIS2 | Accidents
N1 | 0 | 2 | 7 | 60 | 72
N2/N3 | 9 | 7 | 18 | 45 | 81
Numbers only coded for known injury severity

## Slide 11: Conclusion

## Slide 12: Conclusion
Accidents with personal injury  number comparable N1 vs. N2+
Very low number of fatalities for N1
Economic accident costs 5x – 10x higher for N2+
DE registrations: N1 >>> N2+, however unclear about foreign vehicles in DE traffic
Risk associated with N1 seems to be much lower than risk N2+
From our perspective there is no urgent need to implement R151 also for N1 vehicles