## Slide 1: Review of Sunroof Breakage Incidents
James Myers
Safety Standards Engineer

## Slide 2: Background
NHTSA has opened 5 investigations into sunroof breakage since 2004
Latest investigation opened Oct-21-2013 (PE 13-035)
  Models affected were 2011 – 2013 Kia Sorento
  78 unique VINs from ODI and Kia reports
  Investigation opened to analyze scope, frequency, and consequence of failures
    60 vehicles in motion at time of breakage
    14 reports of minor cuts/scratches

## Slide 3: Summary of Recent USA Incident Counts
MMMY | Manufacturer Reported | Vehicle Population
Kia Sorento 2011-2014 | 156 | 93,344
Kia Optima 2011-2014 | 173 | 184,872
Kia Sportage 2011-2014 | 37 | 33,143
Hyundai Elantra GT 2013-2014 | 14 | 18,549
Hyundai Santa Fe 2013-2014 | 27 | 63,611
Hyundai Sonata 2011-2014 | 40 | 106,317
Hyundai Tucson 2011-2014 | 8 | 32,414
Ford Edge 2011-2014 | 88 | 188,723
Ford Escape 2013-2014 | 28 | 154,151
Ford Explorer 2011-2014 | 31 | 220,075
Nissan Murano 2011-2014 | 33 | 127,317
Nissan Pathfinder 2013-2014 | 6 | 57,392
VW Jetta 2011-2014 | 8 | 56,790
VW Tiguan 2011-2014 | 9 | 44,696
Information available on NHTSA website:
www-odi.nhtsa.dot.gov/cars/problems/defect/results.cfm?action_number=EA14002&SearchType=QuickSearch&summary=true
Notes: Location analysis not available

## Slide 4: Other Information
NHTSA sunroof breakage investigations since 2004
  Two recalls
    PE12-027 – Manufacturer recalled improperly installed sunroof
      19,600 MY 2012 Hyundai Veloster vehicles
    PE04-035 – Manufacturer recalled improperly quenched sunroof
      32,100 MY 2004 Nissan Maxima vehicles
  Two closed no recall
    EA06-001 – No clear defect identified
      MY 2004-2006 Cadillac SRX vehicles
    PE06-024 – No clear defect identified
      MY 2005-2006 Scion TC vehicles
Investigation data available at: http://www-odi.nhtsa.dot.gov/owners/SearchSafetyIssues

## Slide 5: James Myers james.myers@dot.gov www.NHTSA.gov