## Slide 1: Status Report from GRE TF AVSR
Dr. K. Manz, DE – Chair
L. Schwenkschuster, GTB - Secretary
AVSR-24-04
Transmitted by the Chair of the GRE TF “Autonomous Vehicle Signalling Requirements” (AVSR) | Informal document GRE-92-xx (92nd GRE, 22–25 April 2025 Agenda item 13(a))

## Slide 2
After the last meetings of GRE TF AVSR,
on the basis of document ECE/TRANS/WP.29/GRE/2023/9/Rev.3,
an intense discussion took place, mainly given on new input received by members from EC and Canada. Which means, that the document is not yet ready as a formal document and is now presented as an informal document GRE-12.
The questions raised in the discussions, has also required guidance from GRVA TF FADS!

## Slide 3
- The new vehicle categories „X“ and „Y“ are seen as subcategories to the existing ones e. g. M, N, O, T, … etc.
That means, no change of the scope.
Further definitions are added:
2.3.12.4. “Operational Design Domain (ODD)” means ….
2.2.12.5. “ADS feature” means ….
- New Paragrapf added:
"3.2.8. If a driver’s seat is fitted but it is not the front seat nearest to the opposing traffic, the applicant shall specify this seating position. "
Results of the last discussions:

## Slide 4
"5.2.1. "In the case of headlamps fitted with measures to prevent discomfort to other road-users in a country where traffic operates on the side of the road opposite to that of the country for which the headlamp was designed, such measures shall be achieved automatically or by the vehicle user with the vehicle in the park condition without the need for special tools (other than those provided with the vehicle). Detailed instructions shall be provided by the vehicle manufacturer with the vehicle.
If the vehicle is equipped with an ADS and the ODD of that ADS includes the change between traffic on both sides of the road, the ADS shall be able to activate the measures when the direction of traffic changes."
This does not apply to dedicated objects that may be added to the exterior of the headlamp.
Results of the last discussions:
- Addition to the so called “ tourist solution”:

## Slide 5
Add new paragraph 5.35.12. to read:
"5.35.12. Driver Assistance Projections, which are intended to support the driver only, shall not be activated if the ADS is active.“
- Clarification between ADS features and conventional automatic features (driver assistance features) and their application:
"5.36. Automatic lighting functions, as defined in this Regulation, shall not be considered an ADS feature. These functions may be used by an ADS feature when it is active, provided that all related requirements in this Regulation are met, and the ADS feature monitors the environment and controls the automatic lighting function. “
Results of the last discussions:

## Slide 6
5.37. Whilst the ADS is active, any tell-tale information specified in paragraphs 5 and 6 of this UN Regulation shall be transmitted to the ADS.
5.38. If not otherwise specified, all Requirements to this Regulation, related to the “driver” or “manual operation” assuming that the “ADS” is not active.
5.39. If an ADS is active and it is not otherwise specified, all active lighting functions prescribed in this Regulation shall be operated by the ADS"
Results of the last discussions:
- Adding of new general paragraphs to simplify the application of conventional and automated operation requirements for the vehicle of the categories' “X” and “Y”: :
5. 40. In the case of vehicles categories X and Y the following specifications will be apply:
5.40.1. for vehicles of Category X will be disregard the presence of:
    a driver [and the related specifications];
5.40.2. for vehicles of the Category Y will be disregard the presence of:
    Any person;
    Visible or audible tell-tales;
    Any manual functions ( e. g. swiches etc….).

## Slide 7
[5.41. To verify, whether, according to this Regulation, the active ADS operation of all lighting functions does not cause any discomfort, the technical service shall perform a test drive which comprises any situation relevant to the system control on the basis of the applicants description and in accordance with Regulation GRVA; it shall be notified whether all modes are activated, performing and de-activated according to the applicant's description; obvious malfunctioning, if any, shall be contested (e.g. excessive angular movement or flicker). ]
Results of the last discussions:

## Slide 8
Last minute proposals, which requires a further discussion:
6.1.1. Presence
- Mandatory on motor vehicles
with the exception for the categories X and Y
- Optional for the categories X and Y
- Prohibited on trailers.
Alternative text:
6.1.1. Presence
- Optional for the categories X and Y
- Mandatory on all other motor vehicles
- Prohibited on trailers.

## Slide 9
Results of the last discussions:
Paragraph 6.1.4.3., amend to read:
"6.1.4.3. In length: At the front of the vehicle. This requirement shall be deemed to be satisfied if the light emitted does not cause discomfort to the driver either directly or indirectly through the devices for indirect vision and/or other reflecting surfaces of the vehicle. Additionally, for vehicles equipped with an ADS, if the light emitted does not influence negatively the performance of the ADS feature either directly or indirectly through the devices for indirect vision and/or other reflecting surfaces of the vehicle.

## Slide 10
Add a new paragraph 6.1.7.2.1., to read:
"6.1.7.2.1. In the case that the vehicle is controlled by an ADS feature, either:
the applicant shall prove to the satisfaction of the Type-Approval Authority that the automatic main-beam operation is controlled by the ADS feature to avoid causing discomfort, distraction or glare to other road users; or
the main-beam headlamps shall be switched OFF while the ADS feature is active."
Paragraph 6.1.7.3., amend to read
"6.1.7.3. It shall always be possible for a driver to switch the main-beam headlamps ON and OFF manually and to manually deactivate switch off the automatic control of the main-beam headlamps.
Moreover, the switching OFF of the main-beam headlamps and the deactivation of their automatic control shall be by means of a simple and immediate manual operation; the use of sub-menus is not allowed. "
Results of the last discussions:

## Slide 11
Accepted results of the last discussions and
Last minute proposals, which requires a further discussion:
Annex 5,
Paragraph 2., amend to read:
"2. Loading conditions for different types of vehicles:
For this paragraph the front seat nearest to the opposing traffic (formerly known as the “driver’s seat”) is referred to as “seating position 1”.
If the seating position 1 is not located on the front seat nearest to the opposing traffic, due to the design or the operational conditions of the vehicle, the manufacturer shall specify the seating position 1.
For vehicles of category Y the test shall be done without occupants. For vehicles of category X the test shall be done without a driver.
For vehicles designed to travel with occupants the following loading conditions shall apply, whereas also in addition for vehicles, where ADS features can be activated, the cases without occupants and seat position 1 is not occupied shall be determined:
… "
Alternativly may be a revision of this Annex with e.g. Pargaraphs 2.5 for Cat. “X” and 2.6. for Cat. “Y” ……

## Slide 12
The next meeting of the GRE Task Force AVSR
Should be determined in this meeting!

## Slide 13: GRE TF AVSR
Thank you for your attention!