## Slide 1: ADS amendments in emission regulations - discussion
Input from the experts of EC – JRC
GRPE TF AVRS #27

## Slide 2: Baseline
The ADS is understood as the “driver” of the vehicle: ADS and human driver at the same level of responsibility while carrying out the DDT.
Driver
ADS
Vehicle driven by a human
Vehicle driven by an ADS feature
The regulation should form an equal level of requirements, enable testing and evaluation of the vehicle, engine or system, whilst an ADS feature is active.

## Slide 3: Baseline
The “ADS user” is not a driver. In fact, it can be a person without any knowledge about the vehicles or driving (i.e. without a driving license).
The ADS remains with all the responsibility for the DDT.
Although, user input might have an effect on emissions.
Driver
Driver- selectable modes
ADS-user
ADS
ADS-user selectable modes
User- selectable modes
interface
interface

## Slide 4: General approach to amend regulations
A high level description

## Slide 5: Amendment methodology: scope and definitions
Scope
  Vehicles equipped with an ADS should be included (X and Y categories) -> RE3 and SR1 references updated.
  Vehicles equipped with an ADS should be eliminated from the scope, if the regulation is not applicable for them (not expected in GRPE).
Definitions
  Whenever necessary (e.g. driver mentioned), definitions should be extended to ADS vehicles
  If necessary, new definitions should be included.

## Slide 6: Amendment methodology: requirements and tests
Requirements for ADS
  Existing requirements should be extended to ADS wherever applicable.
  ADS might be exempted from certain requirements, if not applicable.
  An equal level of requirements should be formulated wherever gaps are identified.
Tests and demonstrations
  The regulation should enable testing of ADS vehicles:
    Existing methodology extended to ADS wherever possible.
    Interpretation or clarification should be added wherever gaps are identified.

## Slide 7: Amendment methodology: data and evaluation
Evaluation, data processing, calculations, etc. (as applicable)
  Existing methodology applicable -> no changes needed
  Existing methodology should be extended to ADS wherever needed.
  New methodology should be implemented, if necessary.

## Slide 8: Specific issues in emission regulations
How to apply the high-level principles to specific concepts in emission regulations?

## Slide 9: Issue 1: interpolation family (1)
Today, interpolation family is affected mostly by vehicle mass, road load and powertrain configuration.
ADS needs to be considered in the interpolation family:
  It has a considerable electric power consumption during operation
  If we allow testing ADS equipped vehicles in manual mode, ADS power consumption needs to be compensated for.

## Slide 10: Issue 1: interpolation family (2)
An “emission test ADS” (e.g. “coastdown mode”, “Type 1 test mode”) may not use all ADS sensors, therefore consumption might be less than the “normal ADS”
Real-world power consumption of ADS needs to be ensured during testing:
  We may consider using an “energy/power load” when testing ADS to ensure real life results.
  ADS testing mode may include an ADS functioning in “shadow mode”, with the aim that the average energy consumption is maintained throughout the test.
  Added cycle energy based on average ADS energy consumption (extrapolation might be needed).

## Slide 11: Issue 2: road load family
ADS needs to be considered in the road load family:
  It might have a considerable effect on the air resistance of the vehicle (additional sensors),
  but it depends on the ADS automation level, system structure and vehicle design.
  Either there will be an additional variant of the manual vehicle, but equipped with ADS,
  or in case of X and Y vehicles, all variants will include the ADS.
The existing interpolation method handles this issue well.

## Slide 12: Issue 3: ADS vehicle speed
R154: 3 WLTC classes based on the power to weight ratio of the vehicle.
ADSs might have a very limited vmax (even below 60 km/h)
But existing methodology covers all possible issues:
  WLTC Class 1 cycle covers low-speed vehicles.
  There are possibilities to downscale the applicable WLTC (see par. 8 of Annex B1).
  If the maximum speed is capped, this can be reduced (see par. 9 of Appendix B1).

## Slide 13: Issue 4: preparation for testing
X and Y vehicles will almost certainly have a manual driving capability up to 6 km/h.
Other vehicles equipped with an ADS will have manual controls for human drivers.
“ADS testing mode” should include manual driving for vehicle testing preparations, support, etc.
Manual mode of ADS vehicles may be used to prepare for the:
  Type 1 test and all dyno-related tests: drive the vehicle onto the dynamometer
  Type 4 test: drive the vehicle from the dyno to the SHED

## Slide 14: Issue 5: operating mode
Both the ADS and the powertrain might have different operating modes
  Powertrain: testing in predominant mode, additional driver selectable modes: well covered in the regulation
    Driver has the ability to change between modes: eco, normal, sport, comfort, 4WD, charge depleting (pure electric for PHEV), charge sustaining etc.
  In the case of an ADS, the ADS user may select different driving modes. This may affect:
    The powertrain operation mode: the ADS changes the powertrain mode after ADS user input.
    The “ADS driving style”: the ADS might use higher/lower acceleration/deceleration demands after ADS user input.

## Slide 15
User selectable modes (responding to driver/user input)
Non-user selectable modes (responding to specific conditions)
Eco
Sport
Comfort
4WD
Zero emission
Charge battery
Fulfils criteria for predominant mode?
Test only predominant mode
Test in best- and worst-case mode
yes
no
Driving at high altitude?
High altitude mode (change engine map)
Entering geofence area?
Critical OBD warning signal?
Heavy vehicle load?
Slippery weather conditions?
Empty battery?
Zero emission mode
Limp home mode
Heavy load mode (change engine map)
Low acc.&4WD mode (change engine map)
Change from EV to ICE mode

## Slide 16: Issue 5: operating mode conclusions
What are the conclusions on ADS mode selection?
Only modes which are (a) selected by the user and (b) affecting FC or emissions are user-selectable modes (see definition of UNR 154)
Every change of mode that is triggered by the ADS in response to a different vehicle or driving condition is NOT a user-selectable mode
Every change of mode that is triggered by the driver or directly by the ADS user is a user-selectable mode (e.g. the user is requested if the trip needs to be fast, normal or relaxing)
For user-selectable modes it needs to be established if one of the modes fulfils the criteria of being the predominant mode
If there is a predominant mode, the vehicle is tested in that mode. Else, the test is done for the worst-case and best-case mode, and the results are averaged

## Slide 17: Example solutions
Textual proposals for different issues

## Slide 18: Example solution: Scope
Scope: include definition of new vehicle categories and ADS through R.E.3.
Footnote 1, amend to read:
"1 As defined in the Consolidated Resolution on the Construction of Vehicles (R.E.3), document ECE/TRANS/WP.29/78/Rev.3, para. 28 –
www.unece.org/trans/main/wp29/wp29wgs/wp29gen/wp29resolutions.htmlhttps://unece.org/transport/vehicle-regulations/wp29/resolutions"

## Slide 19: Example solutions: Definitions
Definitions: include ADS at an equal level of responsibilities as the driver.
Paragraph 2.35., amend to read:
"2.35. "Malfunction indicator" (MI) means an indicator which is part of the alert system and which clearly informs the driver of the vehicle or the ADS (as applicable), in the event of a malfunction.
Whilst and ADS feature is active, the malfunction information is sent as a signal to the ADS;"

## Slide 20: Example solution: Requirements (warning signals 1)
Warning signals: send signal to ADS according to the existing requirements for the driver (tell-tales, MI, failure warning)
Example draft text inspired by R79 working document:
The requirements of this section related to warning signals to the driver do not apply whilst an ADS feature is active. The following requirement shall apply instead:
Whilst an ADS feature is active, warning signals (e.g. failure status) shall be transmitted to the ADS according to the provisions specified for the tell-tales. The means by which it is ensured that existing detected faults are transmitted to the ADS before an ADS feature becomes active (e.g. previously detected faults which remain present) shall be documented by the manufacturer.

## Slide 21: Example solution: Requirements (warning signals 2)
Warning signals: clarify driver warning, driver inducement, etc. Equal level of warning signals should be supplied for the ADS than to the driver (only where applicable, e.g. no need for audible signals for ADS)
Example draft text inspired by R13 working document:
In the case of vehicles equipped with an ADS, whenever this annex mentions “driver” (e.g. driver inducement, driver warning, etc.), it shall be understood as an ADS feature being active. Whenever needed, special provisions regarding vehicles of categories X and Y or vehicles equipped with an ADS are detailed in the corresponding paragraphs.

## Slide 22: Example solution: Requirements (warning signals 3)
Warning signals: send warning signals to ADS according to the principles used for the driver.
Annex 11, paragraph 4.1., amend to read:
"4.1. The vehicle shall include a driver warning system using visual alarms that informs the driver or sends a signal to the ADS, when a low reagent level, incorrect reagent quality, too low a rate of reagent consumption, or a malfunction, has been detected that may be due to tampering and that will lead to operation of the driver inducement system if not rectified in a timely manner. The warning system shall also be active when the driver inducement system described in paragraph 5. has been activated."

## Slide 23: Example solution: Tests
Tests:
  Interpret existing test methods for X and Y categories or in case of ADS.
  Allow execution of tests in manual mode in case of “dual mode” vehicles, if performance in ADS mode would be the same.
  Example text inspired by R13 working document:
Annex 11 , paragraph 1., amend to read:
1. Introduction
This annex sets out the requirements to ensure the correct operation of NOx control measures. It includes requirements for vehicles that rely on the use of a reagent in order to reduce emissions.
For vehicles of categories X and Y, all requirements of this annex shall be fulfilled and all respective demonstrations and tests shall be conducted. If necessary, dedicated methods may be used to conduct the demonstrations and tests. These may include assigning way points to define the test route, selection of different modes or any other method subject to agreement between the vehicle manufacturer and the Type Approval Authority.
For vehicles equipped with an ADS, other than those of categories X and Y, the demonstrations and tests shall be performed at least in the manual driving mode. Tests do not have to be performed in ADS mode providing the manufacturer can demonstrate to the technical service that the same performance can be achieved whilst an ADS feature is active. However, testing to verify this shall be performed at the request of the Type Approval Authority.

## Slide 24: Testing ADS according to R154
Proposed approach to handle emission tests

## Slide 25: Proposed approach: Coastdown test (1)
ADS vehicle (cat. X and Y) should provide the possibility for coastdown testing
  Specific test mode provided for coast-down testing (e.g. “ADS coastdown mode”)
Vehicle is coasted down on a test track
  The test track needs to be part of the ODD of the “ADS coastdown mode”
Coastdown runs may be split at shorter tracks and need to be repeated depending on results
  Allow possibility to give instructions during coastdown runs
Prevent manipulation of coast-down test results
  The “ADS coastdown mode” needs to be checked and approved by the TAA to ensure the validity of the test results (preferably also verify on-board signals, e.g. current from the batteries)
There are two other road-load determination methods (torque-meter and windtunnel)
  preferably allow the “ADS coastdown mode” to facilitate these methods, and at least the method used at type-approval

## Slide 26: Proposed approach: Coastdown test (2)
Suggestions for including the ADS coastdown mode
Describe this in a dedicated paragraph applicable only to ADS vehicles of cat. X and Y
Prepare a functional requirement for an ADS coastdown mode (what does it need to do) rather than specifying this in technical details (how it should work).
A functional requirement makes it easier to specify that the task of the driver in the current paragraphs on road-load determination is replaced by the ADS.
ADS coastdown mode shall also be engaged for the chassis dyno setting procedure.

## Slide 27: Proposed approach: Type 1 test
ADS vehicle (cat. X and Y) should provide the possibility for Type 1 testing
  Specific test mode provided for Type 1 testing (“ADS testing mode”)
Vehicle can be fed with WLTC or any other driving cycle (enabling third-party testing)
  ADS needs to be able to receive the speed cycle
Prevent manipulation of Type-1 test results
The “ADS testing mode” needs to be checked and approved by the TAA to ensure the validity of the test results (avoid smoothing, possibly verify on-board signals)
Check with SAE what they are developing for this (see remark of industry in meeting April 2025)

## Slide 28: Proposed approach: Other tests in UN R154
Type 4 (evaporative emissions): stationary test, no need for driver or ADS
Type 5 test (durability testing): test on track or road
  This test shows similarity with RDE and coastdown testing, the testing functionality could be added to ADS coastdown mode or RDE.
OBD test: based on Type 1 testing, so this functionality could be added to the “ADS testing mode”

## Slide 29: Thank you
© European Union 2025
Unless otherwise noted the reuse of this presentation is authorised under the CC BY 4.0 license. For any use or reproduction of elements that are not owned by the EU, permission may need to be sought directly from the respective right holders.
Slide xx: element concerned, source: e.g. Fotolia.com; Slide xx: element concerned, source: e.g. iStock.com
Notes: Update/add/delete parts of the copy right notice where appropriate.
More information: https://myintracomm.ec.europa.eu/corp/intellectual-property/Documents/2019_Reuse-guidelines%28CC-BY%29.pdf

## Slide 30: Test requirements from draft ADS regulation, examples
8.3.2.3.3. The approval authority or its designated technical service shall verify that the manufacturer has not optimised the ADS for a set of known test cases.
8.3.3.3.2. Any track testing shall be conducted on a testing ground that is part of, or suitably represents, the ODD of the ADS and complies with the requirements under paragraph 7.2.2. of this Regulation.
8.3.3.3.2.1. The approval authority or its designated technical service may request to use the testing ground used by the manufacturer to carry out confirmatory track testing.
8.3.2.3.1.2. The approval authority or its designated technical service shall verify that the manufacturer has suitable processes in place to identify test routes that capture predictable aspects of the ODD (e.g., road types and geometries), elements found in the related nominal situations (e.g., other road users, signs, and signals), and typical dynamic conditions (e.g., high/low traffic densities). The test routes shall also enable verification of requirements for the safety of user interactions, including prior to, at the time of, and after entering and exiting the ODD of an ADS feature.