## Slide 1: Conclusions from TF-AVRS-27
Input from the experts of EC – JRC
GRPE TF AVRS #28

## Slide 2: Conclusion: responsibilities of driver or ADS
The ADS is understood as the “driver” of the vehicle: ADS and human driver at the same level of responsibility while carrying out the DDT.
Driver
ADS
Vehicle driven by a human
Vehicle driven by an ADS feature
The regulation should form an equal level of requirements, enable testing and evaluation of the vehicle, engine or system, whilst an ADS feature is active.

## Slide 3: Conclusion: low speed ADS
ADSs might have a very limited vmax (even below 60 km/h)
But existing methodology covers all possible issues:
  WLTC Class 1 cycle covers low-speed vehicles.
  There are possibilities to downscale the applicable WLTC (see par. 8 of Annex B1).
  If the maximum speed is capped, this can be reduced (see par. 9 of Appendix B1).

## Slide 4: Conlcusion: preparation for testing
X and Y vehicles will almost certainly have a manual driving capability up to 6 km/h.
Other vehicles equipped with an ADS will have manual controls for human drivers.
“ADS testing mode” should include manual driving for vehicle testing preparations, support, etc.
Manual mode of ADS vehicles may be used to prepare for the:
  Type 1 test and all dyno-related tests: drive the vehicle onto the dynamometer
  Type 4 test: drive the vehicle from the dyno to the SHED

## Slide 5: Conclusion: operating mode
Only deliberate human input is considered:
  Manual driving: Driver has the ability to change between modes: eco, normal, sport, comfort, 4WD, charge depleting (pure electric for PHEV), charge sustaining etc.
  Automated driving: the ADS user may select different driving modes. This may affect:
    The powertrain operation mode: the ADS changes the powertrain mode after ADS user input.
    The “ADS driving style”: the ADS might use higher/lower acceleration/deceleration demands after ADS user input.

## Slide 6: Conclusion: user-selectable modes
Driver
Driver- selectable modes
ADS-user
ADS
ADS-user selectable modes
User- selectable modes
interface
interface

## Slide 7
User selectable modes (responding to driver/user input)
Non-user selectable modes (responding to specific conditions)
Eco
Sport
Comfort
4WD
Zero emission
Charge battery
Fulfils criteria for predominant mode?
Test only predominant mode
Test in best- and worst-case mode
yes
no
Driving at high altitude?
High altitude mode (change engine map)
Entering geofence area?
Critical OBD warning signal?
Heavy vehicle load?
Slippery weather conditions?
Empty battery?
Zero emission mode
Limp home mode
Heavy load mode (change engine map)
Low acc.&4WD mode (change engine map)
Change from EV to ICE mode

## Slide 8: Conclusions: operating mode
What are the conclusions on ADS mode selection?
Only modes which are (a) selected by the user and (b) affecting FC or emissions are user-selectable modes (see definition of UNR 154)
Every change of mode that is triggered by the ADS in response to a different vehicle or driving condition is NOT a user-selectable mode
Every change of mode that is triggered by the driver or directly by the ADS user is a user-selectable mode (e.g. the user is requested if the trip needs to be fast, normal or relaxing)
For user-selectable modes it needs to be established if one of the modes fulfils the criteria of being the predominant mode
If there is a predominant mode, the vehicle is tested in that mode. Else, the test is done for the worst-case and best-case mode, and the results are averaged

## Slide 9: Conclusion: Scope
Scope: include definition of new vehicle categories and ADS through R.E.3.
Footnote 1, amend to read:
"1 As defined in the Consolidated Resolution on the Construction of Vehicles (R.E.3), document ECE/TRANS/WP.29/78/Rev.3, para. 28 –
www.unece.org/trans/main/wp29/wp29wgs/wp29gen/wp29resolutions.htmlhttps://unece.org/transport/vehicle-regulations/wp29/resolutions"

## Slide 10: Conclusion: Malfunction indicator
Definitions: include ADS at an equal level of responsibilities as the driver.
Paragraph 3.10.4., amend to read:
“3.10.4. "Malfunction indicatorion (MI)" means a visible or audible indicator that clearly informs the driver of the vehicle and/or sends a signal to the ADS in the event of a malfunction of any emission-related component connected to the OBD system, or the OBD system itself.

## Slide 11: Conclusion: Warning and inducement signals
Insert new paragraph, interpreting the existing provisions for an ADS, e.g. the following:
“1.3. In the context of this appendix, for vehicles other than categories X and Y, the driver shall be informed of reagent and inducement warnings.
For vehicles of categories X and Y, where it is stated in this appendix that the driver shall be informed of reagent and inducement warnings, this shall be understood as a signal that informs the ADS. For these vehicles the requirements related to providing visual warnings to a driver do not have to be fulfilled, but the ADS user shall be informed of inducement warnings.
For vehicles equipped with an ADS feature, but other than categories X and Y, the driver shall be informed of reagent and inducement warnings, while the ADS shall only be informed of reagent and inducement warnings when the ADS is active.

## Slide 12: Conclusion: road load family
ADS needs to be considered in the road load family
The existing interpolation method is able to handle ADS
An “ADS road load determination mode” should be defined to enable measurement of ADS vehicles.

## Slide 13: Conclusion: interpolation family
ADS needs to be considered in the interpolation family:
  It has a considerable electric power consumption during operation
  If we allow testing ADS equipped vehicles in manual mode, ADS power consumption needs to be compensated for.
An “emission test ADS” (e.g. “coastdown mode”, “Type 1 test mode”) may not use all ADS sensors, therefore consumption might be less than the “normal ADS”
Real-world power consumption of ADS needs to be ensured during testing

## Slide 14: Conclusion: road load determination and Type 1 tests
Suggestions for including the ADS road load and Type 1 test mode
Describe in a dedicated paragraph applicable only to ADS vehicles of cat. X and Y
Prepare a functional requirement for an ADS road load mode (what does it need to do) rather than specifying this in technical details (how it should work).
A functional requirement makes it easier to specify that the task of the driver in the current paragraphs on road-load determination is replaced by the ADS.
ADS road load mode shall also be engaged for the chassis dyno setting procedure.

## Slide 15: Thank you
© European Union 2025
Unless otherwise noted the reuse of this presentation is authorised under the CC BY 4.0 license. For any use or reproduction of elements that are not owned by the EU, permission may need to be sought directly from the respective right holders.
Slide xx: element concerned, source: e.g. Fotolia.com; Slide xx: element concerned, source: e.g. iStock.com
Notes: Update/add/delete parts of the copy right notice where appropriate.
More information: https://myintracomm.ec.europa.eu/corp/intellectual-property/Documents/2019_Reuse-guidelines%28CC-BY%29.pdf