## Slide 1
Task Force 3: Electrolyte leakage
Last update- 02/03/2016

## Slide 2
Test items | Purpose of the test | Issue
Vibration | -The user is supposed to continue to use the vehicle after the event. -In this case, stringent requirements should be applied | Leakage in liquid form Vapor from leakage Volatile gas
Thermal shock and cycling |  | 
External short circuit protection | -The proposed test procedure is to confirm the operation of protective function. -In this case, stringent requirements should be applied | 
Overcharge protection |  | 
Over-discharge protection |  | 
Over-temperature protection |  | 
Mechanical integrity | -Same as vehicle post-crash | 
Mechanical shock |  | 
REESS requirements for whole vehicle post-crash | -The user is supposed to stop using the vehicle until certain repair/maintenance is conducted once subject to the event, presuming the battery would not be re-used for any other purpose than vehicle propulsion. -In this case, the requirement relevant to the accident situation, in order to avoid additional risk to the occupants and the surrounding people, should be applied. | Leakage in liquid form Vapor from leakage
Electrolyte Leakage: Present requirement & Purpose
In-use
Post-crash
The fire test does not require leakage criteria and hence out of scope of this TF

## Slide 3
 | Issue | Aqueous Electrolytes | Non-Aqueous Electrolytes
1 | Leakage in liquid form | Irritant, Corrosive Large amounts, order of liters, expected | Flammable, Toxic, Corrosive Small amounts, order of millilitres, expected
2 | Vapor from leakage | No significant amount expected | Toxic / flammable gas
3 | Volatile gas (venting) | Expected in normal operation Flammable gas (e.g.H2) | Not expected in normal operation
4 | Leakage in liquid form | Irritant, Corrosive Large amounts, order of liters, expected | Flammable, Toxic, Corrosive Small amounts, order of millilitres, expected
5 | Vapor from leakage | No significant amount expected | Toxic / flammable gas
Potential Risk
In-use
Post-crash
Potential Risk
Potential risk from non-aqueous electrolytes are different from aqueous electrolytes

## Slide 4
Revised acceptance criteria
Test item | Leakage | Rupture | Fire | Explosion | Isolation Resistance | Retention | Venting
Vibration | √ | √ | √ | √ | √ | - | √
Thermal shock | √ | √ | √ | √ | √ | - | √
Fire resistance | - | - | - | √ | - | - | -
External short circuit | √ | √ | √ | √ | √ | - | √
Over discharge | √ | √ | √ | √ | √ | - | √
Over charge | √ | √ | √ | √ | √ | - | √
Over temperature | √ | √ | √ | √ | √ | - | √
REESS- Mechanical shock | √ | - | √ | √ | √ | - | -
REESS- Mechanical integrity | √ | - | √ | √ | √ | - | -
Vehicle – Post Crash | √ | - | √ | √ | √ | √ | -
The ‘flammability aspect’ and the ‘electric shock aspect’ of electrolyte is already covered in the GTR draft
Hence the objective of the task force is to look in to the chemical risk (corrosive & toxic nature of electrolytes)
In-use
Crash
Additional validation criteria for sealed REESS

## Slide 5
Status of open issues
Issue | Discussion Status | Text proposal | Rational + Regulation text
Definitions | Agreed | Available | Under discussion
Aqueous electrolyte | Agreed | Available | Under discussion
Non-aqueous electrolyte (corrosive nature) | Agreed | Available | Under discussion
Non-aqueous electrolyte (Toxic nature) | Agreed | Available | Under discussion
Post crash: Observation period | Under discussion | Available | Under discussion
Venting | Agreed | Available | Under discussion
The ‘draft text proposal’ with rational is available

## Slide 6
TF3 discussion summary
REESS Types
Aqueous electrolyte REESS
Non-aqueous electrolyte REESS
Open type
Sealed type
Venting :
(In-use)
-Venting expected
-H2 measurement
-Venting as a validation criteria
- 7% leakage criteria
-No leakage (ensure no contact with occupant or people surrounding)
-No leakage
Leakage:
(Vehicle -Post crash)
Leakage:
(Component level test)
Sealed type
3.38
5.1. X.2 ; Annex X
5.1. X.3; 5.3.2; 5.3.3; 5.3.5; 5.3.6; 5.3.7; 5.3.8
5.4.1.1.1
5.4.1.1.2
5.3.2; 5.3.3; 5.3.5; 5.3.6; 5.3.7; 5.3.8
3.41
3.42
3.39
3.40

## Slide 7
Next steps
Action items:
Finalize the draft text proposal (feed back by end of April)
Complete discussion on observation period (30 minutes -> 60 minutes)
Meetings:
No face to face meeting before the 11 EVS meeting